## Slide 1
Ignytion io
Ignytion IO · ignytion.io
10 MBIT ETHERNET PROTOCOL SERIES · OCTOBER 2026
IGNYTION IO · TECHNICAL LAB NOTE
10 Mbit Ethernet protocol:
From RTL to routed GDS
A beginner's walkthrough of a checked open-source reference build
Follow ethernet_core from its communication rules and Verilog source to a routed IHP SG13G2 layout. Worked calculations, measured digital traces and tool results are identified separately. This is an educational block, not a manufactured chip or a signoff-ready design.
STAGE | WHAT IT PRODUCED | RESULT
Simulation | Listed directed checks | PASS directed
Synthesis | 1042 mapped functional cells | PASS mapping
Routing | Routed DEF and extracted SPEF | PASS reference
Timing | TT and slow setup / hold | PASS reference
GDS | Decoded placement agreement | PASS export
Foundry DRC / LVS | No accepted result | UNPERFORMED
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Follow ethernet_core from its communication rules and Verilog source to a routed IHP SG13G2 layout. Worked calculations, measured digital traces and tool results are identified separately. This is an educational block, not a manufactured chip or a signoff-ready design.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 2
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
02 / 24
CONTENTS
What is in this document
Start with the wire-level rules, then follow the same circuit through the tools. Each section has
a specific evidence boundary.
R E A D I N G M A P
SECTION | PAGE
Start here | p. 03
Chip design in ten minutes | p. 04
A MAC is not a 10BASE-T PHY | p. 05
Preamble, padding and FCS | p. 06
A reflected eight-step transform | p. 07
Stream input, non-stallable receive output | p. 08
Two domains and phase-offset tests | p. 09
CRC success does not cover every fault | p. 10
Byte A5 becomes nibbles 5, A | p. 11
Lint: read code before running it | p. 12
Independent frame and CRC checks | p. 13
Synthesis: a description becomes gates | p. 14
Floorplan and placement | p. 15
Clock tree and routing | p. 16
Two measured reference corners | p. 17
Count the right objects | p. 18
DRC and LVS: what is still missing | p. 19
Everything at a glance | p. 20
Run it yourself in WSL | p. 21
Sources, ownership and remaining work | p. 22
Design and physical glossary | p. 23–24
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 3
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
03 / 24
SECTION 1 · START HERE
Start here
A protocol is an agreement about how connected devices exchange information: which wire
carries each bit, when to sample it, and how to recognise a complete transfer.
W H A T W E B U I L T A N D W H A T I T P R O V E S
A Verilog description represents circuits, not software instructions running one after another. Registers remember values; combinational logic calculates the next values. A clock advances the registered state. The next pages first explain this protocol at its wires, then connect those rules to the actual reference RTL.
The implemented unit is ethernet_core in hw/protocols/stretch/ethernet. It is a fixed reference block, not the Jane Street programmable combined emulator or a Tiny Tapeout submission top. No new competition architecture, instruction set, pin map or authority decision is implied by these documents.
No external PHY, MDIO, collision handling or network stack. Test clocks are phase-offset at the same nominal frequency; drift is untested. Later pages give the exact stimulus and the implementation evidence rather than using a broad protocol-compliant label. A successful mapped netlist, routed DEF and decoded GDS establish concrete implementation/export results, not readiness to manufacture.
The reading path starts with chip-design vocabulary, then develops the protocol, calculations, local interface and failure cases. Separate sections explain lint, simulation, synthesis, placement, routing, timing and GDS. The last two pages define design and physical terms. No prior ASIC-flow experience is assumed.
E V I D E N C E V O C A B U L A R Y
Label | Meaning in this document
Worked example | Explicit assumptions; independently calculated
Measured trace | Positive digital regression VCD, where present
Directed PASS | Listed assertions and negative controls
Routed / decoded GDS | Physical export and structural agreement
Signoff | Not performed or claimed
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
A Verilog description represents circuits, not software instructions running one after another. Registers remember values; combinational logic calculates the next values. A clock advances the registered state. The next pages first explain this protocol at its wires, then connect those rules to the actual reference RTL.
The implemented unit is ethernet_core in hw/protocols/stretch/ethernet. It is a fixed reference block, not the Jane Street programmable combined emulator or a Tiny Tapeout submission top. No new competition architecture, instruction set, pin map or authority decision is implied by these documents.
No external PHY, MDIO, collision handling or network stack. Test clocks are phase-offset at the same nominal frequency; drift is untested. Later pages give the exact stimulus and the implementation evidence rather than using a broad protocol-compliant label. A successful mapped netlist, routed DEF and decoded GDS establish concrete implementation/export results, not readiness to manufacture.
The reading path starts with chip-design vocabulary, then develops the protocol, calculations, local interface and failure cases. Separate sections explain lint, simulation, synthesis, placement, routing, timing and GDS. The last two pages define design and physical terms. No prior ASIC-flow experience is assumed.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 4
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
04 / 24
SECTION 2 · CHIP DESIGN
Chip design in ten minutes
Each stage makes the same circuit more concrete. The folders below are the actual unit
layout, not a copied APB command list.
C H I P D E S I G N
RTL states what hardware should do. A simulator checks selected input sequences before any
silicon exists. Synthesis replaces that description with gates from a process library. Physical tools
choose positions and metal routes. Timing analysis checks the resulting delays; stream-out writes
the mask-layout geometry.
T H E P I P E L I N E , S T A G E B Y S T A G E
FOLDER | WHAT HAPPENS HERE
00_lint | Read code for risky patterns; retained warnings
01_rtl | Pinned source and the local wrapper
02_sim | Independent stimulus, comparisons and fatal controls
03_verification | Supplemental checks; not a universal UVM PASS
04_synthesis | Map functional logic to SG13G2 cells
05_dft | Manufacturing test work remains unperformed
06_floorplanning | Die outline, rows, power and pin locations
07_placement | Choose legal positions for mapped cells
09_place_and_route | Clock tree, routing and SPEF extraction
08_sta | Read post-route TT and slow timing reports
10_gds | Stream-out and independent placement decoder
11_physical_verification | Foundry DRC / LVS remain unperformed
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
RTL states what hardware should do. A simulator checks selected input sequences before any silicon exists. Synthesis replaces that description with gates from a process library. Physical tools choose positions and metal routes. Timing analysis checks the resulting delays; stream-out writes the mask-layout geometry.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 5
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
05 / 24
SECTION 3 · INTERFACE BOUNDARY
A MAC is not a 10BASE-T PHY
The block implements full-duplex digital MII frame processing.
I N T E R F A C E B O U N D A R Y
MII transfers four bits per clock. At 2.5 MHz the 400 ns clock period carries one nibble, giving 10 Mbit/s. Bytes cross the interface low nibble first, then high nibble. For byte A5 the visible nibbles are 5 followed by A. This ordering differs from simply reading a printed hexadecimal byte left to right.
A real link still needs an external analogue PHY, suitable magnetics and connector circuitry. Manchester line coding, link negotiation, MDIO management and half-duplex collision/retry are not supplied by this digital reference. Ethernet addressing and FCS processing do not automatically provide an IP, TCP or UDP stack.
The wrapper contains separate TX and RX clocks. TX data and handshake belong to mii_tx_clk;
received output belongs to mii_rx_clk. The consumer cannot assume that simultaneous-looking
frames share a safe common register domain.
M I I O W N E R S H I P
Signal group | Clock / owner
mii_txd, tx_en, tx_er | TX clock; MAC drives
mii_rxd, rx_dv, rx_er | RX clock; external PHY drives
tx_data / ready-valid | TX clock local producer
rx_data / valid / last / user | RX clock local consumer
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
MII transfers four bits per clock. At 2.5 MHz the 400 ns clock period carries one nibble, giving 10 Mbit/s. Bytes cross the interface low nibble first, then high nibble. For byte A5 the visible nibbles are 5 followed by A. This ordering differs from simply reading a printed hexadecimal byte left to right.
A real link still needs an external analogue PHY, suitable magnetics and connector circuitry. Manchester line coding, link negotiation, MDIO management and half-duplex collision/retry are not supplied by this digital reference. Ethernet addressing and FCS processing do not automatically provide an IP, TCP or UDP stack.
The wrapper contains separate TX and RX clocks. TX data and handshake belong to mii_tx_clk; received output belongs to mii_rx_clk. The consumer cannot assume that simultaneous-looking frames share a safe common register domain.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 6
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
06 / 24
SECTION 4 · FRAME FORMAT
Preamble, padding and FCS
The test checks frame structure separately from the local payload stream.
F R A M E F O R M A T
The transmitter emits the synchronising preamble and SFD before the supplied frame bytes. With padding enabled and a minimum 64-byte frame length including FCS, an input shorter than sixty frame bytes is extended before the four-byte FCS is appended. The local input bytes already contain whatever destination/source/type fields the application supplies.
A fourteen-byte input therefore needs forty-six padding bytes to reach sixty, then four FCS bytes.
A sixty-byte input needs no padding. A 256-byte input exceeds the minimum and retains its full
body. The regression checks those three sizes and independently evaluates their transmitted CRC
values.
At 10 Mbit/s, the minimum 64-byte frame itself takes 51.2 us. Including eight preamble/SFD bytes and a twelve-byte inter-frame gap gives 84 byte-times, or 67.2 us of wire scheduling. These are calculated line-rate bounds, not measured application throughput or a payload efficiency claim.
W O R K E D S I Z E B U D G E T
Input frame bytes | Padding | FCS | Result
14 | 46 | 4 | 64 bytes
60 | 0 | 4 | 64 bytes
256 | 0 | 4 | 260 bytes
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The transmitter emits the synchronising preamble and SFD before the supplied frame bytes. With padding enabled and a minimum 64-byte frame length including FCS, an input shorter than sixty frame bytes is extended before the four-byte FCS is appended. The local input bytes already contain whatever destination/source/type fields the application supplies.
A fourteen-byte input therefore needs forty-six padding bytes to reach sixty, then four FCS bytes. A sixty-byte input needs no padding. A 256-byte input exceeds the minimum and retains its full body. The regression checks those three sizes and independently evaluates their transmitted CRC values.
At 10 Mbit/s, the minimum 64-byte frame itself takes 51.2 us. Including eight preamble/SFD bytes and a twelve-byte inter-frame gap gives 84 byte-times, or 67.2 us of wire scheduling. These are calculated line-rate bounds, not measured application throughput or a payload efficiency claim.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 7
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
07 / 24
SECTION 5 · CRC CALCULATION
A reflected eight-step transform
The integrated replacement updates the exact state output consumed by these two MAC
engines.
C R C C A L C U L A T I O N
The byte update first XORs the eight data bits into the low end of the 32-bit state. Each of eight steps shifts right and conditionally XORs EDB88320 if the departing low bit is one. For the usual Ethernet convention the initial state is FFFFFFFF and the final result is complemented. ASCII 123456789 then gives CRC32 CBF43926.
The earlier generic LFSR elaboration was expensive. The replacement narrows the implementation
to this consumed byte/state contract. Its state_out is compared against the preserved upstream
LFSR; its unused data_out is tied to zero. It is therefore not a drop-in generic LFSR replacement for
other consumers.
This mapping is a linear transformation of forty input bits: thirty-two state bits and eight data bits.
Zero plus all forty one-hot basis vectors establish agreement for a truly linear implementation; 256
deterministic mixed vectors add a useful diagnostic cross-check. Fixed nonzero CRC initialisation
and final complement occur around, not inside, that linear transform.
S O U R C E / C O M M A N D S
assign stage[0]=state_in^{24'b0,data_in}; genvar b; generate for(b=0;b<8;b=b+1)begin: crc_bit assign stage[b+1]=(stage[b]>>1)^(stage[b][0]?32'hedb88320:32'b0); end endgenerate assign state_out=stage[8];
01_rtl/ethernet_crc32.v:18; exact contiguous source excerpt
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The byte update first XORs the eight data bits into the low end of the 32-bit state. Each of eight steps shifts right and conditionally XORs EDB88320 if the departing low bit is one. For the usual Ethernet convention the initial state is FFFFFFFF and the final result is complemented. ASCII 123456789 then gives CRC32 CBF43926.
The earlier generic LFSR elaboration was expensive. The replacement narrows the implementation to this consumed byte/state contract. Its state_out is compared against the preserved upstream LFSR; its unused data_out is tied to zero. It is therefore not a drop-in generic LFSR replacement for other consumers.
This mapping is a linear transformation of forty input bits: thirty-two state bits and eight data bits. Zero plus all forty one-hot basis vectors establish agreement for a truly linear implementation; 256 deterministic mixed vectors add a useful diagnostic cross-check. Fixed nonzero CRC initialisation and final complement occur around, not inside, that linear transform.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 8
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
08 / 24
SECTION 6 · RTL INTERFACE
Stream input, non-stallable receive output
The same-looking byte ports have different buffering obligations.
R T L I N T E R F A C E
On TX, the producer supplies data, valid, last and user and respects ready. These signals belong to the transmit clock. The wrapper fixes MII mode, padding enabled, minimum frame length 64 and a twelve-byte gap. Error-underflow remains available, but a passing normal-frame test is not an underflow regression.
On RX, data, valid, last and user belong to the receive clock. There is no rx_ready input, so downstream must accept each valid output or provide a suitable buffer in the same domain. Crossing to a system clock requires an explicit CDC design such as a correctly sized asynchronous FIFO, not a casual combinational connection.
Reset is synchronous active high in both domains. The integration layer must arrange safe assertion and release relative to each clock. The reference constraints apply reset budgets to both clock definitions; those constraints do not by themselves establish system reset reliability. The current SDC defines both MII clocks without set_clock_groups -asynchronous. It therefore retains a synchronous clock relationship in STA rather than modelling arbitrary external PHY phase and frequency. The common reset input has delays in both domains, but safe asynchronous reset delivery/release is not proved by those budgets.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
On TX, the producer supplies data, valid, last and user and respects ready. These signals belong to the transmit clock. The wrapper fixes MII mode, padding enabled, minimum frame length 64 and a twelve-byte gap. Error-underflow remains available, but a passing normal-frame test is not an underflow regression.
On RX, data, valid, last and user belong to the receive clock. There is no rx_ready input, so downstream must accept each valid output or provide a suitable buffer in the same domain. Crossing to a system clock requires an explicit CDC design such as a correctly sized asynchronous FIFO, not a casual combinational connection.
Reset is synchronous active high in both domains. The integration layer must arrange safe assertion and release relative to each clock. The reference constraints apply reset budgets to both clock definitions; those constraints do not by themselves establish system reset reliability. The current SDC defines both MII clocks without set_clock_groups -asynchronous. It therefore retains a synchronous clock relationship in STA rather than modelling arbitrary external PHY phase and frequency. The common reset input has delays in both domains, but safe asynchronous reset delivery/release is not proved by those budgets.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 9
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
09 / 24
SECTION 7 · CONTROL SEQUENCE
Two domains and phase-offset tests
Independent receive stimuli avoid a self-confirming TX-to-RX loop.
C O N T R O L S E Q U E N C E
The bench runs TX with a 400 ns period and RX with the same nominal 400 ns period after an
initial 73 ns offset. Their phases differ; their frequencies do not drift. This establishes separate
stimulus scheduling and exercises the distinct MAC domains, but it is not a frequency-offset or
asynchronous-FIFO stress test.
The receive source creates its own frames and CRC values rather than wiring transmitted nibbles back to the DUT. Valid sixty- and 256-byte receive frames are checked. A corrupt-FCS frame must raise the expected receive error. The transmitter independently checks fourteen-, sixty- and 256-byte input frames, padding and FCS.
The control path must keep last aligned with the final supplied frame byte. The FCS and pad extension are generated by the MAC. End-of-frame on MII and end-of-input on the local stream therefore occur at different times.
D O M A I N - S P E C I F I C T R A N S A C T I O N S
Path | Independent directed cases
TX | 14, 60 and 256 input frame bytes
RX | 60 and 256 valid frame bytes
RX fault | Corrupt FCS
Clock relation | 400 ns each; 73 ns phase offset
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The bench runs TX with a 400 ns period and RX with the same nominal 400 ns period after an initial 73 ns offset. Their phases differ; their frequencies do not drift. This establishes separate stimulus scheduling and exercises the distinct MAC domains, but it is not a frequency-offset or asynchronous-FIFO stress test.
The receive source creates its own frames and CRC values rather than wiring transmitted nibbles back to the DUT. Valid sixty- and 256-byte receive frames are checked. A corrupt-FCS frame must raise the expected receive error. The transmitter independently checks fourteen-, sixty- and 256-byte input frames, padding and FCS.
The control path must keep last aligned with the final supplied frame byte. The FCS and pad extension are generated by the MAC. End-of-frame on MII and end-of-input on the local stream therefore occur at different times.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 10
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
10 / 24
SECTION 8 · FAILURE ANALYSIS
CRC success does not cover every fault
The untested conditions define the next regression work.
F A I L U R E A N A L Y S I S
A corrupted receive FCS is covered, but RXER, runt/oversize acceptance, transmit underflow and clock drift are not established. Half-duplex collisions cannot be claimed because this reference is full duplex and does not implement collision/retry logic. Physical link negotiation and board operation likewise belong to the external PHY integration.
A consumer that cannot drain non-stallable RX output may lose data even when the incoming FCS
is valid. A production integration needs a buffer-capacity budget based on maximum burst size
and consumer latency. Declaring two clocks in STA is not a substitute for proving the
cross-domain queue contract.
The fixed CRC replacement has a deliberately limited compatibility promise. Preserving its unused
data_out zero tie is acceptable for the checked consumers, but reusing the module under a
different generic-LFSR interface would change the contract and require a new review.
N E X T R E G R E S S I O N O B L I G A T I O N S
Area | Unclosed condition
Receive faults | RXER, runt / oversize
Transmit flow | Underflow and error injection
Clock crossing | Frequency drift and buffer stress
PHY / board | MDIO, negotiation, actual link
Half duplex | Not implemented
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
A corrupted receive FCS is covered, but RXER, runt/oversize acceptance, transmit underflow and clock drift are not established. Half-duplex collisions cannot be claimed because this reference is full duplex and does not implement collision/retry logic. Physical link negotiation and board operation likewise belong to the external PHY integration.
A consumer that cannot drain non-stallable RX output may lose data even when the incoming FCS is valid. A production integration needs a buffer-capacity budget based on maximum burst size and consumer latency. Declaring two clocks in STA is not a substitute for proving the cross-domain queue contract.
The fixed CRC replacement has a deliberately limited compatibility promise. Preserving its unused data_out zero tie is acceptable for the checked consumers, but reusing the module under a different generic-LFSR interface would change the contract and require a new review.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 11
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
11 / 24
SECTION 9 · WORKED EXAMPLE
Byte A5 becomes nibbles 5, A
This is a labelled ideal MII sequence, not an exported waveform measurement.
W O R K E D E X A M P L E
At a 2.5 MHz MII clock, each nibble occupies 400 ns and one byte occupies 800 ns. The byte A5 appears as data nibble 5 then nibble A while transmit-enable is asserted. A known preamble/SFD sequence is checked before the frame body so a correctly ordered payload is not accepted in an incorrectly framed transmission.
The normal-frame tests compute FCS independently from the supplied frame and any generated zero padding. The low-nibble-first MII ordering must also hold for the FCS bytes. A local byte comparison alone would miss that serialisation error, which is why the bench observes the nibble interface.
The current Ethernet bench retains decisive logs and source rather than a plotted positive VCD. The document therefore shows the explicit example as a table. A future board trace must identify PHY clock direction, enable timing and error lines before being described as a measured link result.
I D E A L T I M I N G F O R B Y T E A 5
MII cycle | Relative interval | Nibble
First | 0..400 ns | 5
Second | 400..800 ns | A
Recovered byte | After two cycles | A5
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
At a 2.5 MHz MII clock, each nibble occupies 400 ns and one byte occupies 800 ns. The byte A5 appears as data nibble 5 then nibble A while transmit-enable is asserted. A known preamble/SFD sequence is checked before the frame body so a correctly ordered payload is not accepted in an incorrectly framed transmission.
The normal-frame tests compute FCS independently from the supplied frame and any generated zero padding. The low-nibble-first MII ordering must also hold for the FCS bytes. A local byte comparison alone would miss that serialisation error, which is why the bench observes the nibble interface.
The current Ethernet bench retains decisive logs and source rather than a plotted positive VCD. The document therefore shows the explicit example as a table. A future board trace must identify PHY clock direction, enable timing and error lines before being described as a measured link result.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 12
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
12 / 24
SECTION 10 · LINT
Lint: read code before running it
Verilator checks legal but suspicious code patterns without exercising transactions. A warning
count is a review starting point, not proof of correctness.
L I N T
The retained report contains 72 warning messages and 0 error messages. Categories present:
CASEINCOMPLETE, PINCONNECTEMPTY, PINMISSING, PROCASSINIT, SELRANGE, UNUSEDPARAM,
UNUSEDSIGNAL, WIDTHEXPAND, WIDTHTRUNC. These figures count report message headers;
repeated warnings are not necessarily independent defects. The report is hashed in this document
evidence manifest.
The invocation deliberately uses -Wno-fatal so warnings remain visible while lint execution can complete. A successful command therefore does not mean every warning was resolved. Width changes, incomplete cases, reset use and unconnected ports need review against the wrapper contract and directed tests.
Lint cannot show that a receive byte is correct, that a transaction finishes, or that an external
electrical interface is safe. Those questions require a checking testbench, implementation evidence
and separate board or signoff work.
R E T A I N E D W A R N I N G R E V I E W
MEASURE | VALUE
Warning message headers | 72
Error message headers | 0
Clean warning-free RTL? | Not claimed
Protocol behaviour proved by lint? | No
S O U R C E / C O M M A N D S
make lint # inspect, do not just count # 00_lint/lint_report.txt
00_lint/Makefile and run_flow.sh: retained Verilator report
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The retained report contains 72 warning messages and 0 error messages. Categories present: CASEINCOMPLETE, PINCONNECTEMPTY, PINMISSING, PROCASSINIT, SELRANGE, UNUSEDPARAM, UNUSEDSIGNAL, WIDTHEXPAND, WIDTHTRUNC. These figures count report message headers; repeated warnings are not necessarily independent defects. The report is hashed in this document evidence manifest.
The invocation deliberately uses -Wno-fatal so warnings remain visible while lint execution can complete. A successful command therefore does not mean every warning was resolved. Width changes, incomplete cases, reset use and unconnected ports need review against the wrapper contract and directed tests.
Lint cannot show that a receive byte is correct, that a transaction finishes, or that an external electrical interface is safe. Those questions require a checking testbench, implementation evidence and separate board or signoff work.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 13
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
13 / 24
SECTION 11 · SIMULATION AND VERIFICATION
Independent frame and CRC checks
A testbench is code that drives the circuit and judges its outputs. These directed checks use
independent expected data and deliberately failing controls.
S I M U L A T I O N A N D V E R I F I C A T I O N
Directed frame tests assert preamble, SFD, low-nibble-first ordering, padding, payload and independent CRC32 for TX sizes fourteen, sixty and 256. RX uses independently generated sixty- and 256-byte frames and a corrupt-FCS case. Reset quiescence is checked, and a deliberately wrong expected receive byte must fail.
The dedicated CRC regression compares the consumed state_out against the preserved upstream
LFSR over zero, forty one-hot and 256 mixed vectors, checks the standard arithmetic anchor and
rejects an injected mismatch. This addresses the local optimisation separately from frame-level
behaviour.
The result remains a full-duplex digital MAC reference. It is not a complete Ethernet device, a network stack, a frequency-drift regression or foundry signoff. Test coverage is documented per condition, so future work can add RXER and underflow without pretending the current normal-frame run already covers them.
A C C E P T E D P R O O F L A Y E R S
Layer | Evidence
Frame behaviour | Independent TX / RX checks
CRC transform | 297 direct comparisons plus anchor
Checker sensitivity | Deliberate fatal mismatches
Not established | All faults, PHY operation, signoff
A checker must be able to fail
Completion alone is insufficient. Read the successful log and the expected fatal rejection together;
neither is a protocol-compliance certificate.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Directed frame tests assert preamble, SFD, low-nibble-first ordering, padding, payload and independent CRC32 for TX sizes fourteen, sixty and 256. RX uses independently generated sixty- and 256-byte frames and a corrupt-FCS case. Reset quiescence is checked, and a deliberately wrong expected receive byte must fail.
The dedicated CRC regression compares the consumed state_out against the preserved upstream LFSR over zero, forty one-hot and 256 mixed vectors, checks the standard arithmetic anchor and rejects an injected mismatch. This addresses the local optimisation separately from frame-level behaviour.
The result remains a full-duplex digital MAC reference. It is not a complete Ethernet device, a network stack, a frequency-drift regression or foundry signoff. Test coverage is documented per condition, so future work can add RXER and underflow without pretending the current normal-frame run already covers them.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 14
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
14 / 24
SECTION 12 · SYNTHESIS
Synthesis: a description becomes gates
A netlist is a list of logic cells and their connections. Yosys translates the RTL into cells from
the IHP SG13G2 library.
S Y N T H E S I S
A process design kit, or PDK, contains the process-specific files used by implementation tools. This reference uses IHP SG13G2, not the SKY130 library used by the golden APB primer. Standard cells are predesigned gates and storage elements with characterised timing and physical views.
The source is compiled and checked under the unit workspace before synthesis. Yosys maps the functional logic into the pinned IHP SG13G2 standard-cell library. The current netlist contains 1042 functional cells, excluding $scopeinfo metadata. The structural checker rejects remaining generic logic, latches or unresolved instances.
The mapped count excludes $scopeinfo metadata. It is not the count of every placed instance after clock buffers, repair cells and fillers are added. It also does not mean that the original protocol has been independently proven for all possible transactions.
M A P P I N G R E S U L T
MEASURE | CURRENT RESULT
Top module | ethernet_core
Mapped functional cells | 1042
Technology | IHP SG13G2
Unresolved generic logic / latches | Rejected by structural checker
S O U R C E / C O M M A N D S
make synth node verify_build.mjs synth
04_synthesis/synth.tcl; verify_build.mjs synthesis checks
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
A process design kit, or PDK, contains the process-specific files used by implementation tools. This reference uses IHP SG13G2, not the SKY130 library used by the golden APB primer. Standard cells are predesigned gates and storage elements with characterised timing and physical views.
The source is compiled and checked under the unit workspace before synthesis. Yosys maps the functional logic into the pinned IHP SG13G2 standard-cell library. The current netlist contains 1042 functional cells, excluding $scopeinfo metadata. The structural checker rejects remaining generic logic, latches or unresolved instances.
The mapped count excludes $scopeinfo metadata. It is not the count of every placed instance after clock buffers, repair cells and fillers are added. It also does not mean that the original protocol has been independently proven for all possible transactions.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 15
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
15 / 24
SECTION 13 · PHYSICAL IMPLEMENTATION
Floorplan and placement
The floorplan gives the circuit a physical outline. Placement chooses where its cells sit inside
that outline.
P H Y S I C A L I M P L E M E N T A T I O N
The die outline for this standalone block is 500 x 500 um. The floorplan establishes rows and reference power/pin geometry. The placer must fit cells legally without overlaps and with room for routing. This is a block-level educational layout, not a complete padframe or package design.
Mapped functional logic has 1042 cells. After physical additions and fillers, the routed DEF
contains 53,628 placed standard-cell instances. A filler occupies empty row sites; it is not another
functional logic gate. That distinction explains why the two counts differ so much.
Utilisation is the fraction of core area occupied by placed cell area. It is not simply functional-cell
count divided by die size, and it changes between stages. This note does not substitute APB
utilisation, row count or I/O count for unavailable protocol-specific measurements.
A C T U A L P H Y S I C A L R E F E R E N C E
MEASURE | VALUE
Die outline | 500 x 500 um
Mapped functional cells | 1042
Placed standard-cell instances | 53,628
Physical inputs | 06_floorplanning; 07_placement
Placement agreement | DEF compared with decoded GDS
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The die outline for this standalone block is 500 x 500 um. The floorplan establishes rows and reference power/pin geometry. The placer must fit cells legally without overlaps and with room for routing. This is a block-level educational layout, not a complete padframe or package design.
Mapped functional logic has 1042 cells. After physical additions and fillers, the routed DEF contains 53,628 placed standard-cell instances. A filler occupies empty row sites; it is not another functional logic gate. That distinction explains why the two counts differ so much.
Utilisation is the fraction of core area occupied by placed cell area. It is not simply functional-cell count divided by die size, and it changes between stages. This note does not substitute APB utilisation, row count or I/O count for unavailable protocol-specific measurements.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 16
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
16 / 24
SECTION 14 · CLOCK AND WIRES
Clock tree and routing
Clock-tree synthesis distributes clocks to registers. Routing draws the metal connections
between placed cells.
C L O C K A N D W I R E S
A register samples its input at a clock edge. Clock buffers distribute that edge across the block; the difference in arrival times is called skew. The reference is constrained at MII TX/RX: 2.5 MHz / 400 ns. TX and RX have separate MII clock definitions; their relationship is a reference assumption, not arbitrary external PHY CDC signoff.
OpenROAD completes the staged physical flow. The reference die is 500 x 500 um. DEF records routed design geometry and cell placement; SPEF captures extracted parasitics used by the timing analysis. The scripts retain stage-specific output so the result can be investigated instead of relying on a final banner.
Real interconnect has resistance and capacitance, called parasitics. Extraction writes these in SPEF for post-route timing. The retained router-rule DRC file is empty. That checks the router view of its work; it is not a full foundry-deck check of the exported polygons.
R E A D T H E P H Y S I C A L E V I D E N C E
ARTIFACT | QUESTION IT ANSWERS
09_place_and_route/route.def | Where are cells and routed connections?
09_place_and_route/route.spef | Which parasitics were extracted?
Router-rule DRC report | Any reported routing-rule violations?
08_sta/timing_report.txt | What does extracted reference timing report?
Two checks can both be called DRC
The empty router report is accepted routing evidence. Foundry DRC is a separate unperformed
obligation; one result cannot stand in for the other.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
A register samples its input at a clock edge. Clock buffers distribute that edge across the block; the difference in arrival times is called skew. The reference is constrained at MII TX/RX: 2.5 MHz / 400 ns. TX and RX have separate MII clock definitions; their relationship is a reference assumption, not arbitrary external PHY CDC signoff.
OpenROAD completes the staged physical flow. The reference die is 500 x 500 um. DEF records routed design geometry and cell placement; SPEF captures extracted parasitics used by the timing analysis. The scripts retain stage-specific output so the result can be investigated instead of relying on a final banner.
Real interconnect has resistance and capacitance, called parasitics. Extraction writes these in SPEF for post-route timing. The retained router-rule DRC file is empty. That checks the router view of its work; it is not a full foundry-deck check of the exported polygons.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 17
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
17 / 24
SECTION 15 · REFERENCE TIMING
Two measured reference corners
Static timing analysis adds cell and wire delays without simulating input patterns. Setup asks
whether data arrives early enough; hold asks whether it stays stable long enough.
R E F E R E N C E T I M I N G
The physical clock constraint is MII TX/RX: 2.5 MHz / 400 ns. Post-route timing uses the extracted design rather than an ideal pre-route wire estimate. The report at each corner must be inspected for worst setup and hold slack and for VIOLATED markers. The reported values are not a timing guarantee under unstated board, voltage or temperature conditions.
Current TT setup/hold slack is +396.77 / +0.18 ns. The slow-corner values are +395.00 / +0.27 ns.
Both reports contain no VIOLATED marker. These numbers are taken directly from the local report
files at document build time; the evidence manifest retains their hashes.
I/O delays are reference budgets, not a contract with an external target, transceiver or PHY. Bus synchronisation, reset recovery/removal, all additional corners and modes, signal integrity and board timing need their own analysis. Positive slack in these two reports is therefore called reference timing closure, not foundry or system signoff. For Ethernet specifically, the SDC does not declare the two MII domains asynchronous. The quoted slacks use that reference relationship and do not bound arbitrary inter-domain paths or reset behaviour for independent real PHY clocks. No asynchronous CDC or reset timing signoff is claimed.
L I V E E X T R A C T E D S L A C K , N S
Corner | Worst setup | Worst hold
TT | 396.77 | 0.18
Slow | 395.00 | 0.27
Status | PASS reference reports | No VIOLATED markers
Positive slack has a stated boundary
Slack is remaining timing margin. These values apply to the listed clocks, I/O budgets and two library
corners; they are not a board-timing or manufacturing signoff guarantee.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The physical clock constraint is MII TX/RX: 2.5 MHz / 400 ns. Post-route timing uses the extracted design rather than an ideal pre-route wire estimate. The report at each corner must be inspected for worst setup and hold slack and for VIOLATED markers. The reported values are not a timing guarantee under unstated board, voltage or temperature conditions.
Current TT setup/hold slack is +396.77 / +0.18 ns. The slow-corner values are +395.00 / +0.27 ns. Both reports contain no VIOLATED marker. These numbers are taken directly from the local report files at document build time; the evidence manifest retains their hashes.
I/O delays are reference budgets, not a contract with an external target, transceiver or PHY. Bus synchronisation, reset recovery/removal, all additional corners and modes, signal integrity and board timing need their own analysis. Positive slack in these two reports is therefore called reference timing closure, not foundry or system signoff. For Ethernet specifically, the SDC does not declare the two MII domains asynchronous. The quoted slacks use that reference relationship and do not bound arbitrary inter-domain paths or reset behaviour for independent real PHY clocks. No asynchronous CDC or reset timing signoff is claimed.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 18
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
18 / 24
SECTION 16 · GDS STREAM-OUT
Count the right objects
GDS stores layout polygons and hierarchical cell references. Stream-out combines routed
geometry with the real standard-cell layouts from the PDK.
G D S S T R E A M - O U T
The GDS file contains 3,219,696 bytes and 47 structures. The independent decoder finds 53,628 placed standard-cell instances including fillers. That placement count is intentionally much larger than the 1042 mapped functional cells: filler instances occupy unused placement sites and structures are unique hierarchy definitions.
The decoder compares exported cell identities, coordinates and orientations against the routed
DEF. A deliberately altered placement/export expectation fails, including under Python
optimisation, so acceptance is not implemented with removable assert-only checks. Raw file
SHA256 is a run-specific fingerprint because stream-out timestamps can change.
The OpenROAD router-rule DRC report is empty. It is not a foundry-deck DRC result. LVS, antenna,
scan/DFT, power integrity, padframe, tap/endcap strategy and manufacturing signoff remain
unperformed. No empty routing report is promoted into a DRC-clean tapeout claim.
L I V E E X P O R T M E A S U R E M E N T S
Quantity | Current value
Mapped functional cells | 1042
GDS bytes | 3,219,696
GDS structures | 47
Placed standard-cell instances | 53,628
Die | 500 x 500 um
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The GDS file contains 3,219,696 bytes and 47 structures. The independent decoder finds 53,628 placed standard-cell instances including fillers. That placement count is intentionally much larger than the 1042 mapped functional cells: filler instances occupy unused placement sites and structures are unique hierarchy definitions.
The decoder compares exported cell identities, coordinates and orientations against the routed DEF. A deliberately altered placement/export expectation fails, including under Python optimisation, so acceptance is not implemented with removable assert-only checks. Raw file SHA256 is a run-specific fingerprint because stream-out timestamps can change.
The OpenROAD router-rule DRC report is empty. It is not a foundry-deck DRC result. LVS, antenna, scan/DFT, power integrity, padframe, tap/endcap strategy and manufacturing signoff remain unperformed. No empty routing report is promoted into a DRC-clean tapeout claim.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 19
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
19 / 24
SECTION 17 · UNPERFORMED SIGNOFF
DRC and LVS: what is still missing
Design rule checking asks whether geometry follows the process rules. Layout versus
schematic asks whether the extracted layout circuit matches the intended netlist.
U N P E R F O R M E D S I G N O F F
Foundry DRC requires the applicable, qualified rule deck and an inspected report on the final polygons. Typical checks include minimum widths, spacing and enclosure. No foundry-deck DRC result has been accepted for this protocol reference. The router report is narrower evidence.
LVS requires extracting a circuit from the layout and comparing devices and connectivity with the intended circuit. A structural GDS decoder checking cell references, coordinates and orientations does not perform that extraction or connectivity comparison. No accepted LVS match is available.
Antenna, scan/DFT, power integrity, padframe, tap/endcap strategy and manufacturing release
remain unperformed. The golden APB primer reports its own separate checks; those results do not
transfer to SG13G2 or to this design.
S E P A R A T E A C C E P T E D E X P O R T F R O M M I S S I N G S I G N O F F
CHECK | THIS REFERENCE
Router-rule report | Empty; narrower routing evidence
Decoded GDS placement | PASS structural/export agreement
Foundry-deck DRC | UNPERFORMED
Extracted-layout LVS | UNPERFORMED
Manufacturing readiness | Not claimed
A GDS file is not tapeout approval
This package is suitable for studying and reproducing a block implementation. Do not hand it off as a
signoff-clean manufacturing design.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Foundry DRC requires the applicable, qualified rule deck and an inspected report on the final polygons. Typical checks include minimum widths, spacing and enclosure. No foundry-deck DRC result has been accepted for this protocol reference. The router report is narrower evidence.
LVS requires extracting a circuit from the layout and comparing devices and connectivity with the intended circuit. A structural GDS decoder checking cell references, coordinates and orientations does not perform that extraction or connectivity comparison. No accepted LVS match is available.
Antenna, scan/DFT, power integrity, padframe, tap/endcap strategy and manufacturing release remain unperformed. The golden APB primer reports its own separate checks; those results do not transfer to SG13G2 or to this design.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 20
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
20 / 24
SECTION 18 · RESULTS SUMMARY
Everything at a glance
Read each result together with the question it actually answers. The same PASS label never
implies every protocol or manufacturing obligation is closed.
R E S U L T S S U M M A R Y
The directed functional result and the physical export result are both useful, but they prove different things. The physical build uses the fixed wrapper configuration and reference constraints. Additional modes, external peripherals, arbitrary clock relationships and board operation require their own evidence.
Important protocol boundary: No external PHY, MDIO, collision handling or network stack. Test
clocks are phase-offset at the same nominal frequency; drift is untested.
F U L L R E F E R E N C E F L O W
STAGE | TOOL / EVIDENCE | STATUS
Lint | Verilator; 72 retained warnings | Review
Simulation | Independent directed expectations | PASS directed
Negative controls | Deliberate fatal mismatches | PASS rejection
Synthesis | Yosys; 1042 mapped cells | PASS mapping
Floorplan / placement | OpenROAD; 500 x 500 um | PASS reference
Routing / extraction | DEF and SPEF retained | PASS reference
Timing | TT and slow setup / hold | PASS reference
GDS | KLayout; 3,219,696 bytes | PASS export
Foundry DRC / LVS | No accepted report | UNPERFORMED
Full-chip / board | No accepted integration proof | UNPERFORMED
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The directed functional result and the physical export result are both useful, but they prove different things. The physical build uses the fixed wrapper configuration and reference constraints. Additional modes, external peripherals, arbitrary clock relationships and board operation require their own evidence.
Important protocol boundary: No external PHY, MDIO, collision handling or network stack. Test clocks are phase-offset at the same nominal frequency; drift is untested.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 21
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
21 / 24
SECTION 19 · RUN IT YOURSELF
Run it yourself in WSL
Use the pinned source, the unit tool lock and the external PDK revision together.
R U N I T Y O U R S E L F
The proven entry point is a WSL login Bash shell. igny init prepares the packaging runtime.
Unsetting CRUCIBLE_ENV after initialisation allows the unit crucible.toml workspace selection to
control tool resolution rather than an inherited environment override. This is the observed
workflow, not a change to Crucible internals.
Each unit has its existing environment and lock. The common tool set includes Icarus, Verilator,
Yosys, OpenROAD and klayout-stream. The separate PDK checkout is IHP SG13G2 revision
22f43352dd8219f9007eb659e422e0d5fe28c5fb. A tool lock does not pin that external PDK by
itself; IHP_PDK_ROOT must point to the matching installation.
The documented machine could not use the pip klayout package as the expected stream-out
executable; igny tool install klayout-stream supplies the proven converter. make lint sim checks
functional behaviour, make flow executes the staged implementation, and node verify_build.mjs
all inspects artifacts. Review normal and intentionally failing logs before accepting the result.
Re-running a simulation can replace its VCD and invalidate an earlier document trace hash. Retain
a document evidence manifest or regenerate the measured figures after the positive run. Do not
silently preserve an old chart while claiming it is the newly generated waveform.
S O U R C E / C O M M A N D S
igny init unset CRUCIBLE_ENV cd hw/protocols/stretch/ethernet igny workspace sync igny tool install klayout-stream make lint sim make flow node verify_build.mjs all
Run after entering the repository in WSL login Bash; PDK required.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The proven entry point is a WSL login Bash shell. igny init prepares the packaging runtime. Unsetting CRUCIBLE_ENV after initialisation allows the unit crucible.toml workspace selection to control tool resolution rather than an inherited environment override. This is the observed workflow, not a change to Crucible internals.
Each unit has its existing environment and lock. The common tool set includes Icarus, Verilator, Yosys, OpenROAD and klayout-stream. The separate PDK checkout is IHP SG13G2 revision 22f43352dd8219f9007eb659e422e0d5fe28c5fb. A tool lock does not pin that external PDK by itself; IHP_PDK_ROOT must point to the matching installation.
The documented machine could not use the pip klayout package as the expected stream-out executable; igny tool install klayout-stream supplies the proven converter. make lint sim checks functional behaviour, make flow executes the staged implementation, and node verify_build.mjs all inspects artifacts. Review normal and intentionally failing logs before accepting the result.
Re-running a simulation can replace its VCD and invalidate an earlier document trace hash. Retain a document evidence manifest or regenerate the measured figures after the positive run. Do not silently preserve an old chart while claiming it is the newly generated waveform.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 22
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
22 / 24
SECTION 20 · SOURCES AND REMAINING WORK
Sources, ownership and remaining work
The pinned revision identifies the baseline; local integration changes are described separately.
S O U R C E S A N D R E M A I N I N G W O R K
Upstream: https://github.com/alexforencich/verilog-ethernet Pinned commit: 77320a9471d19c7dd383914bc049e02d9f4f1ffb Licence: MIT, Alex Forencich; per-file notices retained. Original source notices remain in the RTL. The document is authored by Ignytion; this does not transfer ownership of upstream code or remove its licence obligations.
Local modifications, directed test stimulus and source boundaries are recorded in hw/protocols/stretch/ethernet/README.md and the repository append-only .context.md. The first three protocol lessons have separate editable 16:9 student decks; this A4 technical note is a reading and evidence document, not a replacement for their instructor notes.
Primary reading: The checked-in KSZ8081MLX PHY data sheet for MII, IEEE 802.3 as the canonical standard, and the pinned MAC RTL. Canonical standard catalogue: https://standards.ieee.org/standard/802_3-2022.html; local PHY snapshot: specs/Ethernet_Specification.pdf
Open work remains explicit: No external PHY, MDIO, collision handling or network stack. Test clocks are phase-offset at the same nominal frequency; drift is untested. Full-chip integration, manufacturing checks and board validation are not closed by the standalone reference flow. The reader can reproduce the listed evidence without assuming those larger obligations have already been completed.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Upstream: https://github.com/alexforencich/verilog-ethernet
Pinned commit: 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Licence: MIT, Alex Forencich; per-file notices retained. Original source notices remain in the RTL. The document is authored by Ignytion; this does not transfer ownership of upstream code or remove its licence obligations.
Local modifications, directed test stimulus and source boundaries are recorded in hw/protocols/stretch/ethernet/README.md and the repository append-only .context.md. The first three protocol lessons have separate editable 16:9 student decks; this A4 technical note is a reading and evidence document, not a replacement for their instructor notes.
Primary reading: The checked-in KSZ8081MLX PHY data sheet for MII, IEEE 802.3 as the canonical standard, and the pinned MAC RTL.
Canonical standard catalogue: https://standards.ieee.org/standard/802_3-2022.html; local PHY snapshot: specs/Ethernet_Specification.pdf
Open work remains explicit: No external PHY, MDIO, collision handling or network stack. Test clocks are phase-offset at the same nominal frequency; drift is untested. Full-chip integration, manufacturing checks and board validation are not closed by the standalone reference flow. The reader can reproduce the listed evidence without assuming those larger obligations have already been completed.
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 23
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
23 / 24
SECTION 21 · DESIGN VOCABULARY
Glossary: design and protocol
Definitions for reading the protocol rules and the checked RTL. Physical implementation
terms follow on the next page.
D E S I G N A N D V E R I F I C A T I O N
TERM | WHAT IT MEANS
Protocol | Rules for exchanging information between devices
RTL | Registers and the logic moving values between them
Verilog | A language used to describe hardware
FSM | A circuit progressing through defined states
Lint | Static source checks; no transaction execution
Testbench | Code that supplies inputs and checks outputs
Coverage | Which defined situations were exercised
Negative control | An intentionally wrong case the checker must reject
VCD | Digital signal-change trace from a simulation
Handshake | Signals agreeing when data is accepted
MAC / PHY | Digital frame engine / physical signalling transceiver
MII | Four-bit Media Independent Interface
FCS | Frame Check Sequence; transmitted CRC32
IFG | Inter-frame gap
Basis vector | One active input bit used to test a linear transform
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 24
Ignytion io
10 MBIT ETHERNET · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
24 / 24
SECTION 22 · PHYSICAL VOCABULARY
Glossary: implementation and signoff
These definitions help distinguish a successfully exported reference layout from a
manufacturing-ready design.
P H Y S I C A L I M P L E M E N T A T I O N
TERM | WHAT IT MEANS
Synthesis | Translate RTL into a technology-cell circuit
Netlist | Cells and the connections between them
Standard cell | Predesigned logic/storage cell in a process library
PDK | Process design kit: process-specific implementation files
SG13G2 | IHP process used by these reference builds
Floorplan | Die/core outline, rows, power and pin geometry
Placement | Choose legal positions for cells
Filler | Physical row-site cell, not functional logic
CTS / skew | Clock distribution / difference in arrival times
Routing / via | Metal connections / links between metal layers
Parasitics / SPEF | Wire resistance/capacitance / extracted data format
Corner | A characterised process, voltage and temperature case
STA / slack | Static timing analysis / remaining timing margin
DEF / GDS | Placement/routing exchange / polygon hierarchy
DRC | Check geometry against applicable process rules
LVS | Compare the extracted layout circuit with its netlist
Signoff | Accepted applicable release checks; unperformed here
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/Ethernet_10M_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Source area: hw/protocols/stretch/ethernet
https://github.com/alexforencich/verilog-ethernet
Pinned commit 77320a9471d19c7dd383914bc049e02d9f4f1ffb
Original upstream notice:
// ===============================================================================
// Ignytion IO - CRUCIBLE CORE
// Copyright (c) 2026 Ignytion IO. All rights reserved.
// Author : IGNYTION_TECH
// File : hw/protocols/stretch/ethernet/UPSTREAM_LICENSE.txt
// Created : 2026-10-03
// Description : 10 Mbit MII MAC reference integration; original notices preserved.
// ===============================================================================
Copyright (c) 2014-2018 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.