## Slide 1
Ignytion io
Ignytion IO · ignytion.io
I2C PROTOCOL SERIES · OCTOBER 2026
IGNYTION IO · TECHNICAL LAB NOTE
I2C protocol:
From RTL to routed GDS
A beginner's walkthrough of a checked open-source reference build
Follow i2c_core from its communication rules and Verilog source to a routed IHP SG13G2 layout. Worked calculations, measured digital traces and tool results are identified separately. This is an educational block, not a manufactured chip or a signoff-ready design.
STAGE | WHAT IT PRODUCED | RESULT
Simulation | Listed directed checks | PASS directed
Synthesis | 1007 mapped functional cells | PASS mapping
Routing | Routed DEF and extracted SPEF | PASS reference
Timing | TT and slow setup / hold | PASS reference
GDS | Decoded placement agreement | PASS export
Foundry DRC / LVS | No accepted result | UNPERFORMED
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Follow i2c_core from its communication rules and Verilog source to a routed IHP SG13G2 layout. Worked calculations, measured digital traces and tool results are identified separately. This is an educational block, not a manufactured chip or a signoff-ready design.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 2
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
02 / 24
CONTENTS
What is in this document
Start with the wire-level rules, then follow the same circuit through the tools. Each section has
a specific evidence boundary.
R E A D I N G M A P
SECTION | PAGE
Start here | p. 03
Chip design in ten minutes | p. 04
Drive low, or release | p. 05
Read a register, not just a byte | p. 06
Nominal rate versus wire rate | p. 07
Registers, command bits and pads | p. 08
Bit control has several phases | p. 09
A NACK is an observation | p. 10
An address and its acknowledgement | p. 11
Lint: read code before running it | p. 12
What the I2C regression establishes | p. 13
Synthesis: a description becomes gates | p. 14
Floorplan and placement | p. 15
Clock tree and routing | p. 16
Two measured reference corners | p. 17
Count the right objects | p. 18
DRC and LVS: what is still missing | p. 19
Everything at a glance | p. 20
Run it yourself in WSL | p. 21
Sources, ownership and remaining work | p. 22
Design and physical glossary | p. 23–24
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 3
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
03 / 24
SECTION 1 · START HERE
Start here
A protocol is an agreement about how connected devices exchange information: which wire
carries each bit, when to sample it, and how to recognise a complete transfer.
W H A T W E B U I L T A N D W H A T I T P R O V E S
A Verilog description represents circuits, not software instructions running one after another. Registers remember values; combinational logic calculates the next values. A clock advances the registered state. The next pages first explain this protocol at its wires, then connect those rules to the actual reference RTL.
The implemented unit is i2c_core in hw/protocols/i2c. It is a fixed reference block, not the Jane Street programmable combined emulator or a Tiny Tapeout submission top. No new competition architecture, instruction set, pin map or authority decision is implied by these documents.
Arbitration is not decisively tested. Stretching and repeated START have indirect data/completion coverage only. Later pages give the exact stimulus and the implementation evidence rather than using a broad protocol-compliant label. A successful mapped netlist, routed DEF and decoded GDS establish concrete implementation/export results, not readiness to manufacture.
The reading path starts with chip-design vocabulary, then develops the protocol, calculations, local interface and failure cases. Separate sections explain lint, simulation, synthesis, placement, routing, timing and GDS. The last two pages define design and physical terms. No prior ASIC-flow experience is assumed.
E V I D E N C E V O C A B U L A R Y
Label | Meaning in this document
Worked example | Explicit assumptions; independently calculated
Measured trace | Positive digital regression VCD, where present
Directed PASS | Listed assertions and negative controls
Routed / decoded GDS | Physical export and structural agreement
Signoff | Not performed or claimed
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
A Verilog description represents circuits, not software instructions running one after another. Registers remember values; combinational logic calculates the next values. A clock advances the registered state. The next pages first explain this protocol at its wires, then connect those rules to the actual reference RTL.
The implemented unit is i2c_core in hw/protocols/i2c. It is a fixed reference block, not the Jane Street programmable combined emulator or a Tiny Tapeout submission top. No new competition architecture, instruction set, pin map or authority decision is implied by these documents.
Arbitration is not decisively tested. Stretching and repeated START have indirect data/completion coverage only. Later pages give the exact stimulus and the implementation evidence rather than using a broad protocol-compliant label. A successful mapped netlist, routed DEF and decoded GDS establish concrete implementation/export results, not readiness to manufacture.
The reading path starts with chip-design vocabulary, then develops the protocol, calculations, local interface and failure cases. Separate sections explain lint, simulation, synthesis, placement, routing, timing and GDS. The last two pages define design and physical terms. No prior ASIC-flow experience is assumed.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 4
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
04 / 24
SECTION 2 · CHIP DESIGN
Chip design in ten minutes
Each stage makes the same circuit more concrete. The folders below are the actual unit
layout, not a copied APB command list.
C H I P D E S I G N
RTL states what hardware should do. A simulator checks selected input sequences before any
silicon exists. Synthesis replaces that description with gates from a process library. Physical tools
choose positions and metal routes. Timing analysis checks the resulting delays; stream-out writes
the mask-layout geometry.
T H E P I P E L I N E , S T A G E B Y S T A G E
FOLDER | WHAT HAPPENS HERE
00_lint | Read code for risky patterns; retained warnings
01_rtl | Pinned source and the local wrapper
02_sim | Independent stimulus, comparisons and fatal controls
03_verification | Supplemental checks; not a universal UVM PASS
04_synthesis | Map functional logic to SG13G2 cells
05_dft | Manufacturing test work remains unperformed
06_floorplanning | Die outline, rows, power and pin locations
07_placement | Choose legal positions for mapped cells
09_place_and_route | Clock tree, routing and SPEF extraction
08_sta | Read post-route TT and slow timing reports
10_gds | Stream-out and independent placement decoder
11_physical_verification | Foundry DRC / LVS remain unperformed
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
RTL states what hardware should do. A simulator checks selected input sequences before any silicon exists. Synthesis replaces that description with gates from a process library. Physical tools choose positions and metal routes. Timing analysis checks the resulting delays; stream-out writes the mask-layout geometry.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 5
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
05 / 24
SECTION 3 · ELECTRICAL RULES
Drive low, or release
Open-drain ownership is a wired-bus rule. The pad-level implementation remains outside this
digital reference.
E L E C T R I C A L R U L E S
When any open-drain participant pulls the shared wire low, the connected receivers observe a low. This supports shared ownership without opposing high and low drivers. Pull-up selection depends on rise time, bus capacitance and sink current. An RTL tri-state model is ideal digital behaviour and does not prove these analogue limits. The integration needs correct output-enable polarity.
These are stated classroom assumptions, not measured board values. The 0.8473 factor describes the 30-to-70 percent RC rise interval. A real design must use the device data sheet limits and include wiring, connector and pin capacitance. NXP UM10204 section 7.1 describes this method. This calculation does not prove electrical compliance of the reference RTL pads.
The pull-up can raise the line only when neither participant sinks current. A digital simulation does
not model pull-up resistance or pad sink current.
The pull-up bounds are Rmin = (VDD - VOL) / IOL and Rmax = tr / (0.8473 x Cbus). With the
stated values these give 2.9 / 0.003 = 967 ohm and 300 ns / (0.8473 x 100 pF) = 3.54 kohm.
Choosing 2.2 kohm predicts tr = 0.8473 x 2200 x 100 pF = 186 ns. Doubling the capacitance
doubles that prediction to 373 ns and exceeds the assumed 300 ns budget.
W O R K E D P U L L - U P B U D G E T
Assumption / result | Value
VDD, VOL, sink capability | 3.3 V, 0.4 V, 3 mA
Cbus, assumed rise-time limit | 100 pF, 300 ns
Rmin / Rmax | 967 ohm / 3.54 kohm
2.2 kohm rise time / current | 186 ns / 1.32 mA
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
When any open-drain participant pulls the shared wire low, the connected receivers observe a low. This supports shared ownership without opposing high and low drivers. Pull-up selection depends on rise time, bus capacitance and sink current. An RTL tri-state model is ideal digital behaviour and does not prove these analogue limits. The integration needs correct output-enable polarity.
These are stated classroom assumptions, not measured board values. The 0.8473 factor describes the 30-to-70 percent RC rise interval. A real design must use the device data sheet limits and include wiring, connector and pin capacitance. NXP UM10204 section 7.1 describes this method. This calculation does not prove electrical compliance of the reference RTL pads.
The pull-up can raise the line only when neither participant sinks current. A digital simulation does not model pull-up resistance or pad sink current.
The pull-up bounds are Rmin = (VDD - VOL) / IOL and Rmax = tr / (0.8473 x Cbus). With the stated values these give 2.9 / 0.003 = 967 ohm and 300 ns / (0.8473 x 100 pF) = 3.54 kohm. Choosing 2.2 kohm predicts tr = 0.8473 x 2200 x 100 pF = 186 ns. Doubling the capacitance doubles that prediction to 373 ns and exceeds the assumed 300 ns budget.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 6
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
06 / 24
SECTION 4 · TRANSACTION RULES
Read a register, not just a byte
A device address selects the target; the application register selects the value within it.
T R A N S A C T I O N R U L E S
The register index and auto-increment behaviour belong to the target’s application contract, not
to I2C itself. The local target model stores bytes for this exercise. A real device datasheet
determines whether this exact multi-byte sequence is valid.
The first acknowledged read requests more bytes. The controller should NACK the final byte before STOP to tell the target that the receive phase is over. The regression checks A5 and 5A. Later uninitialised locations print unknown values but are not asserted, so they cannot count as extra verified payload bytes.
Repeated START keeps the transaction active while changing direction. The target owns read data, and the controller owns the final response. Some devices use different register widths or pointer behaviour; this worked convention is not universal.
H Y P O T H E T I C A L T A R G E T 0 X 5 0 , R E G I S T E R 0 X 0 1
Phase | Byte / bus owner
Address write | A0 from controller; ACK from target
Register selection | 01 from controller; ACK from target
Repeated START, address read | A1 from controller; ACK from target
Final value | A5 from target; NACK from controller
Release bus | STOP from controller
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The register index and auto-increment behaviour belong to the target’s application contract, not to I2C itself. The local target model stores bytes for this exercise. A real device datasheet determines whether this exact multi-byte sequence is valid.
The first acknowledged read requests more bytes. The controller should NACK the final byte before STOP to tell the target that the receive phase is over. The regression checks A5 and 5A. Later uninitialised locations print unknown values but are not asserted, so they cannot count as extra verified payload bytes.
Repeated START keeps the transaction active while changing direction. The target owns read data, and the controller owns the final response. Some devices use different register widths or pointer behaviour; this worked convention is not universal.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 7
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
07 / 24
SECTION 5 · TIMING CALCULATION
Nominal rate versus wire rate
The simulation and physical clocks differ. Divider arithmetic alone does not describe the
measured bus period.
T I M I N G C A L C U L A T I O N
The five-phase divider gives nominal SCL = fwb / [5 x (PRER + 1)]. At 50 MHz, PRER 99 yields 100
kHz and PRER 24 yields 400 kHz before other delays. These are worked configurations, not
independently measured board rates. The regression instead runs at 100 MHz with PRER 0x00C8,
or 200: 1005 core clocks predict 10.05 us and 99.502 kHz.
The positive VCD contains steady address-clock intervals of 10.71 us, or 1071 core cycles and 93.371 kHz. The observed difference is 66 clocks per period, approximately 6.57 percent extra period. Input filtering and synchronisation are possible contributors; the exact state-by-state attribution has not been established. No causal claim is made from the rate difference alone.
Nine clocks are consumed by eight data bits plus ACK. The nominal maximum payload-bit fraction is therefore 8/9, before address, START, STOP and idle overhead. A hypothetical single-byte register read uses four nine-clock byte phases, giving 360 us at an ideal 100 kHz, excluding boundary gaps and stretching.
K E E P T H E T I M I N G C O N T E X T S S E P A R A T E
Context | Clock / result
Physical reference constraint | 50 MHz; 20 ns
Simulation source clock | 100 MHz; always #5
Nominal simulation divider | 10.05 us; 99.502 kHz
Measured steady SCL | 10.71 us; 93.371 kHz
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The five-phase divider gives nominal SCL = fwb / [5 x (PRER + 1)]. At 50 MHz, PRER 99 yields 100 kHz and PRER 24 yields 400 kHz before other delays. These are worked configurations, not independently measured board rates. The regression instead runs at 100 MHz with PRER 0x00C8, or 200: 1005 core clocks predict 10.05 us and 99.502 kHz.
The positive VCD contains steady address-clock intervals of 10.71 us, or 1071 core cycles and 93.371 kHz. The observed difference is 66 clocks per period, approximately 6.57 percent extra period. Input filtering and synchronisation are possible contributors; the exact state-by-state attribution has not been established. No causal claim is made from the rate difference alone.
Nine clocks are consumed by eight data bits plus ACK. The nominal maximum payload-bit fraction is therefore 8/9, before address, START, STOP and idle overhead. A hypothetical single-byte register read uses four nine-clock byte phases, giving 360 us at an ideal 100 kHz, excluding boundary gaps and stretching.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 8
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
08 / 24
SECTION 6 · RTL INTERFACE
Registers, command bits and pads
The local parallel interface drives a protocol engine; it is not itself the I2C wire protocol.
R T L I N T E R F A C E
i2c_core wraps i2c_master_top, followed by the byte and bit controllers. The wrapper adds synchronised reset release and preserves the existing port contract.
Each command field has a separate bit assignment. Bit seven is START, bit six STOP, bit five READ, bit four WRITE, and bit three the response selection. The current bench uses these constants; verify status TIP clears before issuing the next command. A polling loop also needs a system timeout, which is separate from the bare peripheral logic.
ARST_LVL is an elaboration parameter. The default is zero, so low arst_i asserts reset. The wrapper converts polarity and passes active-low reset to the upstream controller. A two-flop release improves clock-domain reset handling but is not a metastability or reset-domain signoff report. There is also a synchronous Wishbone reset input. Pad integration still needs an actual I/O cell and electrical design.
S O U R C E / C O M M A N D S
wire sta = cr[7]; wire sto = cr[6]; wire rd = cr[5]; wire wr = cr[4]; wire ack = cr[3]; wire sl_cont = cr[1]; wire iack = cr[0];
hw/protocols/i2c/01_rtl/i2c_master_top.v:237
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
i2c_core wraps i2c_master_top, followed by the byte and bit controllers. The wrapper adds synchronised reset release and preserves the existing port contract.
Each command field has a separate bit assignment. Bit seven is START, bit six STOP, bit five READ, bit four WRITE, and bit three the response selection. The current bench uses these constants; verify status TIP clears before issuing the next command. A polling loop also needs a system timeout, which is separate from the bare peripheral logic.
ARST_LVL is an elaboration parameter. The default is zero, so low arst_i asserts reset. The wrapper converts polarity and passes active-low reset to the upstream controller. A two-flop release improves clock-domain reset handling but is not a metastability or reset-domain signoff report. There is also a synchronous Wishbone reset input. Pad integration still needs an actual I/O cell and electrical design.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 9
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
09 / 24
SECTION 7 · CONTROL SEQUENCE
Bit control has several phases
The source FSM and the bit divider explain when SDA may change and when the bus is
sampled.
C O N T R O L S E Q U E N C E
The table summarises the actual named states and output-enable assignments, not a newly invented controller. An enable of one releases the open-drain line; it does not force a high voltage. In wr_c the implementation checks SDA for arbitration. Command acknowledgement marks completion of the bit operation, which is separate from target acknowledgement on the ninth bus pulse.
The Wishbone read returns the receive register at address three; writing there queues outgoing
data. This shared address is not an error. The bus acknowledgement means the register operation
completed, not that a remote I2C target acknowledged.
The XOR converts the selected external assertion level into an internal active-low reset. While asserted, both release flops clear. Once the external reset becomes inactive, ones shift through on consecutive clock edges. The controller receives the second stage. This reduces release hazards inside this clock domain; it does not provide board-level reset sequencing for every pad or external target.
S O U R C E - D E R I V E D W R I T E - B I T S E Q U E N C E
State | SCL action | SDA action
wr_a | Pull low | Set current data bit
wr_b | Release | Keep data, allow settling
wr_c | Remain released | Keep data, enable bus check
wr_d | Pull low | Keep data, acknowledge bit command
idle | Await next command | Hold current drive policy
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The table summarises the actual named states and output-enable assignments, not a newly invented controller. An enable of one releases the open-drain line; it does not force a high voltage. In wr_c the implementation checks SDA for arbitration. Command acknowledgement marks completion of the bit operation, which is separate from target acknowledgement on the ninth bus pulse.
The Wishbone read returns the receive register at address three; writing there queues outgoing data. This shared address is not an error. The bus acknowledgement means the register operation completed, not that a remote I2C target acknowledged.
The XOR converts the selected external assertion level into an internal active-low reset. While asserted, both release flops clear. Once the external reset becomes inactive, ones shift through on consecutive clock edges. The controller receives the second stage. This reduces release hazards inside this clock domain; it does not provide board-level reset sequencing for every pad or external target.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 10
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
10 / 24
SECTION 8 · FAILURE ANALYSIS
A NACK is an observation
An unsuccessful transaction must be diagnosed at the address, ownership and timing levels.
F A I L U R E A N A L Y S I S
The bench probes an invalid address and asserts the NACK result. That test is useful because a
controller can generate perfectly shaped clocks while communicating with no device. The
simulation watchdog is a test safety mechanism, not proof of a hardware bus-recovery
implementation.
The actual bus can remain low because another participant holds it. The RTL samples the pad
input. The inherited bench includes a stretching target, but its completion assertion does not
certify arbitrary stretch durations or stuck-low recovery. This limitation belongs in an test report.
The selected OpenCores design contains arbitration logic. Presence of that logic is different from
test coverage. The second controller in this regression remains idle, so arbitration under
contention is not validated.
C O V E R A G E B O U N D A R Y
Mechanism | Evidence strength
A5 / 5A reads and invalid-address NACK | Directed decisive checks
Repeated START and clock stretching | Indirect completion / data checks
Two-controller arbitration | Not tested
Later uninitialised model bytes | Not data-verified
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The bench probes an invalid address and asserts the NACK result. That test is useful because a controller can generate perfectly shaped clocks while communicating with no device. The simulation watchdog is a test safety mechanism, not proof of a hardware bus-recovery implementation.
The actual bus can remain low because another participant holds it. The RTL samples the pad input. The inherited bench includes a stretching target, but its completion assertion does not certify arbitrary stretch durations or stuck-low recovery. This limitation belongs in an test report.
The selected OpenCores design contains arbitration logic. Presence of that logic is different from test coverage. The second controller in this regression remains idle, so arbitration under contention is not validated.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 11
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
11 / 24
SECTION 9 · MEASURED TRACE
An address and its acknowledgement
This chart is decoded from the positive digital regression, not an oscilloscope capture.
M E A S U R E D T R A C E
The selected transaction sends address byte 0x20. Splitting it into a seven-bit address and one direction bit yields target 0x10 and write direction zero. The decoder reads SDA at the first eight rising SCL edges, then separately checks the ninth sample. That response is low, establishing ACK for the plotted address phase.
The waveform is deliberately not relabelled as the hypothetical target 0x50 used in the register-read exercise. Its steady SCL interval is 10.71 us rather than the nominal 10.05 us calculated from the prescaler. Digital values in this trace cannot establish pull-up rise time, voltage thresholds, pad drive strength or electrical compliance. The source VCD hash is recorded in the document evidence manifest.
M E A S U R E D P O S I T I V E R E G R E S S I O N
Chart: SCL
| 0 | 9.02 | 9.02 | 15.05 | 15.05 | 19.91 | 19.91 | 25.94 | 25.94 | 30.62 | 30.62 | 36.65 | 36.65 | 41.33 | 41.33 | 47.36 | 47.36 | 52.04 | 52.04 | 58.07 | 58.07 | 62.75 | 62.75 | 68.78 | 68.78 | 73.46 | 73.46 | 79.49 | 79.49 | 84.17 | 84.17 | 90.2 | 90.2 | 94.88 | 94.88 | 100.91 | 100.91 | 105.59 | 105.59 | 106.91
SCL | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0
Chart: SDA
| 0 | 5 | 5 | 5.71 | 5.71 | 5.72 | 5.72 | 34.64 | 34.64 | 45.35 | 45.35 | 105.591 | 105.591 | 106.91
SDA | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
Logic HIGH=1, LOW=0. Digital simulation, not analogue compliance; source hash retained.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The selected transaction sends address byte 0x20. Splitting it into a seven-bit address and one direction bit yields target 0x10 and write direction zero. The decoder reads SDA at the first eight rising SCL edges, then separately checks the ninth sample. That response is low, establishing ACK for the plotted address phase.
The waveform is deliberately not relabelled as the hypothetical target 0x50 used in the register-read exercise. Its steady SCL interval is 10.71 us rather than the nominal 10.05 us calculated from the prescaler. Digital values in this trace cannot establish pull-up rise time, voltage thresholds, pad drive strength or electrical compliance. The source VCD hash is recorded in the document evidence manifest.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Address byte 0x20 = target 0x10 plus write bit 0. Ninth SCL samples ACK=0. Measured steady SCL period 10.71 us, 93.371 kHz; nominal divider estimate 10.05 us, 99.502 kHz. Extra 66 core cycles per period are observed; their exact internal attribution is not established.
Source VCD hw/protocols/i2c/02_sim/i2c_core.vcd
SHA256 92a33c5d8fa011907725903c0a42a46363a0a713fcafd04ccbc1cf326bed4714
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 12
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
12 / 24
SECTION 10 · LINT
Lint: read code before running it
Verilator checks legal but suspicious code patterns without exercising transactions. A warning
count is a review starting point, not proof of correctness.
L I N T
The retained report contains 3 warning messages and 0 error messages. Categories present:
CASEINCOMPLETE, SYNCASYNCNET, UNUSEDSIGNAL. These figures count report message
headers; repeated warnings are not necessarily independent defects. The report is hashed in this
document evidence manifest.
The invocation deliberately uses -Wno-fatal so warnings remain visible while lint execution can complete. A successful command therefore does not mean every warning was resolved. Width changes, incomplete cases, reset use and unconnected ports need review against the wrapper contract and directed tests.
Lint cannot show that a receive byte is correct, that a transaction finishes, or that an external
electrical interface is safe. Those questions require a checking testbench, implementation evidence
and separate board or signoff work.
R E T A I N E D W A R N I N G R E V I E W
MEASURE | VALUE
Warning message headers | 3
Error message headers | 0
Clean warning-free RTL? | Not claimed
Protocol behaviour proved by lint? | No
S O U R C E / C O M M A N D S
make lint # inspect, do not just count # 00_lint/lint_report.txt
00_lint/Makefile and run_flow.sh: retained Verilator report
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The retained report contains 3 warning messages and 0 error messages. Categories present: CASEINCOMPLETE, SYNCASYNCNET, UNUSEDSIGNAL. These figures count report message headers; repeated warnings are not necessarily independent defects. The report is hashed in this document evidence manifest.
The invocation deliberately uses -Wno-fatal so warnings remain visible while lint execution can complete. A successful command therefore does not mean every warning was resolved. Width changes, incomplete cases, reset use and unconnected ports need review against the wrapper contract and directed tests.
Lint cannot show that a receive byte is correct, that a transaction finishes, or that an external electrical interface is safe. Those questions require a checking testbench, implementation evidence and separate board or signoff work.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 13
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
13 / 24
SECTION 11 · SIMULATION AND VERIFICATION
What the I2C regression establishes
A testbench is code that drives the circuit and judges its outputs. These directed checks use
independent expected data and deliberately failing controls.
S I M U L A T I O N A N D V E R I F I C A T I O N
The bench checks register values, successful A5 and 5A byte transfers, and NACK when the target
model receives an invalid memory address. The existing second controller remains idle. The flow
adds timeout and fatal comparisons, separate interrupt wires and integration through the real
local wrapper.
Repeated START and forced clock stretching occur in the inherited sequence, but there is no independent edge-by-edge property proving every boundary or stretch duration. Third and fourth reads from uninitialised memory are not data-verified. These gaps remain visible rather than being folded into an exhaustive protocol claim.
Negative controls deliberately change expected data or a register result. Their purpose is to show
that the checker rejects a wrong result. A passing negative-control harness means the deliberately
corrupted child run failed as intended; it does not mean the corrupted DUT transaction was
correct.
V E R I F I C A T I O N E V I D E N C E L O C A T I O N S
File / area | Interpretation
02_sim/test.v and positive log | Stimulus, expectations and actual PASS
02_sim negative-control logs | Expected fatal rejection
03_verification | Preserved source / supplemental checks
GATES.md | Acceptance records, not a replacement for logs
A checker must be able to fail
Completion alone is insufficient. Read the successful log and the expected fatal rejection together;
neither is a protocol-compliance certificate.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The bench checks register values, successful A5 and 5A byte transfers, and NACK when the target model receives an invalid memory address. The existing second controller remains idle. The flow adds timeout and fatal comparisons, separate interrupt wires and integration through the real local wrapper.
Repeated START and forced clock stretching occur in the inherited sequence, but there is no independent edge-by-edge property proving every boundary or stretch duration. Third and fourth reads from uninitialised memory are not data-verified. These gaps remain visible rather than being folded into an exhaustive protocol claim.
Negative controls deliberately change expected data or a register result. Their purpose is to show that the checker rejects a wrong result. A passing negative-control harness means the deliberately corrupted child run failed as intended; it does not mean the corrupted DUT transaction was correct.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 14
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
14 / 24
SECTION 12 · SYNTHESIS
Synthesis: a description becomes gates
A netlist is a list of logic cells and their connections. Yosys translates the RTL into cells from
the IHP SG13G2 library.
S Y N T H E S I S
A process design kit, or PDK, contains the process-specific files used by implementation tools. This reference uses IHP SG13G2, not the SKY130 library used by the golden APB primer. Standard cells are predesigned gates and storage elements with characterised timing and physical views.
The source is compiled and checked under the unit workspace before synthesis. Yosys maps the functional logic into the pinned IHP SG13G2 standard-cell library. The current netlist contains 1007 functional cells, excluding $scopeinfo metadata. The structural checker rejects remaining generic logic, latches or unresolved instances.
The mapped count excludes $scopeinfo metadata. It is not the count of every placed instance after clock buffers, repair cells and fillers are added. It also does not mean that the original protocol has been independently proven for all possible transactions.
M A P P I N G R E S U L T
MEASURE | CURRENT RESULT
Top module | i2c_core
Mapped functional cells | 1007
Technology | IHP SG13G2
Unresolved generic logic / latches | Rejected by structural checker
S O U R C E / C O M M A N D S
make synth node verify_build.mjs synth
04_synthesis/synth.tcl; verify_build.mjs synthesis checks
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
A process design kit, or PDK, contains the process-specific files used by implementation tools. This reference uses IHP SG13G2, not the SKY130 library used by the golden APB primer. Standard cells are predesigned gates and storage elements with characterised timing and physical views.
The source is compiled and checked under the unit workspace before synthesis. Yosys maps the functional logic into the pinned IHP SG13G2 standard-cell library. The current netlist contains 1007 functional cells, excluding $scopeinfo metadata. The structural checker rejects remaining generic logic, latches or unresolved instances.
The mapped count excludes $scopeinfo metadata. It is not the count of every placed instance after clock buffers, repair cells and fillers are added. It also does not mean that the original protocol has been independently proven for all possible transactions.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 15
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
15 / 24
SECTION 13 · PHYSICAL IMPLEMENTATION
Floorplan and placement
The floorplan gives the circuit a physical outline. Placement chooses where its cells sit inside
that outline.
P H Y S I C A L I M P L E M E N T A T I O N
The die outline for this standalone block is 300 x 300 um. The floorplan establishes rows and reference power/pin geometry. The placer must fit cells legally without overlaps and with room for routing. This is a block-level educational layout, not a complete padframe or package design.
Mapped functional logic has 1007 cells. After physical additions and fillers, the routed DEF
contains 14,546 placed standard-cell instances. A filler occupies empty row sites; it is not another
functional logic gate. That distinction explains why the two counts differ so much.
Utilisation is the fraction of core area occupied by placed cell area. It is not simply functional-cell
count divided by die size, and it changes between stages. This note does not substitute APB
utilisation, row count or I/O count for unavailable protocol-specific measurements.
A C T U A L P H Y S I C A L R E F E R E N C E
MEASURE | VALUE
Die outline | 300 x 300 um
Mapped functional cells | 1007
Placed standard-cell instances | 14,546
Physical inputs | 06_floorplanning; 07_placement
Placement agreement | DEF compared with decoded GDS
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The die outline for this standalone block is 300 x 300 um. The floorplan establishes rows and reference power/pin geometry. The placer must fit cells legally without overlaps and with room for routing. This is a block-level educational layout, not a complete padframe or package design.
Mapped functional logic has 1007 cells. After physical additions and fillers, the routed DEF contains 14,546 placed standard-cell instances. A filler occupies empty row sites; it is not another functional logic gate. That distinction explains why the two counts differ so much.
Utilisation is the fraction of core area occupied by placed cell area. It is not simply functional-cell count divided by die size, and it changes between stages. This note does not substitute APB utilisation, row count or I/O count for unavailable protocol-specific measurements.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 16
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
16 / 24
SECTION 14 · CLOCK AND WIRES
Clock tree and routing
Clock-tree synthesis distributes clocks to registers. Routing draws the metal connections
between placed cells.
C L O C K A N D W I R E S
A register samples its input at a clock edge. Clock buffers distribute that edge across the block; the difference in arrival times is called skew. The reference is constrained at 50 MHz / 20 ns.
OpenROAD completes the staged physical flow. The reference die is 300 x 300 um. DEF records routed design geometry and cell placement; SPEF captures extracted parasitics used by the timing analysis. The scripts retain stage-specific output so the result can be investigated instead of relying on a final banner.
Real interconnect has resistance and capacitance, called parasitics. Extraction writes these in SPEF for post-route timing. The retained router-rule DRC file is empty. That checks the router view of its work; it is not a full foundry-deck check of the exported polygons.
R E A D T H E P H Y S I C A L E V I D E N C E
ARTIFACT | QUESTION IT ANSWERS
09_place_and_route/route.def | Where are cells and routed connections?
09_place_and_route/route.spef | Which parasitics were extracted?
Router-rule DRC report | Any reported routing-rule violations?
08_sta/timing_report.txt | What does extracted reference timing report?
Two checks can both be called DRC
The empty router report is accepted routing evidence. Foundry DRC is a separate unperformed
obligation; one result cannot stand in for the other.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
A register samples its input at a clock edge. Clock buffers distribute that edge across the block; the difference in arrival times is called skew. The reference is constrained at 50 MHz / 20 ns.
OpenROAD completes the staged physical flow. The reference die is 300 x 300 um. DEF records routed design geometry and cell placement; SPEF captures extracted parasitics used by the timing analysis. The scripts retain stage-specific output so the result can be investigated instead of relying on a final banner.
Real interconnect has resistance and capacitance, called parasitics. Extraction writes these in SPEF for post-route timing. The retained router-rule DRC file is empty. That checks the router view of its work; it is not a full foundry-deck check of the exported polygons.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 17
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
17 / 24
SECTION 15 · REFERENCE TIMING
Two measured reference corners
Static timing analysis adds cell and wire delays without simulating input patterns. Setup asks
whether data arrives early enough; hold asks whether it stays stable long enough.
R E F E R E N C E T I M I N G
The physical clock constraint is 50 MHz / 20 ns. Post-route timing uses the extracted design rather than an ideal pre-route wire estimate. The report at each corner must be inspected for worst setup and hold slack and for VIOLATED markers. The reported values are not a timing guarantee under unstated board, voltage or temperature conditions.
Current TT setup/hold slack is +15.81 / +0.17 ns. The slow-corner values are +14.55 / +0.21 ns.
Both reports contain no VIOLATED marker. These numbers are taken directly from the local report
files at document build time; the evidence manifest retains their hashes.
I/O delays are reference budgets, not a contract with an external target, transceiver or PHY. Bus synchronisation, reset recovery/removal, all additional corners and modes, signal integrity and board timing need their own analysis. Positive slack in these two reports is therefore called reference timing closure, not foundry or system signoff.
L I V E E X T R A C T E D S L A C K , N S
Corner | Worst setup | Worst hold
TT | 15.81 | 0.17
Slow | 14.55 | 0.21
Status | PASS reference reports | No VIOLATED markers
Positive slack has a stated boundary
Slack is remaining timing margin. These values apply to the listed clocks, I/O budgets and two library
corners; they are not a board-timing or manufacturing signoff guarantee.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The physical clock constraint is 50 MHz / 20 ns. Post-route timing uses the extracted design rather than an ideal pre-route wire estimate. The report at each corner must be inspected for worst setup and hold slack and for VIOLATED markers. The reported values are not a timing guarantee under unstated board, voltage or temperature conditions.
Current TT setup/hold slack is +15.81 / +0.17 ns. The slow-corner values are +14.55 / +0.21 ns. Both reports contain no VIOLATED marker. These numbers are taken directly from the local report files at document build time; the evidence manifest retains their hashes.
I/O delays are reference budgets, not a contract with an external target, transceiver or PHY. Bus synchronisation, reset recovery/removal, all additional corners and modes, signal integrity and board timing need their own analysis. Positive slack in these two reports is therefore called reference timing closure, not foundry or system signoff.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 18
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
18 / 24
SECTION 16 · GDS STREAM-OUT
Count the right objects
GDS stores layout polygons and hierarchical cell references. Stream-out combines routed
geometry with the real standard-cell layouts from the PDK.
G D S S T R E A M - O U T
The GDS file contains 1,583,844 bytes and 48 structures. The independent decoder finds 14,546 placed standard-cell instances including fillers. That placement count is intentionally much larger than the 1007 mapped functional cells: filler instances occupy unused placement sites and structures are unique hierarchy definitions.
The decoder compares exported cell identities, coordinates and orientations against the routed
DEF. A deliberately altered placement/export expectation fails, including under Python
optimisation, so acceptance is not implemented with removable assert-only checks. Raw file
SHA256 is a run-specific fingerprint because stream-out timestamps can change.
The OpenROAD router-rule DRC report is empty. It is not a foundry-deck DRC result. LVS, antenna,
scan/DFT, power integrity, padframe, tap/endcap strategy and manufacturing signoff remain
unperformed. No empty routing report is promoted into a DRC-clean tapeout claim.
L I V E E X P O R T M E A S U R E M E N T S
Quantity | Current value
Mapped functional cells | 1007
GDS bytes | 1,583,844
GDS structures | 48
Placed standard-cell instances | 14,546
Die | 300 x 300 um
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The GDS file contains 1,583,844 bytes and 48 structures. The independent decoder finds 14,546 placed standard-cell instances including fillers. That placement count is intentionally much larger than the 1007 mapped functional cells: filler instances occupy unused placement sites and structures are unique hierarchy definitions.
The decoder compares exported cell identities, coordinates and orientations against the routed DEF. A deliberately altered placement/export expectation fails, including under Python optimisation, so acceptance is not implemented with removable assert-only checks. Raw file SHA256 is a run-specific fingerprint because stream-out timestamps can change.
The OpenROAD router-rule DRC report is empty. It is not a foundry-deck DRC result. LVS, antenna, scan/DFT, power integrity, padframe, tap/endcap strategy and manufacturing signoff remain unperformed. No empty routing report is promoted into a DRC-clean tapeout claim.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 19
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
19 / 24
SECTION 17 · UNPERFORMED SIGNOFF
DRC and LVS: what is still missing
Design rule checking asks whether geometry follows the process rules. Layout versus
schematic asks whether the extracted layout circuit matches the intended netlist.
U N P E R F O R M E D S I G N O F F
Foundry DRC requires the applicable, qualified rule deck and an inspected report on the final polygons. Typical checks include minimum widths, spacing and enclosure. No foundry-deck DRC result has been accepted for this protocol reference. The router report is narrower evidence.
LVS requires extracting a circuit from the layout and comparing devices and connectivity with the intended circuit. A structural GDS decoder checking cell references, coordinates and orientations does not perform that extraction or connectivity comparison. No accepted LVS match is available.
Antenna, scan/DFT, power integrity, padframe, tap/endcap strategy and manufacturing release
remain unperformed. The golden APB primer reports its own separate checks; those results do not
transfer to SG13G2 or to this design.
S E P A R A T E A C C E P T E D E X P O R T F R O M M I S S I N G S I G N O F F
CHECK | THIS REFERENCE
Router-rule report | Empty; narrower routing evidence
Decoded GDS placement | PASS structural/export agreement
Foundry-deck DRC | UNPERFORMED
Extracted-layout LVS | UNPERFORMED
Manufacturing readiness | Not claimed
A GDS file is not tapeout approval
This package is suitable for studying and reproducing a block implementation. Do not hand it off as a
signoff-clean manufacturing design.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Foundry DRC requires the applicable, qualified rule deck and an inspected report on the final polygons. Typical checks include minimum widths, spacing and enclosure. No foundry-deck DRC result has been accepted for this protocol reference. The router report is narrower evidence.
LVS requires extracting a circuit from the layout and comparing devices and connectivity with the intended circuit. A structural GDS decoder checking cell references, coordinates and orientations does not perform that extraction or connectivity comparison. No accepted LVS match is available.
Antenna, scan/DFT, power integrity, padframe, tap/endcap strategy and manufacturing release remain unperformed. The golden APB primer reports its own separate checks; those results do not transfer to SG13G2 or to this design.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 20
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
20 / 24
SECTION 18 · RESULTS SUMMARY
Everything at a glance
Read each result together with the question it actually answers. The same PASS label never
implies every protocol or manufacturing obligation is closed.
R E S U L T S S U M M A R Y
The directed functional result and the physical export result are both useful, but they prove different things. The physical build uses the fixed wrapper configuration and reference constraints. Additional modes, external peripherals, arbitrary clock relationships and board operation require their own evidence.
Important protocol boundary: Arbitration is not decisively tested. Stretching and repeated START have indirect data/completion coverage only.
F U L L R E F E R E N C E F L O W
STAGE | TOOL / EVIDENCE | STATUS
Lint | Verilator; 3 retained warnings | Review
Simulation | Independent directed expectations | PASS directed
Negative controls | Deliberate fatal mismatches | PASS rejection
Synthesis | Yosys; 1007 mapped cells | PASS mapping
Floorplan / placement | OpenROAD; 300 x 300 um | PASS reference
Routing / extraction | DEF and SPEF retained | PASS reference
Timing | TT and slow setup / hold | PASS reference
GDS | KLayout; 1,583,844 bytes | PASS export
Foundry DRC / LVS | No accepted report | UNPERFORMED
Full-chip / board | No accepted integration proof | UNPERFORMED
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The directed functional result and the physical export result are both useful, but they prove different things. The physical build uses the fixed wrapper configuration and reference constraints. Additional modes, external peripherals, arbitrary clock relationships and board operation require their own evidence.
Important protocol boundary: Arbitration is not decisively tested. Stretching and repeated START have indirect data/completion coverage only.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 21
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
21 / 24
SECTION 19 · RUN IT YOURSELF
Run it yourself in WSL
Use the pinned source, the unit tool lock and the external PDK revision together.
R U N I T Y O U R S E L F
The proven entry point is a WSL login Bash shell. igny init prepares the packaging runtime.
Unsetting CRUCIBLE_ENV after initialisation allows the unit crucible.toml workspace selection to
control tool resolution rather than an inherited environment override. This is the observed
workflow, not a change to Crucible internals.
Each unit has its existing environment and lock. The common tool set includes Icarus, Verilator,
Yosys, OpenROAD and klayout-stream. The separate PDK checkout is IHP SG13G2 revision
22f43352dd8219f9007eb659e422e0d5fe28c5fb. A tool lock does not pin that external PDK by
itself; IHP_PDK_ROOT must point to the matching installation.
The documented machine could not use the pip klayout package as the expected stream-out
executable; igny tool install klayout-stream supplies the proven converter. make lint sim checks
functional behaviour, make flow executes the staged implementation, and node verify_build.mjs
all inspects artifacts. Review normal and intentionally failing logs before accepting the result.
Re-running a simulation can replace its VCD and invalidate an earlier document trace hash. Retain
a document evidence manifest or regenerate the measured figures after the positive run. Do not
silently preserve an old chart while claiming it is the newly generated waveform.
S O U R C E / C O M M A N D S
igny init unset CRUCIBLE_ENV cd hw/protocols/i2c igny workspace sync igny tool install klayout-stream make lint sim make flow node verify_build.mjs all
Run after entering the repository in WSL login Bash; PDK required.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The proven entry point is a WSL login Bash shell. igny init prepares the packaging runtime. Unsetting CRUCIBLE_ENV after initialisation allows the unit crucible.toml workspace selection to control tool resolution rather than an inherited environment override. This is the observed workflow, not a change to Crucible internals.
Each unit has its existing environment and lock. The common tool set includes Icarus, Verilator, Yosys, OpenROAD and klayout-stream. The separate PDK checkout is IHP SG13G2 revision 22f43352dd8219f9007eb659e422e0d5fe28c5fb. A tool lock does not pin that external PDK by itself; IHP_PDK_ROOT must point to the matching installation.
The documented machine could not use the pip klayout package as the expected stream-out executable; igny tool install klayout-stream supplies the proven converter. make lint sim checks functional behaviour, make flow executes the staged implementation, and node verify_build.mjs all inspects artifacts. Review normal and intentionally failing logs before accepting the result.
Re-running a simulation can replace its VCD and invalidate an earlier document trace hash. Retain a document evidence manifest or regenerate the measured figures after the positive run. Do not silently preserve an old chart while claiming it is the newly generated waveform.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 22
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
22 / 24
SECTION 20 · SOURCES AND REMAINING WORK
Sources, ownership and remaining work
The pinned revision identifies the baseline; local integration changes are described separately.
S O U R C E S A N D R E M A I N I N G W O R K
Upstream: https://github.com/freecores/i2c Pinned commit: 3b067f00ccced753b0502024766a51f58f3e04bc Licence: Richard Herveille permission notice, 2001. Original source notices remain in the RTL. The document is authored by Ignytion; this does not transfer ownership of upstream code or remove its licence obligations.
Local modifications, directed test stimulus and source boundaries are recorded in hw/protocols/i2c/README.md and the repository append-only .context.md. The first three protocol lessons have separate editable 16:9 student decks; this A4 technical note is a reading and evidence document, not a replacement for their instructor notes.
Primary reading: NXP UM10204 Rev. 7 and TI SLVA689 for pull-up arithmetic.
Canonical reading: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf and
https://www.ti.com/lit/pdf/slva689
Open work remains explicit: Arbitration is not decisively tested. Stretching and repeated START have indirect data/completion coverage only. Full-chip integration, manufacturing checks and board validation are not closed by the standalone reference flow. The reader can reproduce the listed evidence without assuming those larger obligations have already been completed.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Upstream: https://github.com/freecores/i2c
Pinned commit: 3b067f00ccced753b0502024766a51f58f3e04bc
Licence: Richard Herveille permission notice, 2001. Original source notices remain in the RTL. The document is authored by Ignytion; this does not transfer ownership of upstream code or remove its licence obligations.
Local modifications, directed test stimulus and source boundaries are recorded in hw/protocols/i2c/README.md and the repository append-only .context.md. The first three protocol lessons have separate editable 16:9 student decks; this A4 technical note is a reading and evidence document, not a replacement for their instructor notes.
Primary reading: NXP UM10204 Rev. 7 and TI SLVA689 for pull-up arithmetic.
Canonical reading: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf and https://www.ti.com/lit/pdf/slva689
Open work remains explicit: Arbitration is not decisively tested. Stretching and repeated START have indirect data/completion coverage only. Full-chip integration, manufacturing checks and board validation are not closed by the standalone reference flow. The reader can reproduce the listed evidence without assuming those larger obligations have already been completed.
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 23
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
23 / 24
SECTION 21 · DESIGN VOCABULARY
Glossary: design and protocol
Definitions for reading the protocol rules and the checked RTL. Physical implementation
terms follow on the next page.
D E S I G N A N D V E R I F I C A T I O N
TERM | WHAT IT MEANS
Protocol | Rules for exchanging information between devices
RTL | Registers and the logic moving values between them
Verilog | A language used to describe hardware
FSM | A circuit progressing through defined states
Lint | Static source checks; no transaction execution
Testbench | Code that supplies inputs and checks outputs
Coverage | Which defined situations were exercised
Negative control | An intentionally wrong case the checker must reject
VCD | Digital signal-change trace from a simulation
Handshake | Signals agreeing when data is accepted
ACK / NACK | Ninth-bit acceptance / non-acceptance response
PRER | Two-byte clock prescaler register
Open drain | Drive low or release; never actively drive high
Wishbone | Local register bus, distinct from the serial I2C bus
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 24
Ignytion io
I2C · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
24 / 24
SECTION 22 · PHYSICAL VOCABULARY
Glossary: implementation and signoff
These definitions help distinguish a successfully exported reference layout from a
manufacturing-ready design.
P H Y S I C A L I M P L E M E N T A T I O N
TERM | WHAT IT MEANS
Synthesis | Translate RTL into a technology-cell circuit
Netlist | Cells and the connections between them
Standard cell | Predesigned logic/storage cell in a process library
PDK | Process design kit: process-specific implementation files
SG13G2 | IHP process used by these reference builds
Floorplan | Die/core outline, rows, power and pin geometry
Placement | Choose legal positions for cells
Filler | Physical row-site cell, not functional logic
CTS / skew | Clock distribution / difference in arrival times
Routing / via | Metal connections / links between metal layers
Parasitics / SPEF | Wire resistance/capacitance / extracted data format
Corner | A characterised process, voltage and temperature case
STA / slack | Static timing analysis / remaining timing margin
DEF / GDS | Placement/routing exchange / polygon hierarchy
DRC | Check geometry against applicable process rules
LVS | Compare the extracted layout circuit with its netlist
Signoff | Accepted applicable release checks; unperformed here
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/I2C_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Source area: hw/protocols/i2c
https://github.com/freecores/i2c
Pinned commit 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notice:
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.