## Slide 1
Ignytion io
Ignytion IO · ignytion.io
SPI PROTOCOL SERIES · OCTOBER 2026
IGNYTION IO · TECHNICAL LAB NOTE
SPI protocol:
From RTL to routed GDS
A beginner's walkthrough of a checked open-source reference build
Follow spi_core from its communication rules and Verilog source to a routed IHP SG13G2 layout. Worked calculations, measured digital traces and tool results are identified separately. This is an educational block, not a manufactured chip or a signoff-ready design.
STAGE | WHAT IT PRODUCED | RESULT
Simulation | Listed directed checks | PASS directed
Synthesis | 131 mapped functional cells | PASS mapping
Routing | Routed DEF and extracted SPEF | PASS reference
Timing | TT and slow setup / hold | PASS reference
GDS | Decoded placement agreement | PASS export
Foundry DRC / LVS | No accepted result | UNPERFORMED
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Follow spi_core from its communication rules and Verilog source to a routed IHP SG13G2 layout. Worked calculations, measured digital traces and tool results are identified separately. This is an educational block, not a manufactured chip or a signoff-ready design.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 2
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
02 / 24
CONTENTS
What is in this document
Start with the wire-level rules, then follow the same circuit through the tools. Each section has
a specific evidence boundary.
R E A D I N G M A P
SECTION | PAGE
Start here | p. 03
Chip design in ten minutes | p. 04
One clock, two data directions | p. 05
Decode CPOL and CPHA as edges | p. 06
Divider, latency and return-path margin | p. 07
A request pulse, not a stream contract | p. 08
Sixteen edges make one byte | p. 09
A byte envelope is not a flash command | p. 10
A5 transmitted, 5A returned | p. 11
Lint: read code before running it | p. 12
Four tested parameter pairs, not eight | p. 13
Synthesis: a description becomes gates | p. 14
Floorplan and placement | p. 15
Clock tree and routing | p. 16
Two measured reference corners | p. 17
Count the right objects | p. 18
DRC and LVS: what is still missing | p. 19
Everything at a glance | p. 20
Run it yourself in WSL | p. 21
Sources, ownership and remaining work | p. 22
Design and physical glossary | p. 23–24
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 3
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
03 / 24
SECTION 1 · START HERE
Start here
A protocol is an agreement about how connected devices exchange information: which wire
carries each bit, when to sample it, and how to recognise a complete transfer.
W H A T W E B U I L T A N D W H A T I T P R O V E S
A Verilog description represents circuits, not software instructions running one after another. Registers remember values; combinational logic calculates the next values. A clock advances the registered state. The next pages first explain this protocol at its wires, then connect those rules to the actual reference RTL.
The implemented unit is spi_core in hw/protocols/spi. It is a fixed reference block, not the Jane Street programmable combined emulator or a Tiny Tapeout submission top. No new competition architecture, instruction set, pin map or authority decision is implied by these documents.
Only four mode/divider pairs are tested; the hardened core is mode 0, divider 2. General multi-byte CS envelopes are absent. Later pages give the exact stimulus and the implementation evidence rather than using a broad protocol-compliant label. A successful mapped netlist, routed DEF and decoded GDS establish concrete implementation/export results, not readiness to manufacture.
The reading path starts with chip-design vocabulary, then develops the protocol, calculations, local interface and failure cases. Separate sections explain lint, simulation, synthesis, placement, routing, timing and GDS. The last two pages define design and physical terms. No prior ASIC-flow experience is assumed.
E V I D E N C E V O C A B U L A R Y
Label | Meaning in this document
Worked example | Explicit assumptions; independently calculated
Measured trace | Positive digital regression VCD, where present
Directed PASS | Listed assertions and negative controls
Routed / decoded GDS | Physical export and structural agreement
Signoff | Not performed or claimed
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
A Verilog description represents circuits, not software instructions running one after another. Registers remember values; combinational logic calculates the next values. A clock advances the registered state. The next pages first explain this protocol at its wires, then connect those rules to the actual reference RTL.
The implemented unit is spi_core in hw/protocols/spi. It is a fixed reference block, not the Jane Street programmable combined emulator or a Tiny Tapeout submission top. No new competition architecture, instruction set, pin map or authority decision is implied by these documents.
Only four mode/divider pairs are tested; the hardened core is mode 0, divider 2. General multi-byte CS envelopes are absent. Later pages give the exact stimulus and the implementation evidence rather than using a broad protocol-compliant label. A successful mapped netlist, routed DEF and decoded GDS establish concrete implementation/export results, not readiness to manufacture.
The reading path starts with chip-design vocabulary, then develops the protocol, calculations, local interface and failure cases. Separate sections explain lint, simulation, synthesis, placement, routing, timing and GDS. The last two pages define design and physical terms. No prior ASIC-flow experience is assumed.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 4
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
04 / 24
SECTION 2 · CHIP DESIGN
Chip design in ten minutes
Each stage makes the same circuit more concrete. The folders below are the actual unit
layout, not a copied APB command list.
C H I P D E S I G N
RTL states what hardware should do. A simulator checks selected input sequences before any
silicon exists. Synthesis replaces that description with gates from a process library. Physical tools
choose positions and metal routes. Timing analysis checks the resulting delays; stream-out writes
the mask-layout geometry.
T H E P I P E L I N E , S T A G E B Y S T A G E
FOLDER | WHAT HAPPENS HERE
00_lint | Read code for risky patterns; retained warnings
01_rtl | Pinned source and the local wrapper
02_sim | Independent stimulus, comparisons and fatal controls
03_verification | Supplemental checks; not a universal UVM PASS
04_synthesis | Map functional logic to SG13G2 cells
05_dft | Manufacturing test work remains unperformed
06_floorplanning | Die outline, rows, power and pin locations
07_placement | Choose legal positions for mapped cells
09_place_and_route | Clock tree, routing and SPEF extraction
08_sta | Read post-route TT and slow timing reports
10_gds | Stream-out and independent placement decoder
11_physical_verification | Foundry DRC / LVS remain unperformed
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
RTL states what hardware should do. A simulator checks selected input sequences before any silicon exists. Synthesis replaces that description with gates from a process library. Physical tools choose positions and metal routes. Timing analysis checks the resulting delays; stream-out writes the mask-layout geometry.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 5
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
05 / 24
SECTION 3 · INTERFACE RULES
One clock, two data directions
Controller and peripheral exchange bits simultaneously while one peripheral owns the
selected response path.
I N T E R F A C E R U L E S
The repository keeps conventional MOSI/MISO names. Multiple peripherals generally share clock and data, with separate chip-select signals. Only the selected peripheral should drive a shared MISO.
A full-duplex transfer does not double the clock count: both wires carry a bit in each period. An implementation may write each bit by index, as this core does, rather than literally shift a register; both can produce the same assembled byte. The outgoing value and incoming value need not match.
Unselected peripherals need appropriate high-impedance behaviour if MISO is shared. Two simultaneously selected push-pull devices can contend, unlike I2C open-drain arbitration. A board that uses separate MISO wires has a different topology. The present unit represents one peripheral selection and has no multi-CS decoder; this section explains system wiring rather than claiming that logic already exists.
D I G I T A L S I G N A L O W N E R S H I P
Signal | Controller / peripheral
SCLK and MOSI | Controller drives
MISO | Selected peripheral drives
CS_n | Controller frames selection
Unselected MISO | Must not contend on a shared wire
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The repository keeps conventional MOSI/MISO names. Multiple peripherals generally share clock and data, with separate chip-select signals. Only the selected peripheral should drive a shared MISO.
A full-duplex transfer does not double the clock count: both wires carry a bit in each period. An implementation may write each bit by index, as this core does, rather than literally shift a register; both can produce the same assembled byte. The outgoing value and incoming value need not match.
Unselected peripherals need appropriate high-impedance behaviour if MISO is shared. Two simultaneously selected push-pull devices can contend, unlike I2C open-drain arbitration. A board that uses separate MISO wires has a different topology. The present unit represents one peripheral selection and has no multi-CS decoder; this section explains system wiring rather than claiming that logic already exists.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 6
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
06 / 24
SECTION 4 · SAMPLING RULES
Decode CPOL and CPHA as edges
Leading means movement away from idle; trailing means return to idle. It does not always
mean rising and falling.
S A M P L I N G R U L E S
With CPOL one, leading is falling. These relative names simplify the mode table. The bus should
settle to its configured idle polarity before and after a transaction.
For CPHA zero, the first data bit must be available before the first leading edge. For CPHA one, the
first leading edge launches data and the trailing edge samples it. Incorrect phase often yields a
one-bit shift.
A mode mismatch does not necessarily produce a clean error flag, because SPI has no mandatory
acknowledgement or checksum.
F O U R M O D E D E F I N I T I O N S
Mode | Idle | Launch/update | Sample
0 | Low | Falling, first bit preloaded | Rising
1 | Low | Rising | Falling
2 | High | Rising, first bit preloaded | Falling
3 | High | Falling | Rising
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
With CPOL one, leading is falling. These relative names simplify the mode table. The bus should settle to its configured idle polarity before and after a transaction.
For CPHA zero, the first data bit must be available before the first leading edge. For CPHA one, the first leading edge launches data and the trailing edge samples it. Incorrect phase often yields a one-bit shift.
A mode mismatch does not necessarily produce a clean error flag, because SPI has no mandatory acknowledgement or checksum.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 7
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
07 / 24
SECTION 5 · TIMING CALCULATION
Divider, latency and return-path margin
The physical reference and the fast simulation have different clock frequencies.
T I M I N G C A L C U L A T I O N
With half-bit divider D, the serial frequency is fcore / (2D). The 50 MHz physical reference with D=2 therefore has a nominal 12.5 MHz SCLK and a 640 ns eight-bit wire interval. D=3 would give 8.333 MHz and 960 ns, but that is a different elaborated configuration. Handshake and CS overhead add to these wire-only durations.
The bench uses a 100 MHz core, not 50 MHz. Its mode-0 D=2 measured transaction therefore has a 40 ns SCLK period, 25 MHz SCLK and 320 ns across eight periods. These numbers describe the regression only; they do not certify the hardened block at a 100 MHz core clock.
A separate board-budget example assumes a 40 ns half-period, 5 ns peripheral clock-to-output, 2 ns round-trip delay and 3 ns receiver setup. The remaining 30 ns is arithmetic margin before pad delay, skew and uncertainty. Internal STA closure at the core clock is not proof of the external peripheral timing contract.
S I M U L A T I O N P A R A M E T E R C O V E R A G E
Mode | Divider 2 | Divider 3
0 | Tested; hardened | Untested
1 | Untested | Tested
2 | Tested | Untested
3 | Untested | Tested
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
With half-bit divider D, the serial frequency is fcore / (2D). The 50 MHz physical reference with D=2 therefore has a nominal 12.5 MHz SCLK and a 640 ns eight-bit wire interval. D=3 would give 8.333 MHz and 960 ns, but that is a different elaborated configuration. Handshake and CS overhead add to these wire-only durations.
The bench uses a 100 MHz core, not 50 MHz. Its mode-0 D=2 measured transaction therefore has a 40 ns SCLK period, 25 MHz SCLK and 320 ns across eight periods. These numbers describe the regression only; they do not certify the hardened block at a 100 MHz core clock.
A separate board-budget example assumes a 40 ns half-period, 5 ns peripheral clock-to-output, 2 ns round-trip delay and 3 ns receiver setup. The remaining 30 ns is arithmetic margin before pad delay, skew and uncertainty. Internal STA closure at the core clock is not proof of the external peripheral timing contract.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 8
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
08 / 24
SECTION 6 · RTL INTERFACE
A request pulse, not a stream contract
The interface names resemble ready-valid signalling, but the imported controller expects a
one-cycle request.
R T L I N T E R F A C E
spi_core wraps the pinned Nandland SPI_Master. The interface is a launch-pulse contract, not an arbitrary AXI stream. There is no rx_ready input to apply receive backpressure. Upstream ready may initially require clocks after reset to settle. Software or a surrounding controller must observe the documented handshake.
The one-cycle delayed valid supports the first-bit preload path. Once the byte has been accepted, the source may change its input data because the core holds a copy. However i_TX_DV is a pulse contract, not a general sustained ready-valid stream. Holding it high retriggers the clock-edge setup logic, which is a misuse of this interface.
The entire CS behaviour is this expression, which makes its limited contract easy to inspect. It is
not a command sequencer with programmable CS setup/hold or a multi-byte length register.
Preserve this boundary in lab exercises.
S O U R C E / C O M M A N D S
assign cs_n = !reset_release[1] || (tx_ready && !tx_valid);
hw/protocols/spi/01_rtl/spi_core.v:32
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
spi_core wraps the pinned Nandland SPI_Master. The interface is a launch-pulse contract, not an arbitrary AXI stream. There is no rx_ready input to apply receive backpressure. Upstream ready may initially require clocks after reset to settle. Software or a surrounding controller must observe the documented handshake.
The one-cycle delayed valid supports the first-bit preload path. Once the byte has been accepted, the source may change its input data because the core holds a copy. However i_TX_DV is a pulse contract, not a general sustained ready-valid stream. Holding it high retriggers the clock-edge setup logic, which is a misuse of this interface.
The entire CS behaviour is this expression, which makes its limited contract easy to inspect. It is not a command sequencer with programmable CS setup/hold or a multi-byte length register. Preserve this boundary in lab exercises.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 9
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
09 / 24
SECTION 7 · CONTROL SEQUENCE
Sixteen edges make one byte
The real controller uses an edge counter and generated leading/trailing flags.
C O N T R O L S E Q U E N C E
A request loads sixteen edge events for an eight-bit transfer. The divider produces leading and trailing flags; TX and RX processes use those flags according to CPHA. The engine returns ready once no edges remain. Keeping valid asserted reloads the counter, so a normal ready-valid producer cannot be attached without adapting the contract. This is a source-derived misuse warning, not a separately measured injected-failure scenario.
The inspected source comes directly from the pinned upstream implementation. r_RX_Bit_Count selects the destination bit, so no shift operator is required. o_RX_DV is a completion pulse and has no receive ready signal. A downstream consumer must capture the byte when that pulse appears.
The bench interrupts an active transfer with reset and checks recovery. Physical reset integration still requires reset-domain analysis. The core clock should keep running for reset release. Lint reports a mixed synchronous/asynchronous use associated with the synchroniser, which remains documented rather than being hidden.
S O U R C E - D E R I V E D C O N T R O L S E Q U E N C E
Phase | State condition | Action
Accept | i_TX_DV pulse | Load 16 edge events, clear ready
Leading edge | Half-period count reached | Toggle clock, pulse leading flag
Trailing edge | Full-period count reached | Toggle clock, pulse trailing flag
Complete | Edge count zero | Return ready, RX valid pulses
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
A request loads sixteen edge events for an eight-bit transfer. The divider produces leading and trailing flags; TX and RX processes use those flags according to CPHA. The engine returns ready once no edges remain. Keeping valid asserted reloads the counter, so a normal ready-valid producer cannot be attached without adapting the contract. This is a source-derived misuse warning, not a separately measured injected-failure scenario.
The inspected source comes directly from the pinned upstream implementation. r_RX_Bit_Count selects the destination bit, so no shift operator is required. o_RX_DV is a completion pulse and has no receive ready signal. A downstream consumer must capture the byte when that pulse appears.
The bench interrupts an active transfer with reset and checks recovery. Physical reset integration still requires reset-domain analysis. The core clock should keep running for reset release. Lint reports a mixed synchronous/asynchronous use associated with the synchroniser, which remains documented rather than being hidden.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 10
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
10 / 24
SECTION 8 · INTEGRATION LIMITS
A byte envelope is not a flash command
The wrapper deasserts selection after each byte. Many real devices require one continuous
envelope around several bytes.
I N T E G R A T I O N L I M I T S
A hypothetical flash read can use the five-byte sequence 03 00 01 02 00: command 03, a
three-byte address 000102, then a dummy transmit byte during which data returns. At 12.5 MHz,
forty SCLK periods take 3.2 us before selection and handshake overhead. The device convention
must be checked against its data sheet. The current byte wrapper cannot preserve one CS
envelope across this complete command.
This is a hypothetical classic three-byte-address read convention; verify the actual flash data sheet
before using it. The present wrapper asserts CS for a single byte envelope and does not
implement a general multi-byte transaction controller. Five transferred bytes take forty SCLK
periods, but keeping CS asserted across them requires another transaction-level design.
The local regression exhausts byte values, which makes it less likely that a lucky test pattern hides
a reversal.
One-bit shifts suggest an edge/phase mismatch; all ones can indicate an undriven pulled-up MISO
line. Signal-integrity failures may depend on frequency or wiring. These are diagnostic candidates
rather than guarantees; inspect the actual peripheral electrical interface and timing.
B E F O R E A T T A C H I N G A P E R I P H E R A L
Question | Required answer
SPI mode and bit order? | From the peripheral data sheet
CS across command / address / data? | Adapt envelope if required
MISO output-disable timing? | Check shared-line contention
Error detection? | Application/device-specific; no mandatory SPI CRC
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
A hypothetical flash read can use the five-byte sequence 03 00 01 02 00: command 03, a three-byte address 000102, then a dummy transmit byte during which data returns. At 12.5 MHz, forty SCLK periods take 3.2 us before selection and handshake overhead. The device convention must be checked against its data sheet. The current byte wrapper cannot preserve one CS envelope across this complete command.
This is a hypothetical classic three-byte-address read convention; verify the actual flash data sheet before using it. The present wrapper asserts CS for a single byte envelope and does not implement a general multi-byte transaction controller. Five transferred bytes take forty SCLK periods, but keeping CS asserted across them requires another transaction-level design.
The local regression exhausts byte values, which makes it less likely that a lucky test pattern hides a reversal.
One-bit shifts suggest an edge/phase mismatch; all ones can indicate an undriven pulled-up MISO line. Signal-integrity failures may depend on frequency or wiring. These are diagnostic candidates rather than guarantees; inspect the actual peripheral electrical interface and timing.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 11
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
11 / 24
SECTION 9 · MEASURED TRACE
A5 transmitted, 5A returned
A positive mode-0 transaction is independently decoded in both directions.
M E A S U R E D T R A C E
The selected peripheral model returns the complement of each transmitted byte. With MOSI A5,
MISO must therefore be 5A. Eight rising SCLK edges inside the active-low CS interval are
reconstructed separately for each data wire. Success is not inferred by looping the controller
output into its input.
Successive rising edges are 40 ns apart: this trace uses the 100 MHz bench clock and divider 2, giving 25 MHz SCLK. The four ideal mode illustrations in the student lesson instead use MISO 3C to demonstrate sampling-edge logic. That deliberate example value is not the responder value measured here. The VCD hash and trace decode remain attached to the figure data.
M E A S U R E D P O S I T I V E R E G R E S S I O N
Chart: CS_n
| 0 | 0.015 | 0.015 | 0.04 | 0.04 | 0.375 | 0.375 | 0.4 | 0.4 | 0.415
CS_n | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0
Chart: SCLK
| 0 | 0.015 | 0.015 | 0.075 | 0.075 | 0.095 | 0.095 | 0.115 | 0.115 | 0.135 | 0.135 | 0.155 | 0.155 | 0.175 | 0.175 | 0.195 | 0.195 | 0.215 | 0.215 | 0.235 | 0.235 | 0.255 | 0.255 | 0.275 | 0.275 | 0.295 | 0.295 | 0.315 | 0.315 | 0.335 | 0.335 | 0.355 | 0.355 | 0.375 | 0.375 | 0.415
SCLK | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0
Chart: MOSI
| 0 | 0.015 | 0.015 | 0.095 | 0.095 | 0.135 | 0.135 | 0.175 | 0.175 | 0.255 | 0.255 | 0.295 | 0.295 | 0.335 | 0.335 | 0.415
MOSI | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
Chart: MISO
| 0 | 0.04 | 0.04 | 0.095 | 0.095 | 0.135 | 0.135 | 0.175 | 0.175 | 0.255 | 0.255 | 0.295 | 0.295 | 0.335 | 0.335 | 0.415
MISO | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0
Logic HIGH=1, LOW=0. Digital simulation, not analogue compliance; source hash retained.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The selected peripheral model returns the complement of each transmitted byte. With MOSI A5, MISO must therefore be 5A. Eight rising SCLK edges inside the active-low CS interval are reconstructed separately for each data wire. Success is not inferred by looping the controller output into its input.
Successive rising edges are 40 ns apart: this trace uses the 100 MHz bench clock and divider 2, giving 25 MHz SCLK. The four ideal mode illustrations in the student lesson instead use MISO 3C to demonstrate sampling-edge logic. That deliberate example value is not the responder value measured here. The VCD hash and trace decode remain attached to the figure data.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Mode 0: eight rising SCLK edges decode MOSI A5 and independent MISO 5A. Divider 2, 100 MHz simulation core, measured SCLK period 40 ns (25 MHz). Physical reference core target is separately 50 MHz.
Source VCD hw/protocols/spi/02_sim/spi_core.vcd
SHA256 c509ff00fb97b21521d32bf028792999d14e6a00aa24e581d1d14ed81c4c80ba
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 12
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
12 / 24
SECTION 10 · LINT
Lint: read code before running it
Verilator checks legal but suspicious code patterns without exercising transactions. A warning
count is a review starting point, not proof of correctness.
L I N T
The retained report contains 1 warning messages and 0 error messages. Categories present:
SYNCASYNCNET. These figures count report message headers; repeated warnings are not
necessarily independent defects. The report is hashed in this document evidence manifest.
The invocation deliberately uses -Wno-fatal so warnings remain visible while lint execution can complete. A successful command therefore does not mean every warning was resolved. Width changes, incomplete cases, reset use and unconnected ports need review against the wrapper contract and directed tests.
Lint cannot show that a receive byte is correct, that a transaction finishes, or that an external
electrical interface is safe. Those questions require a checking testbench, implementation evidence
and separate board or signoff work.
R E T A I N E D W A R N I N G R E V I E W
MEASURE | VALUE
Warning message headers | 1
Error message headers | 0
Clean warning-free RTL? | Not claimed
Protocol behaviour proved by lint? | No
S O U R C E / C O M M A N D S
make lint # inspect, do not just count # 00_lint/lint_report.txt
00_lint/Makefile and run_flow.sh: retained Verilator report
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The retained report contains 1 warning messages and 0 error messages. Categories present: SYNCASYNCNET. These figures count report message headers; repeated warnings are not necessarily independent defects. The report is hashed in this document evidence manifest.
The invocation deliberately uses -Wno-fatal so warnings remain visible while lint execution can complete. A successful command therefore does not mean every warning was resolved. Width changes, incomplete cases, reset use and unconnected ports need review against the wrapper contract and directed tests.
Lint cannot show that a receive byte is correct, that a transaction finishes, or that an external electrical interface is safe. Those questions require a checking testbench, implementation evidence and separate board or signoff work.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 13
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
13 / 24
SECTION 11 · SIMULATION AND VERIFICATION
Four tested parameter pairs, not eight
A testbench is code that drives the circuit and judges its outputs. These directed checks use
independent expected data and deliberately failing controls.
S I M U L A T I O N A N D V E R I F I C A T I O N
The bench instantiates mode 0 with divider 2, mode 1 with divider 3, mode 2 with divider 2 and
mode 3 with divider 3. Each checks all 256 transmitted byte values against an independently
generated complementary receive byte. The mode and divider are correlated; this is not a
four-mode by two-divider cross product.
The real hardened wrapper fixes mode 0 and divider 2. Other modes appearing in simulation do
not mean that configuration can be changed after fabrication. Likewise, general continuous
multi-byte CS framing, multiple peripheral selection and held-valid misuse are not established by
the directed byte tests.
A deliberately wrong receive-byte expectation causes a fatal run. Edge and CS checks accompany
the data comparison. The checker distinguishes a correct byte from mere end-of-simulation, while
still leaving external pad timing and peripheral compatibility outside this proof.
C O V E R A G E S T A T E M E N T
Property | Status
256 bytes x four listed pairs | Directed PASS
Full mode x divider cross product | Not covered
Hardened mode 0, divider 2 | One fixed configuration
Arbitrary peripheral commands / board | Not covered
A checker must be able to fail
Completion alone is insufficient. Read the successful log and the expected fatal rejection together;
neither is a protocol-compliance certificate.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The bench instantiates mode 0 with divider 2, mode 1 with divider 3, mode 2 with divider 2 and mode 3 with divider 3. Each checks all 256 transmitted byte values against an independently generated complementary receive byte. The mode and divider are correlated; this is not a four-mode by two-divider cross product.
The real hardened wrapper fixes mode 0 and divider 2. Other modes appearing in simulation do not mean that configuration can be changed after fabrication. Likewise, general continuous multi-byte CS framing, multiple peripheral selection and held-valid misuse are not established by the directed byte tests.
A deliberately wrong receive-byte expectation causes a fatal run. Edge and CS checks accompany the data comparison. The checker distinguishes a correct byte from mere end-of-simulation, while still leaving external pad timing and peripheral compatibility outside this proof.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 14
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
14 / 24
SECTION 12 · SYNTHESIS
Synthesis: a description becomes gates
A netlist is a list of logic cells and their connections. Yosys translates the RTL into cells from
the IHP SG13G2 library.
S Y N T H E S I S
A process design kit, or PDK, contains the process-specific files used by implementation tools. This reference uses IHP SG13G2, not the SKY130 library used by the golden APB primer. Standard cells are predesigned gates and storage elements with characterised timing and physical views.
The source is compiled and checked under the unit workspace before synthesis. Yosys maps the functional logic into the pinned IHP SG13G2 standard-cell library. The current netlist contains 131 functional cells, excluding $scopeinfo metadata. The structural checker rejects remaining generic logic, latches or unresolved instances.
The mapped count excludes $scopeinfo metadata. It is not the count of every placed instance after clock buffers, repair cells and fillers are added. It also does not mean that the original protocol has been independently proven for all possible transactions.
M A P P I N G R E S U L T
MEASURE | CURRENT RESULT
Top module | spi_core
Mapped functional cells | 131
Technology | IHP SG13G2
Unresolved generic logic / latches | Rejected by structural checker
S O U R C E / C O M M A N D S
make synth node verify_build.mjs synth
04_synthesis/synth.tcl; verify_build.mjs synthesis checks
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
A process design kit, or PDK, contains the process-specific files used by implementation tools. This reference uses IHP SG13G2, not the SKY130 library used by the golden APB primer. Standard cells are predesigned gates and storage elements with characterised timing and physical views.
The source is compiled and checked under the unit workspace before synthesis. Yosys maps the functional logic into the pinned IHP SG13G2 standard-cell library. The current netlist contains 131 functional cells, excluding $scopeinfo metadata. The structural checker rejects remaining generic logic, latches or unresolved instances.
The mapped count excludes $scopeinfo metadata. It is not the count of every placed instance after clock buffers, repair cells and fillers are added. It also does not mean that the original protocol has been independently proven for all possible transactions.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 15
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
15 / 24
SECTION 13 · PHYSICAL IMPLEMENTATION
Floorplan and placement
The floorplan gives the circuit a physical outline. Placement chooses where its cells sit inside
that outline.
P H Y S I C A L I M P L E M E N T A T I O N
The die outline for this standalone block is 300 x 300 um. The floorplan establishes rows and reference power/pin geometry. The placer must fit cells legally without overlaps and with room for routing. This is a block-level educational layout, not a complete padframe or package design.
Mapped functional logic has 131 cells. After physical additions and fillers, the routed DEF contains
17,622 placed standard-cell instances. A filler occupies empty row sites; it is not another functional
logic gate. That distinction explains why the two counts differ so much.
Utilisation is the fraction of core area occupied by placed cell area. It is not simply functional-cell
count divided by die size, and it changes between stages. This note does not substitute APB
utilisation, row count or I/O count for unavailable protocol-specific measurements.
A C T U A L P H Y S I C A L R E F E R E N C E
MEASURE | VALUE
Die outline | 300 x 300 um
Mapped functional cells | 131
Placed standard-cell instances | 17,622
Physical inputs | 06_floorplanning; 07_placement
Placement agreement | DEF compared with decoded GDS
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The die outline for this standalone block is 300 x 300 um. The floorplan establishes rows and reference power/pin geometry. The placer must fit cells legally without overlaps and with room for routing. This is a block-level educational layout, not a complete padframe or package design.
Mapped functional logic has 131 cells. After physical additions and fillers, the routed DEF contains 17,622 placed standard-cell instances. A filler occupies empty row sites; it is not another functional logic gate. That distinction explains why the two counts differ so much.
Utilisation is the fraction of core area occupied by placed cell area. It is not simply functional-cell count divided by die size, and it changes between stages. This note does not substitute APB utilisation, row count or I/O count for unavailable protocol-specific measurements.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 16
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
16 / 24
SECTION 14 · CLOCK AND WIRES
Clock tree and routing
Clock-tree synthesis distributes clocks to registers. Routing draws the metal connections
between placed cells.
C L O C K A N D W I R E S
A register samples its input at a clock edge. Clock buffers distribute that edge across the block; the difference in arrival times is called skew. The reference is constrained at 50 MHz / 20 ns.
OpenROAD completes the staged physical flow. The reference die is 300 x 300 um. DEF records routed design geometry and cell placement; SPEF captures extracted parasitics used by the timing analysis. The scripts retain stage-specific output so the result can be investigated instead of relying on a final banner.
Real interconnect has resistance and capacitance, called parasitics. Extraction writes these in SPEF for post-route timing. The retained router-rule DRC file is empty. That checks the router view of its work; it is not a full foundry-deck check of the exported polygons.
R E A D T H E P H Y S I C A L E V I D E N C E
ARTIFACT | QUESTION IT ANSWERS
09_place_and_route/route.def | Where are cells and routed connections?
09_place_and_route/route.spef | Which parasitics were extracted?
Router-rule DRC report | Any reported routing-rule violations?
08_sta/timing_report.txt | What does extracted reference timing report?
Two checks can both be called DRC
The empty router report is accepted routing evidence. Foundry DRC is a separate unperformed
obligation; one result cannot stand in for the other.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
A register samples its input at a clock edge. Clock buffers distribute that edge across the block; the difference in arrival times is called skew. The reference is constrained at 50 MHz / 20 ns.
OpenROAD completes the staged physical flow. The reference die is 300 x 300 um. DEF records routed design geometry and cell placement; SPEF captures extracted parasitics used by the timing analysis. The scripts retain stage-specific output so the result can be investigated instead of relying on a final banner.
Real interconnect has resistance and capacitance, called parasitics. Extraction writes these in SPEF for post-route timing. The retained router-rule DRC file is empty. That checks the router view of its work; it is not a full foundry-deck check of the exported polygons.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 17
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
17 / 24
SECTION 15 · REFERENCE TIMING
Two measured reference corners
Static timing analysis adds cell and wire delays without simulating input patterns. Setup asks
whether data arrives early enough; hold asks whether it stays stable long enough.
R E F E R E N C E T I M I N G
The physical clock constraint is 50 MHz / 20 ns. Post-route timing uses the extracted design rather than an ideal pre-route wire estimate. The report at each corner must be inspected for worst setup and hold slack and for VIOLATED markers. The reported values are not a timing guarantee under unstated board, voltage or temperature conditions.
Current TT setup/hold slack is +15.79 / +0.17 ns. The slow-corner values are +15.73 / +0.33 ns.
Both reports contain no VIOLATED marker. These numbers are taken directly from the local report
files at document build time; the evidence manifest retains their hashes.
I/O delays are reference budgets, not a contract with an external target, transceiver or PHY. Bus synchronisation, reset recovery/removal, all additional corners and modes, signal integrity and board timing need their own analysis. Positive slack in these two reports is therefore called reference timing closure, not foundry or system signoff.
L I V E E X T R A C T E D S L A C K , N S
Corner | Worst setup | Worst hold
TT | 15.79 | 0.17
Slow | 15.73 | 0.33
Status | PASS reference reports | No VIOLATED markers
Positive slack has a stated boundary
Slack is remaining timing margin. These values apply to the listed clocks, I/O budgets and two library
corners; they are not a board-timing or manufacturing signoff guarantee.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The physical clock constraint is 50 MHz / 20 ns. Post-route timing uses the extracted design rather than an ideal pre-route wire estimate. The report at each corner must be inspected for worst setup and hold slack and for VIOLATED markers. The reported values are not a timing guarantee under unstated board, voltage or temperature conditions.
Current TT setup/hold slack is +15.79 / +0.17 ns. The slow-corner values are +15.73 / +0.33 ns. Both reports contain no VIOLATED marker. These numbers are taken directly from the local report files at document build time; the evidence manifest retains their hashes.
I/O delays are reference budgets, not a contract with an external target, transceiver or PHY. Bus synchronisation, reset recovery/removal, all additional corners and modes, signal integrity and board timing need their own analysis. Positive slack in these two reports is therefore called reference timing closure, not foundry or system signoff.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 18
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
18 / 24
SECTION 16 · GDS STREAM-OUT
Count the right objects
GDS stores layout polygons and hierarchical cell references. Stream-out combines routed
geometry with the real standard-cell layouts from the PDK.
G D S S T R E A M - O U T
The GDS file contains 1,060,628 bytes and 41 structures. The independent decoder finds 17,622 placed standard-cell instances including fillers. That placement count is intentionally much larger than the 131 mapped functional cells: filler instances occupy unused placement sites and structures are unique hierarchy definitions.
The decoder compares exported cell identities, coordinates and orientations against the routed
DEF. A deliberately altered placement/export expectation fails, including under Python
optimisation, so acceptance is not implemented with removable assert-only checks. Raw file
SHA256 is a run-specific fingerprint because stream-out timestamps can change.
The OpenROAD router-rule DRC report is empty. It is not a foundry-deck DRC result. LVS, antenna,
scan/DFT, power integrity, padframe, tap/endcap strategy and manufacturing signoff remain
unperformed. No empty routing report is promoted into a DRC-clean tapeout claim.
L I V E E X P O R T M E A S U R E M E N T S
Quantity | Current value
Mapped functional cells | 131
GDS bytes | 1,060,628
GDS structures | 41
Placed standard-cell instances | 17,622
Die | 300 x 300 um
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The GDS file contains 1,060,628 bytes and 41 structures. The independent decoder finds 17,622 placed standard-cell instances including fillers. That placement count is intentionally much larger than the 131 mapped functional cells: filler instances occupy unused placement sites and structures are unique hierarchy definitions.
The decoder compares exported cell identities, coordinates and orientations against the routed DEF. A deliberately altered placement/export expectation fails, including under Python optimisation, so acceptance is not implemented with removable assert-only checks. Raw file SHA256 is a run-specific fingerprint because stream-out timestamps can change.
The OpenROAD router-rule DRC report is empty. It is not a foundry-deck DRC result. LVS, antenna, scan/DFT, power integrity, padframe, tap/endcap strategy and manufacturing signoff remain unperformed. No empty routing report is promoted into a DRC-clean tapeout claim.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 19
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
19 / 24
SECTION 17 · UNPERFORMED SIGNOFF
DRC and LVS: what is still missing
Design rule checking asks whether geometry follows the process rules. Layout versus
schematic asks whether the extracted layout circuit matches the intended netlist.
U N P E R F O R M E D S I G N O F F
Foundry DRC requires the applicable, qualified rule deck and an inspected report on the final polygons. Typical checks include minimum widths, spacing and enclosure. No foundry-deck DRC result has been accepted for this protocol reference. The router report is narrower evidence.
LVS requires extracting a circuit from the layout and comparing devices and connectivity with the intended circuit. A structural GDS decoder checking cell references, coordinates and orientations does not perform that extraction or connectivity comparison. No accepted LVS match is available.
Antenna, scan/DFT, power integrity, padframe, tap/endcap strategy and manufacturing release
remain unperformed. The golden APB primer reports its own separate checks; those results do not
transfer to SG13G2 or to this design.
S E P A R A T E A C C E P T E D E X P O R T F R O M M I S S I N G S I G N O F F
CHECK | THIS REFERENCE
Router-rule report | Empty; narrower routing evidence
Decoded GDS placement | PASS structural/export agreement
Foundry-deck DRC | UNPERFORMED
Extracted-layout LVS | UNPERFORMED
Manufacturing readiness | Not claimed
A GDS file is not tapeout approval
This package is suitable for studying and reproducing a block implementation. Do not hand it off as a
signoff-clean manufacturing design.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Foundry DRC requires the applicable, qualified rule deck and an inspected report on the final polygons. Typical checks include minimum widths, spacing and enclosure. No foundry-deck DRC result has been accepted for this protocol reference. The router report is narrower evidence.
LVS requires extracting a circuit from the layout and comparing devices and connectivity with the intended circuit. A structural GDS decoder checking cell references, coordinates and orientations does not perform that extraction or connectivity comparison. No accepted LVS match is available.
Antenna, scan/DFT, power integrity, padframe, tap/endcap strategy and manufacturing release remain unperformed. The golden APB primer reports its own separate checks; those results do not transfer to SG13G2 or to this design.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 20
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
20 / 24
SECTION 18 · RESULTS SUMMARY
Everything at a glance
Read each result together with the question it actually answers. The same PASS label never
implies every protocol or manufacturing obligation is closed.
R E S U L T S S U M M A R Y
The directed functional result and the physical export result are both useful, but they prove different things. The physical build uses the fixed wrapper configuration and reference constraints. Additional modes, external peripherals, arbitrary clock relationships and board operation require their own evidence.
Important protocol boundary: Only four mode/divider pairs are tested; the hardened core is mode
0, divider 2. General multi-byte CS envelopes are absent.
F U L L R E F E R E N C E F L O W
STAGE | TOOL / EVIDENCE | STATUS
Lint | Verilator; 1 retained warnings | Review
Simulation | Independent directed expectations | PASS directed
Negative controls | Deliberate fatal mismatches | PASS rejection
Synthesis | Yosys; 131 mapped cells | PASS mapping
Floorplan / placement | OpenROAD; 300 x 300 um | PASS reference
Routing / extraction | DEF and SPEF retained | PASS reference
Timing | TT and slow setup / hold | PASS reference
GDS | KLayout; 1,060,628 bytes | PASS export
Foundry DRC / LVS | No accepted report | UNPERFORMED
Full-chip / board | No accepted integration proof | UNPERFORMED
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The directed functional result and the physical export result are both useful, but they prove different things. The physical build uses the fixed wrapper configuration and reference constraints. Additional modes, external peripherals, arbitrary clock relationships and board operation require their own evidence.
Important protocol boundary: Only four mode/divider pairs are tested; the hardened core is mode 0, divider 2. General multi-byte CS envelopes are absent.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 21
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
21 / 24
SECTION 19 · RUN IT YOURSELF
Run it yourself in WSL
Use the pinned source, the unit tool lock and the external PDK revision together.
R U N I T Y O U R S E L F
The proven entry point is a WSL login Bash shell. igny init prepares the packaging runtime.
Unsetting CRUCIBLE_ENV after initialisation allows the unit crucible.toml workspace selection to
control tool resolution rather than an inherited environment override. This is the observed
workflow, not a change to Crucible internals.
Each unit has its existing environment and lock. The common tool set includes Icarus, Verilator,
Yosys, OpenROAD and klayout-stream. The separate PDK checkout is IHP SG13G2 revision
22f43352dd8219f9007eb659e422e0d5fe28c5fb. A tool lock does not pin that external PDK by
itself; IHP_PDK_ROOT must point to the matching installation.
The documented machine could not use the pip klayout package as the expected stream-out
executable; igny tool install klayout-stream supplies the proven converter. make lint sim checks
functional behaviour, make flow executes the staged implementation, and node verify_build.mjs
all inspects artifacts. Review normal and intentionally failing logs before accepting the result.
Re-running a simulation can replace its VCD and invalidate an earlier document trace hash. Retain
a document evidence manifest or regenerate the measured figures after the positive run. Do not
silently preserve an old chart while claiming it is the newly generated waveform.
S O U R C E / C O M M A N D S
igny init unset CRUCIBLE_ENV cd hw/protocols/spi igny workspace sync igny tool install klayout-stream make lint sim make flow node verify_build.mjs all
Run after entering the repository in WSL login Bash; PDK required.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The proven entry point is a WSL login Bash shell. igny init prepares the packaging runtime. Unsetting CRUCIBLE_ENV after initialisation allows the unit crucible.toml workspace selection to control tool resolution rather than an inherited environment override. This is the observed workflow, not a change to Crucible internals.
Each unit has its existing environment and lock. The common tool set includes Icarus, Verilator, Yosys, OpenROAD and klayout-stream. The separate PDK checkout is IHP SG13G2 revision 22f43352dd8219f9007eb659e422e0d5fe28c5fb. A tool lock does not pin that external PDK by itself; IHP_PDK_ROOT must point to the matching installation.
The documented machine could not use the pip klayout package as the expected stream-out executable; igny tool install klayout-stream supplies the proven converter. make lint sim checks functional behaviour, make flow executes the staged implementation, and node verify_build.mjs all inspects artifacts. Review normal and intentionally failing logs before accepting the result.
Re-running a simulation can replace its VCD and invalidate an earlier document trace hash. Retain a document evidence manifest or regenerate the measured figures after the positive run. Do not silently preserve an old chart while claiming it is the newly generated waveform.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 22
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
22 / 24
SECTION 20 · SOURCES AND REMAINING WORK
Sources, ownership and remaining work
The pinned revision identifies the baseline; local integration changes are described separately.
S O U R C E S A N D R E M A I N I N G W O R K
Upstream: https://github.com/nandland/spi-master Pinned commit: 1ab581969f8ea2f794072a144b55cd74e5a54f34 Licence: MIT, russell-merrick, 2019. Original source notices remain in the RTL. The document is authored by Ignytion; this does not transfer ownership of upstream code or remove its licence obligations.
Local modifications, directed test stimulus and source boundaries are recorded in hw/protocols/spi/README.md and the repository append-only .context.md. The first three protocol lessons have separate editable 16:9 student decks; this A4 technical note is a reading and evidence document, not a replacement for their instructor notes.
Primary reading: Microchip TB3215 for SPI edge conventions, plus the pinned Nandland
implementation.
Primary guide:
https://www.microchip.com/content/dam/mchp/documents/MCU08/ApplicationNotes/Applicatio
nNotes/TB3215-Getting-Started-with-SPI-DS90003215.pdf
Open work remains explicit: Only four mode/divider pairs are tested; the hardened core is mode 0, divider 2. General multi-byte CS envelopes are absent. Full-chip integration, manufacturing checks and board validation are not closed by the standalone reference flow. The reader can reproduce the listed evidence without assuming those larger obligations have already been completed.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Upstream: https://github.com/nandland/spi-master
Pinned commit: 1ab581969f8ea2f794072a144b55cd74e5a54f34
Licence: MIT, russell-merrick, 2019. Original source notices remain in the RTL. The document is authored by Ignytion; this does not transfer ownership of upstream code or remove its licence obligations.
Local modifications, directed test stimulus and source boundaries are recorded in hw/protocols/spi/README.md and the repository append-only .context.md. The first three protocol lessons have separate editable 16:9 student decks; this A4 technical note is a reading and evidence document, not a replacement for their instructor notes.
Primary reading: Microchip TB3215 for SPI edge conventions, plus the pinned Nandland implementation.
Primary guide: https://www.microchip.com/content/dam/mchp/documents/MCU08/ApplicationNotes/ApplicationNotes/TB3215-Getting-Started-with-SPI-DS90003215.pdf
Open work remains explicit: Only four mode/divider pairs are tested; the hardened core is mode 0, divider 2. General multi-byte CS envelopes are absent. Full-chip integration, manufacturing checks and board validation are not closed by the standalone reference flow. The reader can reproduce the listed evidence without assuming those larger obligations have already been completed.
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 23
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
23 / 24
SECTION 21 · DESIGN VOCABULARY
Glossary: design and protocol
Definitions for reading the protocol rules and the checked RTL. Physical implementation
terms follow on the next page.
D E S I G N A N D V E R I F I C A T I O N
TERM | WHAT IT MEANS
Protocol | Rules for exchanging information between devices
RTL | Registers and the logic moving values between them
Verilog | A language used to describe hardware
FSM | A circuit progressing through defined states
Lint | Static source checks; no transaction execution
Testbench | Code that supplies inputs and checks outputs
Coverage | Which defined situations were exercised
Negative control | An intentionally wrong case the checker must reject
VCD | Digital signal-change trace from a simulation
Handshake | Signals agreeing when data is accepted
CPOL | Clock idle polarity
CPHA | Leading or trailing sample-edge selection
CS_n | Active-low peripheral selection
Half-bit divider | Core cycles between serial clock transitions
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 24
Ignytion io
SPI · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
24 / 24
SECTION 22 · PHYSICAL VOCABULARY
Glossary: implementation and signoff
These definitions help distinguish a successfully exported reference layout from a
manufacturing-ready design.
P H Y S I C A L I M P L E M E N T A T I O N
TERM | WHAT IT MEANS
Synthesis | Translate RTL into a technology-cell circuit
Netlist | Cells and the connections between them
Standard cell | Predesigned logic/storage cell in a process library
PDK | Process design kit: process-specific implementation files
SG13G2 | IHP process used by these reference builds
Floorplan | Die/core outline, rows, power and pin geometry
Placement | Choose legal positions for cells
Filler | Physical row-site cell, not functional logic
CTS / skew | Clock distribution / difference in arrival times
Routing / via | Metal connections / links between metal layers
Parasitics / SPEF | Wire resistance/capacitance / extracted data format
Corner | A characterised process, voltage and temperature case
STA / slack | Static timing analysis / remaining timing margin
DEF / GDS | Placement/routing exchange / polygon hierarchy
DRC | Check geometry against applicable process rules
LVS | Compare the extracted layout circuit with its netlist
Signoff | Accepted applicable release checks; unperformed here
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/SPI_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Source area: hw/protocols/spi
https://github.com/nandland/spi-master
Pinned commit 1ab581969f8ea2f794072a144b55cd74e5a54f34
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/spi/01_rtl/LICENSE.nandland
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
MIT License
Copyright (c) 2019 russell-merrick
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all
copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY,
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE
SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.