## Slide 1
Ignytion io
Ignytion IO · ignytion.io
UART PROTOCOL SERIES · OCTOBER 2026
IGNYTION IO · TECHNICAL LAB NOTE
UART protocol:
From RTL to routed GDS
A beginner's walkthrough of a checked open-source reference build
Follow uart_core from its communication rules and Verilog source to a routed IHP SG13G2 layout. Worked calculations, measured digital traces and tool results are identified separately. This is an educational block, not a manufactured chip or a signoff-ready design.
STAGE | WHAT IT PRODUCED | RESULT
Simulation | Listed directed checks | PASS directed
Synthesis | 543 mapped functional cells | PASS mapping
Routing | Routed DEF and extracted SPEF | PASS reference
Timing | TT and slow setup / hold | PASS reference
GDS | Decoded placement agreement | PASS export
Foundry DRC / LVS | No accepted result | UNPERFORMED
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Follow uart_core from its communication rules and Verilog source to a routed IHP SG13G2 layout. Worked calculations, measured digital traces and tool results are identified separately. This is an educational block, not a manufactured chip or a signoff-ready design.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 2
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
02 / 24
CONTENTS
What is in this document
Start with the wire-level rules, then follow the same circuit through the tools. Each section has
a specific evidence boundary.
R E A D I N G M A P
SECTION | PAGE
Start here | p. 03
Chip design in ten minutes | p. 04
UART logic is not RS-232 | p. 05
Send bit zero first | p. 06
Integer prescale and sample drift | p. 07
Backpressure ends at the byte buffer | p. 08
Qualify START, then sample centres | p. 09
Framing and overrun are different faults | p. 10
Two different full-duplex bytes | p. 11
Lint: read code before running it | p. 12
Exhaustive bytes at one prescale | p. 13
Synthesis: a description becomes gates | p. 14
Floorplan and placement | p. 15
Clock tree and routing | p. 16
Two measured reference corners | p. 17
Count the right objects | p. 18
DRC and LVS: what is still missing | p. 19
Everything at a glance | p. 20
Run it yourself in WSL | p. 21
Sources, ownership and remaining work | p. 22
Design and physical glossary | p. 23–24
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 3
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
03 / 24
SECTION 1 · START HERE
Start here
A protocol is an agreement about how connected devices exchange information: which wire
carries each bit, when to sample it, and how to recognise a complete transfer.
W H A T W E B U I L T A N D W H A T I T P R O V E S
A Verilog description represents circuits, not software instructions running one after another. Registers remember values; combinational logic calculates the next values. A clock advances the registered state. The next pages first explain this protocol at its wires, then connect those rules to the actual reference RTL.
The implemented unit is uart_core in hw/protocols/uart. It is a fixed reference block, not the Jane Street programmable combined emulator or a Tiny Tapeout submission top. No new competition architecture, instruction set, pin map or authority decision is implied by these documents.
All 256 bytes are tested at prescale 4 only. The 2..7 sweep uses fixed TX 0x96 and RX 0x69. No parity or hardware flow control. Later pages give the exact stimulus and the implementation evidence rather than using a broad protocol-compliant label. A successful mapped netlist, routed DEF and decoded GDS establish concrete implementation/export results, not readiness to manufacture.
The reading path starts with chip-design vocabulary, then develops the protocol, calculations, local interface and failure cases. Separate sections explain lint, simulation, synthesis, placement, routing, timing and GDS. The last two pages define design and physical terms. No prior ASIC-flow experience is assumed.
E V I D E N C E V O C A B U L A R Y
Label | Meaning in this document
Worked example | Explicit assumptions; independently calculated
Measured trace | Positive digital regression VCD, where present
Directed PASS | Listed assertions and negative controls
Routed / decoded GDS | Physical export and structural agreement
Signoff | Not performed or claimed
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
A Verilog description represents circuits, not software instructions running one after another. Registers remember values; combinational logic calculates the next values. A clock advances the registered state. The next pages first explain this protocol at its wires, then connect those rules to the actual reference RTL.
The implemented unit is uart_core in hw/protocols/uart. It is a fixed reference block, not the Jane Street programmable combined emulator or a Tiny Tapeout submission top. No new competition architecture, instruction set, pin map or authority decision is implied by these documents.
All 256 bytes are tested at prescale 4 only. The 2..7 sweep uses fixed TX 0x96 and RX 0x69. No parity or hardware flow control. Later pages give the exact stimulus and the implementation evidence rather than using a broad protocol-compliant label. A successful mapped netlist, routed DEF and decoded GDS establish concrete implementation/export results, not readiness to manufacture.
The reading path starts with chip-design vocabulary, then develops the protocol, calculations, local interface and failure cases. Separate sections explain lint, simulation, synthesis, placement, routing, timing and GDS. The last two pages define design and physical terms. No prior ASIC-flow experience is assumed.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 4
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
04 / 24
SECTION 2 · CHIP DESIGN
Chip design in ten minutes
Each stage makes the same circuit more concrete. The folders below are the actual unit
layout, not a copied APB command list.
C H I P D E S I G N
RTL states what hardware should do. A simulator checks selected input sequences before any
silicon exists. Synthesis replaces that description with gates from a process library. Physical tools
choose positions and metal routes. Timing analysis checks the resulting delays; stream-out writes
the mask-layout geometry.
T H E P I P E L I N E , S T A G E B Y S T A G E
FOLDER | WHAT HAPPENS HERE
00_lint | Read code for risky patterns; retained warnings
01_rtl | Pinned source and the local wrapper
02_sim | Independent stimulus, comparisons and fatal controls
03_verification | Supplemental checks; not a universal UVM PASS
04_synthesis | Map functional logic to SG13G2 cells
05_dft | Manufacturing test work remains unperformed
06_floorplanning | Die outline, rows, power and pin locations
07_placement | Choose legal positions for mapped cells
09_place_and_route | Clock tree, routing and SPEF extraction
08_sta | Read post-route TT and slow timing reports
10_gds | Stream-out and independent placement decoder
11_physical_verification | Foundry DRC / LVS remain unperformed
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
RTL states what hardware should do. A simulator checks selected input sequences before any silicon exists. Synthesis replaces that description with gates from a process library. Physical tools choose positions and metal routes. Timing analysis checks the resulting delays; stream-out writes the mask-layout geometry.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 5
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
05 / 24
SECTION 3 · ELECTRICAL BOUNDARY
UART logic is not RS-232
The asynchronous framing convention does not specify the board-level voltage interface.
E L E C T R I C A L B O U N D A R Y
The local rxd and txd pins carry logic-level signals. RS-232 uses different voltage levels and
polarity and cannot safely connect directly to ordinary digital pins. Full duplex uses independent
wires in each direction. Flow-control pins such as RTS/CTS are optional system features absent
from this wrapper.
A UART is a framing and timing function, not a promise about connector voltages. Never connect
an RS-232 voltage directly to a low-voltage ASIC input. An external transceiver can convert levels
and polarity. RS-485 uses differential signalling and may require driver-enable timing for a shared
half-duplex link. Those electrical functions are not in uart_core.
UART tells us where a byte begins and ends. An application still needs to define how many bytes
make a message and what the message means.
S E P A R A T E L O G I C F R O M T R A N S P O R T
Element | Meaning
txd / rxd | Digital core-level serial signals
3.3 V / 5 V compatibility | Requires compatible pads or translation
RS-232 | Requires an appropriate level-shifting transceiver
USB-to-UART bridge | Separate USB function; not supplied by this core
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The local rxd and txd pins carry logic-level signals. RS-232 uses different voltage levels and polarity and cannot safely connect directly to ordinary digital pins. Full duplex uses independent wires in each direction. Flow-control pins such as RTS/CTS are optional system features absent from this wrapper.
A UART is a framing and timing function, not a promise about connector voltages. Never connect an RS-232 voltage directly to a low-voltage ASIC input. An external transceiver can convert levels and polarity. RS-485 uses differential signalling and may require driver-enable timing for a shared half-duplex link. Those electrical functions are not in uart_core.
UART tells us where a byte begins and ends. An application still needs to define how many bytes make a message and what the message means.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 6
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
06 / 24
SECTION 4 · FRAME RULES
Send bit zero first
The fixed wrapper format is 8N1: START, eight data bits and one high STOP.
F R A M E R U L E S
8N1 means eight data bits, no parity and one stop bit. It consumes ten bit periods per byte. There is no runtime parity setting.
Writing a number on paper usually puts the most significant bit on the left, while UART sends D0
first. The editable table shows temporal order.
For binary UART signalling, baud equals serial bit rate here. It does not equal useful payload bits per second because framing consumes two intervals per byte. The 32-byte calculation excludes idle gaps, scheduling delays and packet headers. If an application sends each value as ASCII digits, its useful measurement rate can be lower still. These are arithmetic examples for 8N1, not a measured link benchmark.
For 32 payload bytes in 8N1, the minimum is 32 x 10 = 320 wire bits. At 115200 baud this takes 320 / 115200 = 2.778 ms before gaps. The useful byte ceiling is 115200 / 10 = 11,520 bytes/s, even though the serial bit rate is 115200 bit/s.
W O R K E D B Y T E 0 X 5 3
Field | Serial value
START | 0
b0..b7 | 1 1 0 0 1 0 1 0
STOP | 1
115200 baud useful byte ceiling | 11,520 bytes/s before gaps
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
8N1 means eight data bits, no parity and one stop bit. It consumes ten bit periods per byte. There is no runtime parity setting.
Writing a number on paper usually puts the most significant bit on the left, while UART sends D0 first. The editable table shows temporal order.
For binary UART signalling, baud equals serial bit rate here. It does not equal useful payload bits per second because framing consumes two intervals per byte. The 32-byte calculation excludes idle gaps, scheduling delays and packet headers. If an application sends each value as ASCII digits, its useful measurement rate can be lower still. These are arithmetic examples for 8N1, not a measured link benchmark.
For 32 payload bytes in 8N1, the minimum is 32 x 10 = 320 wire bits. At 115200 baud this takes 320 / 115200 = 2.778 ms before gaps. The useful byte ceiling is 115200 / 10 = 11,520 bytes/s, even though the serial bit rate is 115200 bit/s.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 7
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
07 / 24
SECTION 5 · TIMING CALCULATION
Integer prescale and sample drift
The prescaler controls eight core-clock groups per data-bit interval.
T I M I N G C A L C U L A T I O N
Nominal baud = fclk / (8P). At 50 MHz and a desired 115200 baud, the ideal integer divisor is
50,000,000 / (8 x 115200) = 54.253. Choosing P54 gives 115740.74 baud, +0.4694 percent error;
P55 gives 113636.36 baud, -1.3573 percent. These are calculated examples. The full byte-space
test runs at P4, and the separate fixed-byte sweep covers P2 through P7.
This simplified drift example is a timing model, not a universal two-percent acceptance rule. The receiver re-synchronizes on a new START, but not on every data bit. Long runs without data transitions still need correct local timing. The ideal half-bit margin is reduced by start detection, synchronisation, clock error and line distortion. Check a specific receiver data sheet or implementation before declaring an allowed total clock mismatch.
An ideal receiver checks START near its half-bit point, then samples data at 1.5, 2.5 through 8.5 bit intervals from the detected start and STOP at 9.5. At the P4 regression setting a bit is 0.64 us; nominal data-centre offsets are therefore 0.96, 1.60 through 5.44 us. The actual local RX counter waits half a bit to confirm START, then full-bit intervals for later samples. Its input synchroniser and detection delay must also be accounted for.
C A L C U L A T E D 5 0 M H Z E X A M P L E S
Prescale | Baud | Error vs 115200
54 | 115740.74 | +0.4694%
55 | 113636.36 | -1.3573%
4, actual regression | 1,562,500 | Not a 115200-baud test
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Nominal baud = fclk / (8P). At 50 MHz and a desired 115200 baud, the ideal integer divisor is 50,000,000 / (8 x 115200) = 54.253. Choosing P54 gives 115740.74 baud, +0.4694 percent error; P55 gives 113636.36 baud, -1.3573 percent. These are calculated examples. The full byte-space test runs at P4, and the separate fixed-byte sweep covers P2 through P7.
This simplified drift example is a timing model, not a universal two-percent acceptance rule. The receiver re-synchronizes on a new START, but not on every data bit. Long runs without data transitions still need correct local timing. The ideal half-bit margin is reduced by start detection, synchronisation, clock error and line distortion. Check a specific receiver data sheet or implementation before declaring an allowed total clock mismatch.
An ideal receiver checks START near its half-bit point, then samples data at 1.5, 2.5 through 8.5 bit intervals from the detected start and STOP at 9.5. At the P4 regression setting a bit is 0.64 us; nominal data-centre offsets are therefore 0.96, 1.60 through 5.44 us. The actual local RX counter waits half a bit to confirm START, then full-bit intervals for later samples. Its input synchroniser and detection delay must also be accounted for.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 8
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
08 / 24
SECTION 6 · RTL INTERFACE
Backpressure ends at the byte buffer
Ready-valid can stop a local producer. It cannot pause bits already arriving on rxd.
R T L I N T E R F A C E
Ready-valid allows a producer to hold a request until accepted. The selected transmitter does not
provide an unbounded queue. Inspect upstream RTL to understand when it can accept another
byte.
The source has a one-byte output register rather than an arbitrarily deep FIFO. Backpressure protects a byte only until another frame completes. A larger FIFO or external flow control would be another design. The current test exercises a limited ready stall and an isolated overrun; it does not promise lossless indefinite stalls.
The two-stage chain reduces propagation of metastability into the logic, but it cannot mathematically guarantee no failures. Its delay affects the start detection and must be considered with the baud interval. The marker guides implementation tools; it does not itself prove CDC correctness. The physical flow still needs proper placement and system integration checks before a reliability claim. A separate counter stage in upstream uart_rx samples this synchronised signal.
S O U R C E / C O M M A N D S
(* async_reg = "true" *) reg [1:0] rx_sync; always @(posedge clk) if (rst) rx_sync <= 2'b11; else rx_sync <= {rx_sync[0],rxd}; uart controller (
hw/protocols/uart/01_rtl/uart_core.v:24
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Ready-valid allows a producer to hold a request until accepted. The selected transmitter does not provide an unbounded queue. Inspect upstream RTL to understand when it can accept another byte.
The source has a one-byte output register rather than an arbitrarily deep FIFO. Backpressure protects a byte only until another frame completes. A larger FIFO or external flow control would be another design. The current test exercises a limited ready stall and an isolated overrun; it does not promise lossless indefinite stalls.
The two-stage chain reduces propagation of metastability into the logic, but it cannot mathematically guarantee no failures. Its delay affects the start detection and must be considered with the baud interval. The marker guides implementation tools; it does not itself prove CDC correctness. The physical flow still needs proper placement and system integration checks before a reliability claim. A separate counter stage in upstream uart_rx samples this synchronised signal.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 9
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
09 / 24
SECTION 7 · CONTROL SEQUENCE
Qualify START, then sample centres
The receiver rejects short starts before committing to a full frame.
C O N T R O L S E Q U E N C E
When the initial candidate START does not remain low until the confirmation point, the receiver clears its bit counter and timer. If the line is still low, it advances to the data phase and loads a full-bit wait. This is a specific digital false-start check, not proof of immunity to every glitch width or analogue noise pattern.
The table corresponds to the counter-based uart_rx.v control sequence. A pending timer prevents a new sample until the proper interval expires. At count ten the receiver confirms START; at nine through two it shifts in the eight data bits; at one it evaluates STOP. It returns to zero after the frame. START detection initialises a half-bit delay and later data stages initialize full-bit delays. Output buffering and error flags are separate from this serial phase counter.
The data register includes a high bit for the STOP phase alongside the payload. txd becomes low for START while busy becomes high. Later timer expirations shift data bits into the output. No parity generation or alternative word length is enabled by this wrapper.
S O U R C E - D E R I V E D R E C E I V E S E Q U E N C E
bit_cnt | Phase | Action when timer expires
0 | Idle | Observe low candidate START
10 | Confirm START | Continue only if line stays low
9 through 2 | Data b0 through b7 | Shift sampled RX into data register
1 | STOP | Accept data or flag framing error
0 again | Finish | Return to idle detection
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
When the initial candidate START does not remain low until the confirmation point, the receiver clears its bit counter and timer. If the line is still low, it advances to the data phase and loads a full-bit wait. This is a specific digital false-start check, not proof of immunity to every glitch width or analogue noise pattern.
The table corresponds to the counter-based uart_rx.v control sequence. A pending timer prevents a new sample until the proper interval expires. At count ten the receiver confirms START; at nine through two it shifts in the eight data bits; at one it evaluates STOP. It returns to zero after the frame. START detection initialises a half-bit delay and later data stages initialize full-bit delays. Output buffering and error flags are separate from this serial phase counter.
The data register includes a high bit for the STOP phase alongside the payload. txd becomes low for START while busy becomes high. Later timer expirations shift data bits into the output. No parity generation or alternative word length is enabled by this wrapper.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 10
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
10 / 24
SECTION 8 · FAILURE ANALYSIS
Framing and overrun are different faults
A low STOP is a wire-framing failure; a full output buffer is a consumer-capacity failure.
F A I L U R E A N A L Y S I S
A framing error checks the expected STOP level; it is not a checksum across the data. A wrong data bit with a valid STOP may go undetected by an 8N1 receiver. Sustained low after malformed STOP can resemble another START in this core, producing later recovery activity. The test drains that recovery before isolating the overrun check.
This source branch belongs to the STOP-sampling stage. A valid STOP writes the newly assembled data register and marks it available. The prior valid state becomes the overrun flag. This means the error reports loss/overwrite risk; it does not automatically queue another byte.
Synchronous reset requires a running clock to take effect. Reset polarity differs from the default I2C and SPI wrappers. Declaration initializers in upstream code are visible lint warnings. The actual reset path and mapped flops still require inspection.
F A U L T A N D C O N S E Q U E N C E
Condition | Expected interpretation
STOP sampled low | frame_error
Completed byte with pending output | overrun / data-loss risk
Long low recovery stimulus | May resemble a new START
Data changed with valid STOP | May require application checksum to detect
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
A framing error checks the expected STOP level; it is not a checksum across the data. A wrong data bit with a valid STOP may go undetected by an 8N1 receiver. Sustained low after malformed STOP can resemble another START in this core, producing later recovery activity. The test drains that recovery before isolating the overrun check.
This source branch belongs to the STOP-sampling stage. A valid STOP writes the newly assembled data register and marks it available. The prior valid state becomes the overrun flag. This means the error reports loss/overwrite risk; it does not automatically queue another byte.
Synchronous reset requires a running clock to take effect. Reset polarity differs from the default I2C and SPI wrappers. Declaration initializers in upstream code are visible lint warnings. The actual reset path and mapped flops still require inspection.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 11
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
11 / 24
SECTION 9 · MEASURED TRACE
Two different full-duplex bytes
The waveform contains TX 0x53 and independently driven RX 0xAC.
M E A S U R E D T R A C E
At the actual 50 MHz simulation clock, prescale 4 produces 32 core clocks per bit, or 0.64 us. An 8N1 frame occupies ten bit intervals and therefore 6.4 us, before any idle gaps. Sampling TX at the eight data centres reconstructs 53; sampling the separately aligned RX centres reconstructs AC. Both STOP samples are high.
The received byte is the complement of the transmitted byte, so the plot demonstrates
independent stimulus rather than TX-to-RX loopback. This is a fast directed digital regression at
1.5625 Mbaud, not a measured 115200-baud board capture. The illustrative prescale-54
configuration elsewhere is a calculation, not one of the tested sweep points.
M E A S U R E D P O S I T I V E R E G R E S S I O N
Chart: TX
| 0 | 0.32 | 0.32 | 0.96 | 0.96 | 2.24 | 2.24 | 3.52 | 3.52 | 4.16 | 4.16 | 4.8 | 4.8 | 5.44 | 5.44 | 6.08 | 6.08 | 7.04
TX | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
Chart: RX
| 0 | 0.31 | 0.31 | 2.23 | 2.23 | 3.51 | 3.51 | 4.15 | 4.15 | 4.79 | 4.79 | 5.43 | 5.43 | 7.04
RX | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
Logic HIGH=1, LOW=0. Digital simulation, not analogue compliance; source hash retained.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
At the actual 50 MHz simulation clock, prescale 4 produces 32 core clocks per bit, or 0.64 us. An 8N1 frame occupies ten bit intervals and therefore 6.4 us, before any idle gaps. Sampling TX at the eight data centres reconstructs 53; sampling the separately aligned RX centres reconstructs AC. Both STOP samples are high.
The received byte is the complement of the transmitted byte, so the plot demonstrates independent stimulus rather than TX-to-RX loopback. This is a fast directed digital regression at 1.5625 Mbaud, not a measured 115200-baud board capture. The illustrative prescale-54 configuration elsewhere is a calculation, not one of the tested sweep points.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
TX data 0x53 and independent RX data 0xAC, LSB first, STOP high. Prescale 4, bit time 0.64 us.
Source VCD hw/protocols/uart/02_sim/uart_core.vcd
SHA256 adbfeb21e2f40fc1017325b344bd8b465fc06fbea7b51137b15223519d00fcec
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 12
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
12 / 24
SECTION 10 · LINT
Lint: read code before running it
Verilator checks legal but suspicious code patterns without exercising transactions. A warning
count is a review starting point, not proof of correctness.
L I N T
The retained report contains 20 warning messages and 0 error messages. Categories present:
PROCASSINIT, WIDTHEXPAND. These figures count report message headers; repeated warnings
are not necessarily independent defects. The report is hashed in this document evidence manifest.
The invocation deliberately uses -Wno-fatal so warnings remain visible while lint execution can complete. A successful command therefore does not mean every warning was resolved. Width changes, incomplete cases, reset use and unconnected ports need review against the wrapper contract and directed tests.
Lint cannot show that a receive byte is correct, that a transaction finishes, or that an external
electrical interface is safe. Those questions require a checking testbench, implementation evidence
and separate board or signoff work.
R E T A I N E D W A R N I N G R E V I E W
MEASURE | VALUE
Warning message headers | 20
Error message headers | 0
Clean warning-free RTL? | Not claimed
Protocol behaviour proved by lint? | No
S O U R C E / C O M M A N D S
make lint # inspect, do not just count # 00_lint/lint_report.txt
00_lint/Makefile and run_flow.sh: retained Verilator report
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The retained report contains 20 warning messages and 0 error messages. Categories present: PROCASSINIT, WIDTHEXPAND. These figures count report message headers; repeated warnings are not necessarily independent defects. The report is hashed in this document evidence manifest.
The invocation deliberately uses -Wno-fatal so warnings remain visible while lint execution can complete. A successful command therefore does not mean every warning was resolved. Width changes, incomplete cases, reset use and unconnected ports need review against the wrapper contract and directed tests.
Lint cannot show that a receive byte is correct, that a transaction finishes, or that an external electrical interface is safe. Those questions require a checking testbench, implementation evidence and separate board or signoff work.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 13
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
13 / 24
SECTION 11 · SIMULATION AND VERIFICATION
Exhaustive bytes at one prescale
A testbench is code that drives the circuit and judges its outputs. These directed checks use
independent expected data and deliberately failing controls.
S I M U L A T I O N A N D V E R I F I C A T I O N
The full-duplex run tests all 256 byte values at prescale 4. A separate sweep uses prescales 2
through 7 with fixed TX 96 and RX 69. Combining those descriptions into all bytes at all prescalers
would overstate the evidence. Neither test establishes arbitrary baud mismatch tolerance.
Directed checks include receive backpressure, malformed STOP and framing error, receive-buffer overrun, reset abort and a successful later transfer. The malformed-STOP source can remain low long enough to resemble another START. The bench drains the resulting recovery word before isolating the subsequent overrun check.
An injected wrong receive-byte expectation must fail fatally. The wrapper remains fixed to 8N1 with no parity, CTS/RTS or alternative word length. The two-stage receive synchroniser reduces metastability propagation, but these digital tests are not a CDC reliability or reset signoff result.
C O V E R A G E M A T R I X
Case | Actual stimulus
Full byte space | 256 values at prescale 4
Divider sweep | 2..7; TX 96 / RX 69
Consumer faults | Stall, overrun, malformed STOP
Not tested | Parity, other word formats, arbitrary drift
A checker must be able to fail
Completion alone is insufficient. Read the successful log and the expected fatal rejection together;
neither is a protocol-compliance certificate.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The full-duplex run tests all 256 byte values at prescale 4. A separate sweep uses prescales 2 through 7 with fixed TX 96 and RX 69. Combining those descriptions into all bytes at all prescalers would overstate the evidence. Neither test establishes arbitrary baud mismatch tolerance.
Directed checks include receive backpressure, malformed STOP and framing error, receive-buffer overrun, reset abort and a successful later transfer. The malformed-STOP source can remain low long enough to resemble another START. The bench drains the resulting recovery word before isolating the subsequent overrun check.
An injected wrong receive-byte expectation must fail fatally. The wrapper remains fixed to 8N1 with no parity, CTS/RTS or alternative word length. The two-stage receive synchroniser reduces metastability propagation, but these digital tests are not a CDC reliability or reset signoff result.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 14
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
14 / 24
SECTION 12 · SYNTHESIS
Synthesis: a description becomes gates
A netlist is a list of logic cells and their connections. Yosys translates the RTL into cells from
the IHP SG13G2 library.
S Y N T H E S I S
A process design kit, or PDK, contains the process-specific files used by implementation tools. This reference uses IHP SG13G2, not the SKY130 library used by the golden APB primer. Standard cells are predesigned gates and storage elements with characterised timing and physical views.
The source is compiled and checked under the unit workspace before synthesis. Yosys maps the functional logic into the pinned IHP SG13G2 standard-cell library. The current netlist contains 543 functional cells, excluding $scopeinfo metadata. The structural checker rejects remaining generic logic, latches or unresolved instances.
The mapped count excludes $scopeinfo metadata. It is not the count of every placed instance after clock buffers, repair cells and fillers are added. It also does not mean that the original protocol has been independently proven for all possible transactions.
M A P P I N G R E S U L T
MEASURE | CURRENT RESULT
Top module | uart_core
Mapped functional cells | 543
Technology | IHP SG13G2
Unresolved generic logic / latches | Rejected by structural checker
S O U R C E / C O M M A N D S
make synth node verify_build.mjs synth
04_synthesis/synth.tcl; verify_build.mjs synthesis checks
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
A process design kit, or PDK, contains the process-specific files used by implementation tools. This reference uses IHP SG13G2, not the SKY130 library used by the golden APB primer. Standard cells are predesigned gates and storage elements with characterised timing and physical views.
The source is compiled and checked under the unit workspace before synthesis. Yosys maps the functional logic into the pinned IHP SG13G2 standard-cell library. The current netlist contains 543 functional cells, excluding $scopeinfo metadata. The structural checker rejects remaining generic logic, latches or unresolved instances.
The mapped count excludes $scopeinfo metadata. It is not the count of every placed instance after clock buffers, repair cells and fillers are added. It also does not mean that the original protocol has been independently proven for all possible transactions.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 15
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
15 / 24
SECTION 13 · PHYSICAL IMPLEMENTATION
Floorplan and placement
The floorplan gives the circuit a physical outline. Placement chooses where its cells sit inside
that outline.
P H Y S I C A L I M P L E M E N T A T I O N
The die outline for this standalone block is 300 x 300 um. The floorplan establishes rows and reference power/pin geometry. The placer must fit cells legally without overlaps and with room for routing. This is a block-level educational layout, not a complete padframe or package design.
Mapped functional logic has 543 cells. After physical additions and fillers, the routed DEF contains
16,512 placed standard-cell instances. A filler occupies empty row sites; it is not another functional
logic gate. That distinction explains why the two counts differ so much.
Utilisation is the fraction of core area occupied by placed cell area. It is not simply functional-cell
count divided by die size, and it changes between stages. This note does not substitute APB
utilisation, row count or I/O count for unavailable protocol-specific measurements.
A C T U A L P H Y S I C A L R E F E R E N C E
MEASURE | VALUE
Die outline | 300 x 300 um
Mapped functional cells | 543
Placed standard-cell instances | 16,512
Physical inputs | 06_floorplanning; 07_placement
Placement agreement | DEF compared with decoded GDS
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The die outline for this standalone block is 300 x 300 um. The floorplan establishes rows and reference power/pin geometry. The placer must fit cells legally without overlaps and with room for routing. This is a block-level educational layout, not a complete padframe or package design.
Mapped functional logic has 543 cells. After physical additions and fillers, the routed DEF contains 16,512 placed standard-cell instances. A filler occupies empty row sites; it is not another functional logic gate. That distinction explains why the two counts differ so much.
Utilisation is the fraction of core area occupied by placed cell area. It is not simply functional-cell count divided by die size, and it changes between stages. This note does not substitute APB utilisation, row count or I/O count for unavailable protocol-specific measurements.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 16
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
16 / 24
SECTION 14 · CLOCK AND WIRES
Clock tree and routing
Clock-tree synthesis distributes clocks to registers. Routing draws the metal connections
between placed cells.
C L O C K A N D W I R E S
A register samples its input at a clock edge. Clock buffers distribute that edge across the block; the difference in arrival times is called skew. The reference is constrained at 50 MHz / 20 ns.
OpenROAD completes the staged physical flow. The reference die is 300 x 300 um. DEF records routed design geometry and cell placement; SPEF captures extracted parasitics used by the timing analysis. The scripts retain stage-specific output so the result can be investigated instead of relying on a final banner.
Real interconnect has resistance and capacitance, called parasitics. Extraction writes these in SPEF for post-route timing. The retained router-rule DRC file is empty. That checks the router view of its work; it is not a full foundry-deck check of the exported polygons.
R E A D T H E P H Y S I C A L E V I D E N C E
ARTIFACT | QUESTION IT ANSWERS
09_place_and_route/route.def | Where are cells and routed connections?
09_place_and_route/route.spef | Which parasitics were extracted?
Router-rule DRC report | Any reported routing-rule violations?
08_sta/timing_report.txt | What does extracted reference timing report?
Two checks can both be called DRC
The empty router report is accepted routing evidence. Foundry DRC is a separate unperformed
obligation; one result cannot stand in for the other.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
A register samples its input at a clock edge. Clock buffers distribute that edge across the block; the difference in arrival times is called skew. The reference is constrained at 50 MHz / 20 ns.
OpenROAD completes the staged physical flow. The reference die is 300 x 300 um. DEF records routed design geometry and cell placement; SPEF captures extracted parasitics used by the timing analysis. The scripts retain stage-specific output so the result can be investigated instead of relying on a final banner.
Real interconnect has resistance and capacitance, called parasitics. Extraction writes these in SPEF for post-route timing. The retained router-rule DRC file is empty. That checks the router view of its work; it is not a full foundry-deck check of the exported polygons.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 17
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
17 / 24
SECTION 15 · REFERENCE TIMING
Two measured reference corners
Static timing analysis adds cell and wire delays without simulating input patterns. Setup asks
whether data arrives early enough; hold asks whether it stays stable long enough.
R E F E R E N C E T I M I N G
The physical clock constraint is 50 MHz / 20 ns. Post-route timing uses the extracted design rather than an ideal pre-route wire estimate. The report at each corner must be inspected for worst setup and hold slack and for VIOLATED markers. The reported values are not a timing guarantee under unstated board, voltage or temperature conditions.
Current TT setup/hold slack is +15.75 / +0.17 ns. The slow-corner values are +14.45 / +0.24 ns.
Both reports contain no VIOLATED marker. These numbers are taken directly from the local report
files at document build time; the evidence manifest retains their hashes.
I/O delays are reference budgets, not a contract with an external target, transceiver or PHY. Bus synchronisation, reset recovery/removal, all additional corners and modes, signal integrity and board timing need their own analysis. Positive slack in these two reports is therefore called reference timing closure, not foundry or system signoff.
L I V E E X T R A C T E D S L A C K , N S
Corner | Worst setup | Worst hold
TT | 15.75 | 0.17
Slow | 14.45 | 0.24
Status | PASS reference reports | No VIOLATED markers
Positive slack has a stated boundary
Slack is remaining timing margin. These values apply to the listed clocks, I/O budgets and two library
corners; they are not a board-timing or manufacturing signoff guarantee.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The physical clock constraint is 50 MHz / 20 ns. Post-route timing uses the extracted design rather than an ideal pre-route wire estimate. The report at each corner must be inspected for worst setup and hold slack and for VIOLATED markers. The reported values are not a timing guarantee under unstated board, voltage or temperature conditions.
Current TT setup/hold slack is +15.75 / +0.17 ns. The slow-corner values are +14.45 / +0.24 ns. Both reports contain no VIOLATED marker. These numbers are taken directly from the local report files at document build time; the evidence manifest retains their hashes.
I/O delays are reference budgets, not a contract with an external target, transceiver or PHY. Bus synchronisation, reset recovery/removal, all additional corners and modes, signal integrity and board timing need their own analysis. Positive slack in these two reports is therefore called reference timing closure, not foundry or system signoff.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 18
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
18 / 24
SECTION 16 · GDS STREAM-OUT
Count the right objects
GDS stores layout polygons and hierarchical cell references. Stream-out combines routed
geometry with the real standard-cell layouts from the PDK.
G D S S T R E A M - O U T
The GDS file contains 1,284,780 bytes and 45 structures. The independent decoder finds 16,512 placed standard-cell instances including fillers. That placement count is intentionally much larger than the 543 mapped functional cells: filler instances occupy unused placement sites and structures are unique hierarchy definitions.
The decoder compares exported cell identities, coordinates and orientations against the routed
DEF. A deliberately altered placement/export expectation fails, including under Python
optimisation, so acceptance is not implemented with removable assert-only checks. Raw file
SHA256 is a run-specific fingerprint because stream-out timestamps can change.
The OpenROAD router-rule DRC report is empty. It is not a foundry-deck DRC result. LVS, antenna,
scan/DFT, power integrity, padframe, tap/endcap strategy and manufacturing signoff remain
unperformed. No empty routing report is promoted into a DRC-clean tapeout claim.
L I V E E X P O R T M E A S U R E M E N T S
Quantity | Current value
Mapped functional cells | 543
GDS bytes | 1,284,780
GDS structures | 45
Placed standard-cell instances | 16,512
Die | 300 x 300 um
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The GDS file contains 1,284,780 bytes and 45 structures. The independent decoder finds 16,512 placed standard-cell instances including fillers. That placement count is intentionally much larger than the 543 mapped functional cells: filler instances occupy unused placement sites and structures are unique hierarchy definitions.
The decoder compares exported cell identities, coordinates and orientations against the routed DEF. A deliberately altered placement/export expectation fails, including under Python optimisation, so acceptance is not implemented with removable assert-only checks. Raw file SHA256 is a run-specific fingerprint because stream-out timestamps can change.
The OpenROAD router-rule DRC report is empty. It is not a foundry-deck DRC result. LVS, antenna, scan/DFT, power integrity, padframe, tap/endcap strategy and manufacturing signoff remain unperformed. No empty routing report is promoted into a DRC-clean tapeout claim.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 19
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
19 / 24
SECTION 17 · UNPERFORMED SIGNOFF
DRC and LVS: what is still missing
Design rule checking asks whether geometry follows the process rules. Layout versus
schematic asks whether the extracted layout circuit matches the intended netlist.
U N P E R F O R M E D S I G N O F F
Foundry DRC requires the applicable, qualified rule deck and an inspected report on the final polygons. Typical checks include minimum widths, spacing and enclosure. No foundry-deck DRC result has been accepted for this protocol reference. The router report is narrower evidence.
LVS requires extracting a circuit from the layout and comparing devices and connectivity with the intended circuit. A structural GDS decoder checking cell references, coordinates and orientations does not perform that extraction or connectivity comparison. No accepted LVS match is available.
Antenna, scan/DFT, power integrity, padframe, tap/endcap strategy and manufacturing release
remain unperformed. The golden APB primer reports its own separate checks; those results do not
transfer to SG13G2 or to this design.
S E P A R A T E A C C E P T E D E X P O R T F R O M M I S S I N G S I G N O F F
CHECK | THIS REFERENCE
Router-rule report | Empty; narrower routing evidence
Decoded GDS placement | PASS structural/export agreement
Foundry-deck DRC | UNPERFORMED
Extracted-layout LVS | UNPERFORMED
Manufacturing readiness | Not claimed
A GDS file is not tapeout approval
This package is suitable for studying and reproducing a block implementation. Do not hand it off as a
signoff-clean manufacturing design.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Foundry DRC requires the applicable, qualified rule deck and an inspected report on the final polygons. Typical checks include minimum widths, spacing and enclosure. No foundry-deck DRC result has been accepted for this protocol reference. The router report is narrower evidence.
LVS requires extracting a circuit from the layout and comparing devices and connectivity with the intended circuit. A structural GDS decoder checking cell references, coordinates and orientations does not perform that extraction or connectivity comparison. No accepted LVS match is available.
Antenna, scan/DFT, power integrity, padframe, tap/endcap strategy and manufacturing release remain unperformed. The golden APB primer reports its own separate checks; those results do not transfer to SG13G2 or to this design.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 20
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
20 / 24
SECTION 18 · RESULTS SUMMARY
Everything at a glance
Read each result together with the question it actually answers. The same PASS label never
implies every protocol or manufacturing obligation is closed.
R E S U L T S S U M M A R Y
The directed functional result and the physical export result are both useful, but they prove different things. The physical build uses the fixed wrapper configuration and reference constraints. Additional modes, external peripherals, arbitrary clock relationships and board operation require their own evidence.
Important protocol boundary: All 256 bytes are tested at prescale 4 only. The 2..7 sweep uses fixed
TX 0x96 and RX 0x69. No parity or hardware flow control.
F U L L R E F E R E N C E F L O W
STAGE | TOOL / EVIDENCE | STATUS
Lint | Verilator; 20 retained warnings | Review
Simulation | Independent directed expectations | PASS directed
Negative controls | Deliberate fatal mismatches | PASS rejection
Synthesis | Yosys; 543 mapped cells | PASS mapping
Floorplan / placement | OpenROAD; 300 x 300 um | PASS reference
Routing / extraction | DEF and SPEF retained | PASS reference
Timing | TT and slow setup / hold | PASS reference
GDS | KLayout; 1,284,780 bytes | PASS export
Foundry DRC / LVS | No accepted report | UNPERFORMED
Full-chip / board | No accepted integration proof | UNPERFORMED
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The directed functional result and the physical export result are both useful, but they prove different things. The physical build uses the fixed wrapper configuration and reference constraints. Additional modes, external peripherals, arbitrary clock relationships and board operation require their own evidence.
Important protocol boundary: All 256 bytes are tested at prescale 4 only. The 2..7 sweep uses fixed TX 0x96 and RX 0x69. No parity or hardware flow control.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 21
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
21 / 24
SECTION 19 · RUN IT YOURSELF
Run it yourself in WSL
Use the pinned source, the unit tool lock and the external PDK revision together.
R U N I T Y O U R S E L F
The proven entry point is a WSL login Bash shell. igny init prepares the packaging runtime.
Unsetting CRUCIBLE_ENV after initialisation allows the unit crucible.toml workspace selection to
control tool resolution rather than an inherited environment override. This is the observed
workflow, not a change to Crucible internals.
Each unit has its existing environment and lock. The common tool set includes Icarus, Verilator,
Yosys, OpenROAD and klayout-stream. The separate PDK checkout is IHP SG13G2 revision
22f43352dd8219f9007eb659e422e0d5fe28c5fb. A tool lock does not pin that external PDK by
itself; IHP_PDK_ROOT must point to the matching installation.
The documented machine could not use the pip klayout package as the expected stream-out
executable; igny tool install klayout-stream supplies the proven converter. make lint sim checks
functional behaviour, make flow executes the staged implementation, and node verify_build.mjs
all inspects artifacts. Review normal and intentionally failing logs before accepting the result.
Re-running a simulation can replace its VCD and invalidate an earlier document trace hash. Retain
a document evidence manifest or regenerate the measured figures after the positive run. Do not
silently preserve an old chart while claiming it is the newly generated waveform.
S O U R C E / C O M M A N D S
igny init unset CRUCIBLE_ENV cd hw/protocols/uart igny workspace sync igny tool install klayout-stream make lint sim make flow node verify_build.mjs all
Run after entering the repository in WSL login Bash; PDK required.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
The proven entry point is a WSL login Bash shell. igny init prepares the packaging runtime. Unsetting CRUCIBLE_ENV after initialisation allows the unit crucible.toml workspace selection to control tool resolution rather than an inherited environment override. This is the observed workflow, not a change to Crucible internals.
Each unit has its existing environment and lock. The common tool set includes Icarus, Verilator, Yosys, OpenROAD and klayout-stream. The separate PDK checkout is IHP SG13G2 revision 22f43352dd8219f9007eb659e422e0d5fe28c5fb. A tool lock does not pin that external PDK by itself; IHP_PDK_ROOT must point to the matching installation.
The documented machine could not use the pip klayout package as the expected stream-out executable; igny tool install klayout-stream supplies the proven converter. make lint sim checks functional behaviour, make flow executes the staged implementation, and node verify_build.mjs all inspects artifacts. Review normal and intentionally failing logs before accepting the result.
Re-running a simulation can replace its VCD and invalidate an earlier document trace hash. Retain a document evidence manifest or regenerate the measured figures after the positive run. Do not silently preserve an old chart while claiming it is the newly generated waveform.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 22
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
22 / 24
SECTION 20 · SOURCES AND REMAINING WORK
Sources, ownership and remaining work
The pinned revision identifies the baseline; local integration changes are described separately.
S O U R C E S A N D R E M A I N I N G W O R K
Upstream: https://github.com/alexforencich/verilog-uart Pinned commit: 1b867e53af738e4a8bc7c839ca2f1c07f40382dc Licence: MIT, Alex Forencich, 2014-2017. Original source notices remain in the RTL. The document is authored by Ignytion; this does not transfer ownership of upstream code or remove its licence obligations.
Local modifications, directed test stimulus and source boundaries are recorded in hw/protocols/uart/README.md and the repository append-only .context.md. The first three protocol lessons have separate editable 16:9 student decks; this A4 technical note is a reading and evidence document, not a replacement for their instructor notes.
Primary reading: Microchip EUSART/AUSART framing reference, plus the pinned verilog-uart counters and handshake. Primary framing reference: https://developerhelp.microchip.com/xwiki/bin/view/products/mcu-mpu/8bit-pic/peripherals/eus art-ausart/
Open work remains explicit: All 256 bytes are tested at prescale 4 only. The 2..7 sweep uses fixed TX 0x96 and RX 0x69. No parity or hardware flow control. Full-chip integration, manufacturing checks and board validation are not closed by the standalone reference flow. The reader can reproduce the listed evidence without assuming those larger obligations have already been completed.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Upstream: https://github.com/alexforencich/verilog-uart
Pinned commit: 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Licence: MIT, Alex Forencich, 2014-2017. Original source notices remain in the RTL. The document is authored by Ignytion; this does not transfer ownership of upstream code or remove its licence obligations.
Local modifications, directed test stimulus and source boundaries are recorded in hw/protocols/uart/README.md and the repository append-only .context.md. The first three protocol lessons have separate editable 16:9 student decks; this A4 technical note is a reading and evidence document, not a replacement for their instructor notes.
Primary reading: Microchip EUSART/AUSART framing reference, plus the pinned verilog-uart counters and handshake.
Primary framing reference: https://developerhelp.microchip.com/xwiki/bin/view/products/mcu-mpu/8bit-pic/peripherals/eusart-ausart/
Open work remains explicit: All 256 bytes are tested at prescale 4 only. The 2..7 sweep uses fixed TX 0x96 and RX 0x69. No parity or hardware flow control. Full-chip integration, manufacturing checks and board validation are not closed by the standalone reference flow. The reader can reproduce the listed evidence without assuming those larger obligations have already been completed.
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 23
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
23 / 24
SECTION 21 · DESIGN VOCABULARY
Glossary: design and protocol
Definitions for reading the protocol rules and the checked RTL. Physical implementation
terms follow on the next page.
D E S I G N A N D V E R I F I C A T I O N
TERM | WHAT IT MEANS
Protocol | Rules for exchanging information between devices
RTL | Registers and the logic moving values between them
Verilog | A language used to describe hardware
FSM | A circuit progressing through defined states
Lint | Static source checks; no transaction execution
Testbench | Code that supplies inputs and checks outputs
Coverage | Which defined situations were exercised
Negative control | An intentionally wrong case the checker must reject
VCD | Digital signal-change trace from a simulation
Handshake | Signals agreeing when data is accepted
8N1 | Eight data bits, no parity, one STOP bit
Prescale | Integer number of core clocks per eighth-bit interval
Frame error | STOP sample was not high
Overrun | New completed receive data met an occupied output buffer
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.

## Slide 24
Ignytion io
UART · RTL TO GDS · A BEGINNER'S WALKTHROUGH
© 2026 Ignytion IO · ignytion.io
October 2026 · Version 2.0
24 / 24
SECTION 22 · PHYSICAL VOCABULARY
Glossary: implementation and signoff
These definitions help distinguish a successfully exported reference layout from a
manufacturing-ready design.
P H Y S I C A L I M P L E M E N T A T I O N
TERM | WHAT IT MEANS
Synthesis | Translate RTL into a technology-cell circuit
Netlist | Cells and the connections between them
Standard cell | Predesigned logic/storage cell in a process library
PDK | Process design kit: process-specific implementation files
SG13G2 | IHP process used by these reference builds
Floorplan | Die/core outline, rows, power and pin geometry
Placement | Choose legal positions for cells
Filler | Physical row-site cell, not functional logic
CTS / skew | Clock distribution / difference in arrival times
Routing / via | Metal connections / links between metal layers
Parasitics / SPEF | Wire resistance/capacitance / extracted data format
Corner | A characterised process, voltage and temperature case
STA / slack | Static timing analysis / remaining timing margin
DEF / GDS | Placement/routing exchange / polygon hierarchy
DRC | Check geometry against applicable process rules
LVS | Compare the extracted layout circuit with its netlist
Signoff | Accepted applicable release checks; unperformed here
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. All rights reserved.
Author: IGNYTION_TECH
File: docs/UART_Protocol_RTL_to_GDS_Ignytion_A4.pptx
Created: 2026-10-03
Source area: hw/protocols/uart
https://github.com/alexforencich/verilog-uart
Pinned commit 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notice:
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.
Reference build only; foundry DRC/LVS and full-chip signoff unperformed.