## Slide 1
I2C STUDENT LAB
Ignytion io
01/44
I2C protocol and ASIC build
A student lesson on a shared two-wire bus
Protocol rules, RTL interfaces, verification and routed GDS
IGNYTION_TECH October 2026
Reference build. Foundry DRC/LVS and full-chip signoff are unperformed.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Lesson goal: follow a byte from software through a controller to a target, then distinguish functional simulation from physical implementation. Students need basic binary numbers, registers and clocked logic. The local build is a fixed-function reference with an IHP SG13G2 implementation. It does not yet implement the competition’s programmable emulator.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 2
I2C STUDENT LAB
Ignytion io
02/44
What a communication protocol defines
Devices agree on the meaning of signals over time.
The rules identify the receiver, frame the data and report acceptance.
RTL implements these rules with registers, counters and state.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Use a temperature sensor as the classroom example. A CPU wants a measurement but only sees voltage levels on pins. A protocol gives those levels an agreed meaning. Distinguish electrical behaviour, bit timing and application register meaning. A device address selects a target, while the register address selects something inside that target. Those are different fields.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 3
I2C STUDENT LAB
Ignytion io
03/44
The two bus wires
SDA carries addresses, data and acknowledgements.
SCL marks when each data bit is valid.
All devices share a reference ground and compatible voltage levels.
Signal | Purpose | Normal idle
SDA | Bidirectional serial data | High
SCL | Serial clock, stretching supported by protocol | High
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Explain controller and target roles. The controller starts a transfer and normally generates SCL. A target responds to its address. Bidirectional SDA changes owner during acknowledgement and read phases. The core exposes separate input, output and enable pins because digital core signals need pad-level integration.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 4
I2C STUDENT LAB
Ignytion io
04/44
Open-drain signalling
A participant pulls a line low or releases it.
A pull-up resistor restores a released line to high.
A released output must still observe the actual bus input.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Demonstrate with switches to ground and a resistor to supply. If any switch closes, everyone observes low. This supports shared ownership without opposing high and low drivers. Pull-up selection depends on rise time, bus capacitance and sink current. An RTL tri-state model is ideal digital behaviour and does not prove these analogue limits. The integration needs correct output-enable polarity.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 5
I2C STUDENT LAB
Ignytion io
05/44
Open-drain ownership truth table
Released means high impedance, not actively driven high.
The actual bus value depends on every participant.
Controller | Target | SDA observed
Release | Release | 1, via pull-up
Pull low | Release | 0
Release | Pull low | 0
Pull low | Pull low | 0
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Work through each row with two switches to ground. The pull-up can raise the line only when neither participant sinks current. Explain why a controller sending a logical one must observe SDA: another controller can still pull it low. A digital simulation does not model pull-up resistance or pad sink current.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 6
I2C STUDENT LAB
Ignytion io
06/44
Pull-up calculation: a 3.3 V bus
Assume Cbus = 100 pF, tr limit = 300 ns, VOL = 0.4 V, IOL = 3 mA.
Rmin = (3.3 - 0.4) / 0.003 = 967 ohm
Rmax = 300 ns / (0.8473 x 100 pF) = 3.54 kohm
2.2 kohm gives tr about 186 ns and sink current about 1.32 mA.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
These are stated classroom assumptions, not measured board values. The 0.8473 factor describes the 30-to-70 percent RC rise interval. A real design must use the device data sheet limits and include wiring, connector and pin capacitance. Ask what happens when capacitance doubles: the same pull-up gives about 373 ns rise time and fails the assumed 300 ns budget. NXP UM10204 section 7.1 describes this method. This calculation does not prove electrical compliance of our RTL pads.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 7
I2C STUDENT LAB
Ignytion io
07/44
START, STOP and repeated START
START: SDA falls while SCL remains high.
STOP: SDA rises while SCL remains high.
Repeated START begins another addressed phase without releasing the bus.
Phase | SCL | SDA change
START | High | High to low
Data update | Low | Next bit may change
Data valid | High | Stable
STOP | High | Low to high
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
For ordinary data, SDA should stay stable while SCL is high. START and STOP are exceptions that define a transaction boundary. A typical register read writes a register index and then uses repeated START to switch to read direction. The bench exercises that sequence, but does not independently assert every legal timing parameter.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 8
I2C STUDENT LAB
Ignytion io
08/44
START and STOP: annotated edge trace
Slot 2: SDA falls with SCL high, creating START.
Slots 4 and 7 change data while SCL is low. Slot 9 creates STOP.
Chart: SCL
| 0 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 7 | 8 | 8 | 9 | 9 | 10 | 10 | 11
SCL | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1
Chart: SDA
| 0 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 7 | 8 | 8 | 9 | 9 | 10 | 10 | 11
SDA | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
Logic levels: HIGH=1, LOW=0. IDEAL WORKED EXAMPLE: logic values, not a measured trace
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Read the x-axis as illustrative timing slots, not nanoseconds. Ask the class which transitions establish boundaries and which simply prepare data. This crop illustrates edge rules only and does not contain a complete addressed transaction. Ordinary data stays stable during SCL high. START and STOP deliberately change SDA during high.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 9
I2C STUDENT LAB
Ignytion io
09/44
Eight data bits and a ninth response
A byte travels most significant bit first.
The transmitter releases SDA for the ninth clock.
The receiver returns ACK low or leaves NACK high.
Clock | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Meaning | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | ACK/NACK
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Walk through one byte and ask who owns SDA on clock nine. For a write, the target acknowledges each received byte. For a read, the controller acknowledges received data. Clock count includes the response bit, so one payload byte consumes at least nine SCL periods. Additional address and control phases add overhead.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 10
I2C STUDENT LAB
Ignytion io
10/44
The address byte
The common address format uses seven address bits.
The eighth bit selects write 0 or read 1.
A datasheet may display a seven-bit address or an already shifted byte.
Target address | Direction | Address byte
0x10 | Write | 0x20
0x10 | Read | 0x21
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Use address 0x10 from this bench. Shift it left by one: the write address byte is 0x20 and the read byte is 0x21. Do not confuse either byte with the register index. Reserved addresses and ten-bit addressing exist, but this lesson’s example uses seven-bit addressing.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 11
I2C STUDENT LAB
Ignytion io
11/44
Address 0x50: nine clock pulses
Seven-bit address 1010000 plus write bit 0 gives byte 0xA0.
Odd-numbered half-bit slots sample 1 0 1 0 0 0 0 0, then ACK=0.
Chart: SCL
| 0 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 7 | 8 | 8 | 9 | 9 | 10 | 10 | 11 | 11 | 12 | 12 | 13 | 13 | 14 | 14 | 15 | 15 | 16 | 16 | 17 | 17 | 18
SCL | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
Chart: SDA
| 0 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 7 | 8 | 8 | 9 | 9 | 10 | 10 | 11 | 11 | 12 | 12 | 13 | 13 | 14 | 14 | 15 | 15 | 16 | 16 | 17 | 17 | 18
SDA | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Logic levels: HIGH=1, LOW=0. IDEAL WORKED EXAMPLE: logic values, not a measured trace
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Decode every high SCL interval before looking at the answer. The transmitted byte is the address shifted left once plus direction, not the seven-bit number itself. SDA on the ninth interval belongs to the addressed target, while the controller supplies SCL. This is a pedagogical target address; the actual regression uses target 0x10 and transmits 0x20.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 12
I2C STUDENT LAB
Ignytion io
12/44
Worked register write
Example: target 0x10, register 0x01, values 0xA5 and 0x5A.
Each transmitted byte needs its own ACK.
STOP finishes the transaction.
Order | Bus item | Response owner
1 | START, 0x20 | Target ACK
2 | Register index 0x01 | Target ACK
3 | Data 0xA5 | Target ACK
4 | Data 0x5A, STOP | Target ACK before STOP
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Narrate the software sequence while students identify SDA ownership. The register index and auto-increment behaviour belong to the target’s application contract, not to I2C itself. The local target model stores bytes for this exercise. A real device datasheet determines whether this exact multi-byte sequence is valid.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 13
I2C STUDENT LAB
Ignytion io
13/44
Worked register read
Write the register index before the read phase.
Repeated START carries 0x21 for read direction.
The controller acknowledges more data and NACKs the final byte.
Phase | Transmitter | Receiver response
Address and index | Controller | Target ACK
Repeated START and 0x21 | Controller | Target ACK
First data byte | Target | Controller ACK
Last data byte | Target | Controller NACK then STOP
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
The first acknowledged read requests more bytes. The controller should NACK the final byte before STOP to tell the target that the receive phase is over. Our regression checks A5 and 5A. Later uninitialized locations print unknown values but are not asserted, so they cannot count as extra verified payload bytes.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 14
I2C STUDENT LAB
Ignytion io
14/44
Final read byte: controller sends NACK
The target transmits 0xA5 as 1 0 1 0 0 1 0 1.
The controller releases SDA for ninth-bit NACK=1, then issues STOP.
Chart: SCL
| 0 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 7 | 8 | 8 | 9 | 9 | 10 | 10 | 11 | 11 | 12 | 12 | 13 | 13 | 14 | 14 | 15 | 15 | 16 | 16 | 17 | 17 | 18
SCL | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
Chart: SDA
| 0 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 7 | 8 | 8 | 9 | 9 | 10 | 10 | 11 | 11 | 12 | 12 | 13 | 13 | 14 | 14 | 15 | 15 | 16 | 16 | 17 | 17 | 18
SDA | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Logic levels: HIGH=1, LOW=0. IDEAL WORKED EXAMPLE: logic values, not a measured trace
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
The receiver owns the acknowledgement bit. During a read, the controller receives the data and therefore chooses ACK or NACK. NACK on the final requested byte means the controller does not want another byte, which is an expected end condition. Contrast this with an address NACK, where the target did not accept selection. START/STOP are outside this byte-only crop.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 15
I2C STUDENT LAB
Ignytion io
15/44
Register read: ownership by phase
Example target 0x50, register 0x01, result 0xA5.
The register index is a device convention, separate from the bus address.
Phase | Wire byte/event | SDA sender
Select for write | START, A0 | Controller
Choose register | 01, with target ACK | Controller
Select for read | Repeated START, A1 | Controller
Read result | A5 | Target
Finish | NACK, STOP | Controller
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Walk through why the controller first writes an index even though the application wants a read. Repeated START keeps the transaction active while changing direction. The target owns read data, and the controller owns the final response. Some devices use different register widths or pointer behaviour; this worked convention is not universal.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 16
I2C STUDENT LAB
Ignytion io
16/44
Acknowledgement and error handling
NACK can mean no addressed target or rejected data.
Software must inspect status instead of assuming success.
A transfer timeout protects software from a stuck bus.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
The bench probes an invalid address and asserts the NACK result. That test is useful because a controller can generate perfectly shaped clocks while communicating with no device. Discuss application retry policy separately from protocol signalling. The simulation watchdog is a test safety mechanism, not proof of a hardware bus-recovery implementation.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 17
I2C STUDENT LAB
Ignytion io
17/44
Clock stretching
A target can hold SCL low to delay progress.
The controller must wait for the observed line to rise.
The model exercises stretching indirectly.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Distinguish releasing SCL from observing SCL high. The actual bus can remain low because another participant holds it. The RTL samples the pad input. The inherited bench includes a stretching target, but its completion assertion does not certify arbitrary stretch durations or stuck-low recovery. This limitation belongs in an honest test report.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 18
I2C STUDENT LAB
Ignytion io
18/44
Multiple-controller arbitration
Two controllers may begin while the bus is idle.
A controller that sends a released 1 but observes 0 loses arbitration.
A losing controller stops driving the contested transfer.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
The selected OpenCores design contains arbitration logic. Presence of that logic is different from test coverage. The second controller in this regression remains idle, so arbitration under contention is not validated. Ask students to construct a separate test where controllers diverge on an address bit. Review NXP rules before implementing such a test.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 19
I2C STUDENT LAB
Ignytion io
19/44
Bus rate and throughput
Standard-mode commonly runs up to 100 kbit/s.
Fast-mode commonly runs up to 400 kbit/s.
Address and ACK overhead reduce useful payload throughput.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Explain that a 50 MHz core clock does not mean a 50 MHz I2C bus. The divider generates slower serial timing. Electrical rise/fall limits also constrain speed. For an illustrative one-byte register write, address, index and data consume 27 clocks before START/STOP timing. Do not claim this core passes every speed grade merely because synthesis meets its system-clock target.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 20
I2C STUDENT LAB
Ignytion io
20/44
Prescaler calculation for this RTL
Nominal SCL = fwb / (5 x (PRER + 1)).
At 50 MHz and PRER=99: SCL = 100 kHz.
At PRER=24: SCL = 400 kHz before stretching and input filtering.
Context | PRER expression | Nominal result
50 MHz, 100 kHz | 50e6 / (5 x 100e3) - 1 = 99 | 100 kHz
50 MHz, 400 kHz | 50e6 / (5 x 400e3) - 1 = 24 | 400 kHz
Test at 100 MHz | 0x00C8 = 200 | 99.502 kHz
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
This formula follows the OpenCores five-phase bit controller and the divider reload. It is a nominal calculation, not a guarantee of wire duty cycle or electrical compliance. The physical reference targets 50 MHz, but the existing regression uses a 100 MHz testbench clock and PRER 0x00C8, giving a nominal 99.502 kHz. Keep those contexts separate. Explain the plus one by counting inclusive counter values. Program the low and high prescaler bytes while the core is disabled; obey the source register contract.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 21
I2C STUDENT LAB
Ignytion io
21/44
Useful throughput: the ACK overhead
A 1-byte register write needs address, index and data: 27 SCL pulses.
At 100 kHz, those pulses take 270 us before boundary and software delays.
A 1-byte combined read needs 36 pulses, or 360 us before other delays.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Count nine pulses for each byte, including acknowledgement. The combined read sends write address and index, then read address and one returned byte. Only the returned byte is useful payload for that read, giving about 2778 bytes per second before additional overhead. This is different from the 100000 bits per second wire clock. Clock stretching and software polling can lower throughput further. These numbers are calculated examples, not benchmark measurements.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 22
I2C STUDENT LAB
Ignytion io
22/44
The local register interface
Wishbone selects a register and reads or writes one byte.
The controller separates register, byte and bit-level work.
Interrupt and status outputs report progress.
Offset | Read | Write
0 / 1 | Prescaler low / high | Prescaler low / high
2 | Control | Control
3 | Receive byte | Transmit byte
4 | Status | Command
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Trace i2c_core into i2c_master_top, then byte_ctrl and bit_ctrl. The wrapper adds synchronized reset release and preserves the existing port contract. Explain why an internal software bus and an external serial bus are separate interfaces.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 23
I2C STUDENT LAB
Ignytion io
23/44
I2C implementation responsibilities
The register block stores configuration and commands.
The byte controller shifts eight bits and handles the ninth bit.
The bit controller sequences SCL/SDA and observes the bus.
Module | Responsibility
i2c_core | Ports and reset release
i2c_master_top | Wishbone registers and status
i2c_master_byte_ctrl | Byte shifting and ACK/NACK
i2c_master_bit_ctrl | Bit phases, synchronization and stretching
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Follow the real hierarchy rather than treating the wrapper as the whole protocol implementation. A software write becomes a command, the byte controller converts it to bit operations, and the bit controller waits for line conditions. The reset wrapper adds synchronized release. Input synchronizers/filtering do not remove the need for external electrical compliance.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 24
I2C STUDENT LAB
Ignytion io
24/44
RTL walkthrough: register reads
The same address can name different read and write registers.
Address 3 reads RXR but writes TXR. Address 4 reads status but writes commands.
case (wb_adr_i) // synopsys parallel_case
3'b000: wb_dat_o <= prer[ 7:0];
3'b001: wb_dat_o <= prer[15:8];
3'b010: wb_dat_o <= ctr;
3'b011: wb_dat_o <= rxr; // write is transmit register (txr)
3'b100: wb_dat_o <= sr; // write is command register (cr)
3'b101: wb_dat_o <= txr; // Debug out of TXR
3'b110: wb_dat_o <= cr; // Debug out control reg
3'b111: wb_dat_o <= {1'b0,sladr}; // slave address register
hw/protocols/i2c/01_rtl/i2c_master_top.v:175
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Explain each case arm using actual source. The Wishbone read returns the receive register at address three; writing there queues outgoing data. This shared address is not an error. The bus acknowledgement means the register operation completed, not that a remote I2C target acknowledged. Keep those two acknowledgements distinct when debugging.
Actual source excerpt: hw/protocols/i2c/01_rtl/i2c_master_top.v:175
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 25
I2C STUDENT LAB
Ignytion io
25/44
RTL walkthrough: command bits
0x90 requests START plus write. 0x10 requests another write byte.
Read commands choose ACK/NACK separately from data direction.
wire sta = cr[7];
wire sto = cr[6];
wire rd = cr[5];
wire wr = cr[4];
wire ack = cr[3];
wire sl_cont = cr[1];
wire iack = cr[0];
hw/protocols/i2c/01_rtl/i2c_master_top.v:237
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Decode hexadecimal commands one bit at a time. Bit seven is START, bit six STOP, bit five READ, bit four WRITE, and bit three the response selection. The current bench uses these constants; verify status TIP clears before issuing the next command. A polling loop also needs a system timeout, which is separate from the bare peripheral logic.
Actual source excerpt: hw/protocols/i2c/01_rtl/i2c_master_top.v:237
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 26
I2C STUDENT LAB
Ignytion io
26/44
Reset and pad integration
Default external asynchronous reset is active low.
The wrapper asserts reset asynchronously and releases it through two flops.
Separate pad inputs and enables preserve shared-bus behaviour.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
ARST_LVL is an elaboration parameter. The default is zero, so low arst_i asserts reset. The wrapper converts polarity and passes active-low reset to the upstream controller. A two-flop release improves clock-domain reset handling but is not a metastability or reset-domain signoff report. There is also a synchronous Wishbone reset input. Pad integration still needs an actual I/O cell and electrical design.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 27
I2C STUDENT LAB
Ignytion io
27/44
RTL walkthrough: reset release
Assertion is asynchronous. Release requires two wb_clk_i edges.
Default ARST_LVL=0 means arst_i is active low.
wire reset_n = arst_i ^ ARST_LVL;
(* async_reg = "true" *) reg [1:0] reset_release;
always @(posedge wb_clk_i or negedge reset_n)
if (!reset_n) reset_release <= 2'b00;
else reset_release <= {reset_release[0], 1'b1};
i2c_master_top #(.ARST_LVL(1'b0)) controller (
hw/protocols/i2c/01_rtl/i2c_core.v:23
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
The XOR converts the selected external assertion level into an internal active-low reset. While asserted, both release flops clear. Once the external reset becomes inactive, ones shift through on consecutive clock edges. The controller receives the second stage. This reduces release hazards inside this clock domain; it does not provide board-level reset sequencing for every pad or external target.
Actual source excerpt: hw/protocols/i2c/01_rtl/i2c_core.v:23
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 28
I2C STUDENT LAB
Ignytion io
28/44
What the I2C regression proves
Register access and checked A5/5A write/read results pass.
An invalid address produces the expected NACK.
Independent injected A5 and 5A mismatches both fail.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Read the PASS line and the negative-control logs rather than treating $finish as success. List absent evidence: active arbitration, exhaustive target behaviours, full timing-spec assertions and analogue bus limits. This is directed functional verification. Unknown later reads remain visible and unclaimed. Local evidence: hw/protocols/i2c/02_sim/test.v and simulation/negative-control logs.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 29
I2C STUDENT LAB
Ignytion io
29/44
Measured I2C trace: address and ACK
Actual positive regression, target 0x10, write address byte 0x20.
Measured period 10.71 us (93.371 kHz); nominal divider gives 10.05 us.
Chart: SCL
| 0 | 9.02 | 9.02 | 15.05 | 15.05 | 19.91 | 19.91 | 25.94 | 25.94 | 30.62 | 30.62 | 36.65 | 36.65 | 41.33 | 41.33 | 47.36 | 47.36 | 52.04 | 52.04 | 58.07 | 58.07 | 62.75 | 62.75 | 68.78 | 68.78 | 73.46 | 73.46 | 79.49 | 79.49 | 84.17 | 84.17 | 90.2 | 90.2 | 94.88 | 94.88 | 100.91 | 100.91 | 105.59 | 105.59 | 106.91
SCL | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0
Chart: SDA
| 0 | 5 | 5 | 5.71 | 5.71 | 5.72 | 5.72 | 34.64 | 34.64 | 45.35 | 45.35 | 105.591 | 105.591 | 106.91
SDA | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
Logic levels: HIGH=1, LOW=0. MEASURED: positive Icarus regression
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
This is a crop from the current positive Icarus run. A separate VCD decoder verified the first eight rising-edge samples form 0x20 and the ninth sample is zero. The x-axis is microseconds relative to the crop start. Treat it as measured digital behaviour, not an oscilloscope capture or proof of analogue rise time. Source and run-specific VCD hash are in the chart manifest. The waveform has 1071 core cycles per steady SCL period, versus a nominal divider count of 1005. The extra 66 cycles are observed, not yet attributed to individual filter or synchronizer states. Do not present the nominal rate as a measured wire rate.
Measured waveform: hw/protocols/i2c/02_sim/i2c_core.vcd
VCD SHA256 (run-specific): 92a33c5d8fa011907725903c0a42a46363a0a713fcafd04ccbc1cf326bed4714
Address byte 0x20 = target 0x10 plus write bit 0. Ninth SCL samples ACK=0. Measured steady SCL period 10.71 us, 93.371 kHz; nominal divider estimate 10.05 us, 99.502 kHz. Extra 66 core cycles per period are observed; their exact internal attribution is not established.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 30
I2C STUDENT LAB
Ignytion io
30/44
Fault diagnosis: observations first
An ACK failure and a stuck bus have different causes.
The current test proves selected functional cases, not every recovery policy.
Observation | First checks
Address NACK | 7-bit address, shifted byte, target reset/power
SDA stuck low | Pad enable polarity, wiring, target state
SCL never rises | Stretching target, pull-up, output enable
Wrong data at ACK bit | SDA ownership changes too late
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Ask students to choose the first check before rewriting the RTL. A wrong shifted address is different from a wrong register index. An output-enable polarity error can hold SDA low even with correct command bytes. Multi-controller arbitration needs an independently active second controller, which the current regression does not provide.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 31
I2C STUDENT LAB
Ignytion io
31/44
Guided lab: register-read prediction
Before running: decode A0, 01, A1, A5 and their senders.
At 100 kHz, predict the minimum byte-clock time.
In the real test, locate PRER=0x00C8 and the fatal negative controls.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Students first write the predicted answer, then locate the relevant source and logs. Use the hypothetical target 0x50 for the paper exercise and the actual target 0x10 for the baseline test. Do not silently change the supplied regression to match a classroom address. Run make sim only in the existing unit, and inspect both the normal PASS banner and deliberately failing comparison. The following slide supplies the model answer.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 32
I2C STUDENT LAB
Ignytion io
32/44
Lab solution: read sequence and timing
A0 selects target 0x50 for write. 01 selects its register.
A1 selects that target for read. Target sends A5, controller sends NACK.
4 bytes x 9 pulses = 36 pulses, or 360 us at 100 kHz.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
The target acknowledges both selection bytes and the index. The controller acknowledges received data only when it wants more bytes; it NACKs the final byte in this one-byte read. Repeated START separates the write and read address phases without a STOP between them. Boundary timing, software latency and stretching are excluded from the 360 microsecond estimate. The actual build uses a different programmed divider, so do not compare this estimate to that trace as if the assumptions matched.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 33
I2C STUDENT LAB
Ignytion io
33/44
Lab solution: evidence navigation
02_sim/test.v defines the transaction and checks A5/5A.
negative_control.log and negative_control_5a.log must contain FATAL.
08_sta separates setup/hold evidence from the protocol-level test.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Require students to point to an actual assertion rather than a display statement. A negative control intentionally corrupts an expected value, not the production RTL. Its nonzero exit proves the comparison can reject a mismatch. Then ask students why positive setup slack does not prove the I2C protocol is functionally correct: timing analysis checks paths and constraints, whereas the bench checks the meaning of serial transactions.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 34
I2C STUDENT LAB
Ignytion io
34/44
Bit-controller FSM: a write-bit operation
Actual c_state sequence: wr_a, wr_b, wr_c, wr_d, then idle.
A released SCL output still depends on the observed bus, allowing stretching.
State | SCL action | SDA action
wr_a | Pull low | Set current data bit
wr_b | Release | Keep data, allow settling
wr_c | Remain released | Keep data, enable bus check
wr_d | Pull low | Keep data, acknowledge bit command
idle | Await next command | Hold current drive policy
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Read the write branch in i2c_master_bit_ctrl.v. The table summarizes the actual named states and output-enable assignments, not a newly invented controller. An enable of one releases the open-drain line; it does not force a high voltage. In wr_c the implementation checks SDA for arbitration. Command acknowledgement marks completion of the bit operation, which is separate from target acknowledgement on the ninth bus pulse.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 35
I2C STUDENT LAB
Ignytion io
35/44
Source and reproducible workspace
freecores/i2c at 3b067f00ccced753b0502024766a51f58f3e04bc
Original upstream notices and licences remain in the repository.
crucible.toml selects the protocol environment and crucible.lock pins its tools.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Explain why a repository URL alone is insufficient for reproducibility: the branch can change. A commit identifies the chosen source revision. Local wrappers and benches are separate integration work. Igny records tool bindings, while the PDK revision is pinned separately. Source identity does not mean every upstream feature has been validated.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 36
I2C STUDENT LAB
Ignytion io
36/44
WSL Igny laboratory commands
igny init
unset CRUCIBLE_ENV
cd <repository>/hw/protocols/i2c
make flow
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Use the existing unit directory, not a new project folder. After initialization, unset a stale environment override so the workspace selection applies. The unit run script then selects janestreet-i2c. If tools are missing, bind or install Icarus, Verilator, Yosys, OpenROAD and klayout-stream. Lock the workspace after changing bindings. Keep the actual SG13G2 PDK available.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 37
I2C STUDENT LAB
Ignytion io
37/44
Lint and functional verification
make lint elaborates every RTL source for the selected top.
make sim runs assertions and deliberate negative controls.
Warnings remain visible and need review.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Verilator lint can identify widths, unused logic and reset-related warnings. The reference retains upstream warnings instead of claiming warning-free RTL. A simulator exit code or $finish alone is not a PASS. Read the assertion banner, negative-control fatal message and waveform. A deliberately wrong expected byte must fail to demonstrate that comparisons are active.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 38
I2C STUDENT LAB
Ignytion io
38/44
Technology-mapped synthesis
make synth maps i2c_core to SG13G2 standard cells.
The mapped design contains 1007 functional cells.
The build inserts technology tie cells for constant nets.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Yosys elaborates, optimizes and maps combinational/sequential logic using Liberty timing data. Cell counts exclude scope metadata and differ from physical counts that include fillers and buffers. The flow uses hilomap for SG13G2 tie-high and tie-low cells. A zero unresolved-cell report and no latch cells are separate checks from functional correctness.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 39
I2C STUDENT LAB
Ignytion io
39/44
Floorplan, placement and clock tree
Reference die is 300 by 300 micrometres.
Placement chooses legal cell locations and builds the power grid.
Clock-tree synthesis buffers the clock before detailed routing.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
The die area is 90000 square micrometres, derived from DEF units and DIEAREA. This rectangle is a reference block, not a Tiny Tapeout tile allocation. CTS manages clock latency, skew and electrical loading. Hold repair may add delay cells. The UART experiment exposed a real root fanout violation, showing why successful execution alone does not establish closure.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 40
I2C STUDENT LAB
Ignytion io
40/44
Routing and extracted timing
Detailed routing connects placed cells using allowed layers.
Extraction provides routed parasitic resistance and capacitance.
STA checks both typical and slow Liberty corners at 20 ns.
Corner | Setup slack ns | Hold slack ns
Typical | 15.81 | 0.17
Slow | 14.55 | 0.21
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Explain setup as meeting a capture deadline and hold as avoiding an excessively early change. Positive slack means the analyzed constraint has margin. I/O delays and clock uncertainty are assumed reference budgets. Two passing corners do not establish all process, voltage, temperature and RC combinations. Router DRC checks a subset of geometry rules, not foundry signoff.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 41
I2C STUDENT LAB
Ignytion io
41/44
The routed GDS result
10_gds/i2c_core.gds contains 1,583,844 bytes.
The decoder resolves 48 structures and compares 14,546 placed cell instances.
Coordinates, orientations and referenced cell identities agree with DEF.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
klayout-stream strm2gds combines routed DEF, technology/cell LEF and actual standard-cell GDS using the PDK layer map. The independent binary reader checks valid records, resolved references and exact standard-cell placement/orientation counts. Many instances are filler cells, so this number is not the synthesized logic-cell count. Raw hashes are run-specific because GDS contains timestamps.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 42
I2C STUDENT LAB
Ignytion io
42/44
Evidence and signoff boundaries
Functional tests, mapped synthesis and routed export have evidence.
Foundry DRC, LVS, antenna and full-chip signoff have not run.
Jane Street still requires a programmable emulator on its CMOS5L template.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Distinguish the achieved student reference from a manufacturable submission. Structural GDS comparison is not electrical equivalence. Router-rule DRC is not a foundry deck. The current fixed-function SG13G2 blocks do not satisfy the competition’s reprogrammable general-purpose emulator requirement or process/template requirement. No tapeout-ready claim is justified.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 43
I2C STUDENT LAB
Ignytion io
43/44
I2C laboratory exercises
Decode a byte using the protocol rules covered in this lesson.
Change one expected result and observe a fatal test failure.
Compare functional cell count with physical filler/buffer counts.
Locate the worst setup and hold paths in both timing reports.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Ask students to write a prediction before simulation. Keep changed expectations in a separate temporary exercise branch so the baseline remains reproducible. Have them explain why the negative control is evidence about the bench rather than a defect in the DUT. Then read exact startpoint, endpoint, clock path and data arrival time from the reports. Students should state the limitations of each artifact.
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////

## Slide 44
I2C STUDENT LAB
Ignytion io
44/44
Review questions and reading
Which event establishes the first bit of a transfer?
Who owns the data wire at each stage?
What does the current regression leave untested?
Why does an exported GDS not prove signoff?
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/I2C_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Answers depend on the protocol: I2C uses START and addressed phases, SPI uses select plus the agreed clock edges, and UART uses START plus local baud timing. Revisit each byte-order rule. Reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Upstream: freecores/i2c at 3b067f00ccced753b0502024766a51f58f3e04bc
Flow: OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Competition: Jane Street official requirements: https://blog.janestreet.com/protocol-emulator-asic-competition/
Protocol reading: NXP UM10204 Rev. 7: https://cache.nxp.com/docs/en/user-guide/UM10204.pdf
Implementation evidence: hw/protocols/i2c/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
//// ////
//// Copyright (C) 2001 Richard Herveille ////
//// richard@asics.ws ////
//// ////
//// This source file may be used and distributed without ////
//// restriction provided that this copyright statement is not ////
//// removed from the file and that any derivative work contains ////
//// the original copyright notice and the associated disclaimer.////
//// ////
//// THIS SOFTWARE IS PROVIDED ``AS IS'' AND WITHOUT ANY ////
//// EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED ////
//// TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS ////
//// FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR ////
//// OR CONTRIBUTORS BE LIABLE FOR ANY DIRECT, INDIRECT, ////
//// INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES ////
//// (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE ////
//// GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR ////
//// BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF ////
//// LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT ////
//// (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT ////
//// OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE ////
//// POSSIBILITY OF SUCH DAMAGE. ////
//// ////