## Slide 1
UART STUDENT LAB
Ignytion io
01/44
UART protocol and ASIC build
A student lesson on asynchronous serial bytes
Frame timing, receiver sampling, verification and routed GDS
IGNYTION_TECH October 2026
Reference build. Foundry DRC/LVS and full-chip signoff are unperformed.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Lesson goal: decode an 8N1 frame without a shared clock wire and relate baud rate to local clock cycles. The local UART core is a full-duplex byte interface. Explain the distinction between a UART logic-level signal and RS-232 electrical signalling.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 2
UART STUDENT LAB
Ignytion io
02/44
Asynchronous serial communication
The transmitter and receiver use their own local clocks.
A START transition establishes the beginning of a frame.
Both ends must agree on baud rate and frame format.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Asynchronous means no clock is carried with each transmitted bit. It does not mean the hardware lacks a clock. Explain why sampling must occur near the centre of each bit and why mismatch accumulates as the frame progresses. The STOP interval returns the link to an idle state.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 3
UART STUDENT LAB
Ignytion io
03/44
TX, RX and electrical levels
TX from one device connects to RX at the other.
A shared ground and compatible signalling levels are required.
An external transceiver is needed for RS-232 or RS-485 links.
Pin | Role | Idle for this UART
txd | Transmit serial output | High
rxd | Receive serial input | High
clk | Local logic clock | 50 MHz reference target
rst | Synchronous active-high reset | Low during normal operation
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
The local rxd and txd pins carry logic-level signals. RS-232 uses different voltage levels and polarity and cannot safely connect directly to ordinary digital pins. Full duplex uses independent wires in each direction. Flow-control pins such as RTS/CTS are optional system features absent from this wrapper.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 4
UART STUDENT LAB
Ignytion io
04/44
UART logic levels and electrical interfaces
The RTL expects logic-level RX/TX with a shared reference.
RS-232 voltage conversion and RS-485 bus control need separate hardware.
Interface | Electrical meaning | Extra hardware
Logic UART | Digital RX/TX levels | Compatible pads and ground
RS-232 | Different voltage/polarity convention | Level-converting transceiver
RS-485 | Differential shared link | Transceiver and bus-control policy
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
A UART is a framing and timing function, not a promise about connector voltages. Never connect an RS-232 voltage directly to a low-voltage ASIC input. An external transceiver can convert levels and polarity. RS-485 uses differential signalling and may require driver-enable timing for a shared half-duplex link. Those electrical functions are not in uart_core.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 5
UART STUDENT LAB
Ignytion io
05/44
The 8N1 frame
One low START bit begins the frame.
Eight data bits travel least significant bit first.
No parity bit and one high STOP bit complete the frame.
Interval | START | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7 | STOP
Meaning | 0 | LSB |  |  |  |  |  |  | MSB | 1
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
8N1 means eight data bits, no parity and one stop bit. It consumes ten bit periods per byte. Explain that UART implementations may support other formats, but this selected core and wrapper are configured for eight-bit data with no parity. There is no runtime parity setting.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 6
UART STUDENT LAB
Ignytion io
06/44
Worked frame for 0x53
0x53 is binary 01010011 when written MSB first.
The wire sends data bits in the opposite index order.
START and STOP surround the eight data bits.
Time order | START | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7 | STOP
Line value | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Spell out the value 0x53=83 decimal. Writing a number on paper usually puts the most significant bit on the left, while UART sends D0 first. The editable table shows temporal order. Ask students to reconstruct the hexadecimal byte from the observed stream.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 7
UART STUDENT LAB
Ignytion io
07/44
0x53 frame: LSB-first waveform
Frame slots: idle, START, b0..b7, STOP, idle.
0x53 sends data bits 1 1 0 0 1 0 1 0.
Chart: TX
| 0 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 7 | 8 | 8 | 9 | 9 | 10 | 10 | 11 | 11 | 12
TX | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1
Logic levels: HIGH=1, LOW=0. IDEAL WORKED EXAMPLE: logic values, not a measured trace
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Translate hexadecimal 53 into binary 01010011, then reverse the reading order for transmission: bit zero goes first. START is low for a bit interval and STOP is high. The initial and final high intervals are idle. This ideal waveform uses whole bit slots, not a measured baud rate. A signal that remains high between consecutive one bits still contains two separately timed bits.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 8
UART STUDENT LAB
Ignytion io
08/44
Baud rate and useful byte rate
Bit period equals one divided by baud.
8N1 carries eight useful bits in ten transmitted bit periods.
At 115200 baud, the ideal maximum is 11520 bytes/s.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Baud and bits per second coincide for this binary UART link. Calculate a bit period of about 8.681 microseconds and a frame period of about 86.806 microseconds at 115200 baud. Gaps or software delays reduce useful throughput. These are arithmetic examples, not measured throughput of this implementation.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 9
UART STUDENT LAB
Ignytion io
09/44
8N1 useful throughput calculation
START + 8 data + STOP = 10 wire bits per payload byte.
At 115200 baud: 11,520 bytes/s before gaps and application overhead.
A 32-byte message uses at least 320 bit intervals, about 2.778 ms.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
For binary UART signalling, baud equals serial bit rate here. It does not equal useful payload bits per second because framing consumes two intervals per byte. The 32-byte calculation excludes idle gaps, scheduling delays and packet headers. If an application sends each value as ASCII digits, its useful measurement rate can be lower still. These are arithmetic examples for 8N1, not a measured link benchmark.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 10
UART STUDENT LAB
Ignytion io
10/44
The local prescaler
Bit duration is 8 times prescale local clock cycles.
Nominal baud is f_clk divided by 8 times prescale.
Hold prescale stable while transmission or reception is busy.
Core clock | Prescale | Nominal baud
50 MHz | 2 | 3125000
50 MHz | 7 | 892857.14
50 MHz | 54 | 115740.74 (example only)
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
At the 50 MHz reference core clock, prescale 54 yields about 115740.74 baud, roughly 0.469 percent above 115200. This is an illustrative operating point, not part of the current regression. The tests validate divisors 2 through 7. Integer rounding and each endpoint’s clock error contribute to mismatch.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 11
UART STUDENT LAB
Ignytion io
11/44
Integer prescaler: 115200 baud at 50 MHz
Choose P near 50,000,000 / (8 x 115200) = 54.253.
P=54 gives 115740.74 baud, error +0.4694%.
P=55 gives 113636.36 baud, error -1.3573%.
Prescale | Calculated baud | Error versus 115200
54 | 115740.74 | +0.4694%
55 | 113636.36 | -1.3573%
651 for 9600 | 9600.61 | +0.0064%
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
The core uses an integer prescale and eight times that many core clocks per bit. Rounding the ideal prescaler to 54 gives the closer result in this example. A small arithmetic error is not a complete compatibility proof: clock tolerances, start-edge uncertainty and sample placement still matter. The actual directed regression sweeps P two through seven; P54 is a calculated classroom configuration, not one of the measured sweep points.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 12
UART STUDENT LAB
Ignytion io
12/44
Receiver sampling
The receiver detects a low START candidate.
It checks and samples within the expected bit intervals.
A two-flop wrapper synchronizer samples external RX.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Trace uart_core rx_sync into uart_rx. The asynchronous input can arrive near a clock edge. A synchronizer reduces propagation of metastability, but does not eliminate all risk or replace CDC analysis. Oversampling-related timing logic lives in the upstream receiver. Independent bench stimulus drives real serial bits rather than depositing parallel receive data.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 13
UART STUDENT LAB
Ignytion io
13/44
Receiver timing: centre-of-bit samples
Relative to START: centres are 0.5T, 1.5T, ... 9.5T.
START begins at chart slot 1. Data samples follow the START confirmation.
Chart: TX
| 0 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 7 | 8 | 8 | 9 | 9 | 10 | 10 | 11 | 11 | 12
TX | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1
Chart: Ideal centre ticks
| 0 | 1.5 | 1.5 | 1.56 | 1.56 | 2.5 | 2.5 | 2.56 | 2.56 | 3.5 | 3.5 | 3.56 | 3.56 | 4.5 | 4.5 | 4.56 | 4.56 | 5.5 | 5.5 | 5.56 | 5.56 | 6.5 | 6.5 | 6.56 | 6.56 | 7.5 | 7.5 | 7.56 | 7.56 | 8.5 | 8.5 | 8.56 | 8.56 | 9.5 | 9.5 | 9.56 | 9.56 | 10.5 | 10.5 | 10.56 | 10.56 | 12
Ideal centre ticks | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0
Logic levels: HIGH=1, LOW=0. IDEAL WORKED EXAMPLE: logic values, not a measured trace
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
The plotted sample ticks are an ideal teaching schedule, not a statement that this RTL uses a majority vote. START begins at chart time one, so its centre is at one point five. The ticks align to the START, eight data and STOP centres. The local RX implementation uses a counter to wait half a bit to confirm START, then full-bit waits for later samples. Input synchronization adds detection delay. Follow the source excerpt next rather than assuming every UART has the same oversampling implementation.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 14
UART STUDENT LAB
Ignytion io
14/44
RTL walkthrough: rejecting a false START
The receiver confirms the line is still low after its initial wait.
If it is high, it abandons the candidate frame.
if (bit_cnt > DATA_WIDTH+1) begin
if (!rxd_reg) begin
bit_cnt <= bit_cnt - 1;
prescale_reg <= (prescale << 3)-1;
end else begin
bit_cnt <= 0;
prescale_reg <= 0;
end
end else if (bit_cnt > 1) begin
hw/protocols/uart/01_rtl/uart_rx.v:117
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Read the actual branch rather than describe generic UART majority voting. When the initial candidate START does not remain low until the confirmation point, the receiver clears its bit counter and timer. If the line is still low, it advances to the data phase and loads a full-bit wait. This is a specific digital false-start check, not proof of immunity to every glitch width or analogue noise pattern.
Actual source excerpt: hw/protocols/uart/01_rtl/uart_rx.v:117
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 15
UART STUDENT LAB
Ignytion io
15/44
Baud mismatch and noise
Sampling error grows across the frame.
A false START or a low STOP can corrupt the byte.
The current tests do not certify arbitrary clock mismatch or noise.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Explain that a receiver does not continuously share phase with the transmitter. A fresh START helps re-establish timing for each frame. Do not promise a universal percentage tolerance because it depends on frame format and receiver implementation. Suggest a future bench sweep over positive and negative mismatch and short noise pulses.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 16
UART STUDENT LAB
Ignytion io
16/44
Baud mismatch accumulates across a frame
If receiver bit time differs by 2%, centre error grows by about 0.02T per bit.
Near the STOP centre at 9.5T, that is about 0.19T before other errors.
Start-detection delay and jitter consume additional sampling margin.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
This simplified drift example is a timing model, not a universal two-percent acceptance rule. The receiver re-synchronizes on a new START, but not on every data bit. Long runs without data transitions still need correct local timing. The ideal half-bit margin is reduced by start detection, synchronization, clock error and line distortion. Check a specific receiver data sheet or implementation before declaring an allowed total clock mismatch.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 17
UART STUDENT LAB
Ignytion io
17/44
Transmit ready-valid handshake
Keep tx_valid and tx_data stable until tx_ready accepts them.
Acceptance occurs on a clock edge with both signals high.
tx_busy describes serial activity after the byte enters the transmitter.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Compare this with the SPI launch-pulse interface. Ready-valid allows a producer to hold a request until accepted. Explain why a one-cycle pulse can lose a byte if ready is low. The selected transmitter does not provide an unbounded queue. Inspect upstream RTL to understand when it can accept another byte.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 18
UART STUDENT LAB
Ignytion io
18/44
Ready-valid stall: stable byte until acceptance
The source holds valid and data while ready=0.
Acceptance occurs only at a core-clock edge where both equal 1.
Chart: valid
| 0 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7
valid | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
Chart: ready
| 0 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7
ready | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1
Logic levels: HIGH=1, LOW=0. IDEAL WORKED EXAMPLE: logic values, not a measured trace
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
This ideal transaction concerns the byte-stream interface, not the serial baud clock. The submitted data remains constant through the stall; only valid and ready are shown. At cycle four both are high, so the byte transfers at that sampling edge. UART supports this held-valid contract, unlike the SPI pulse interface in this repository. The next byte may be presented after acceptance, subject to the core ready signal.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 19
UART STUDENT LAB
Ignytion io
19/44
Receive backpressure
rx_valid identifies a buffered byte.
rx_data must remain stable until rx_ready accepts it.
Another arriving byte can cause overrun while the buffer is occupied.
Situation | Expected behaviour
valid 1, ready 0 | Retain pending byte
valid 1, ready 1 | Consumer accepts byte
New byte, pending result occupied | Overrun indication may assert
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
The bench holds the receive byte for four cycles while applying backpressure. It asserts valid and data stability. A one-byte holding register is not a FIFO of arbitrary depth. The overrun test isolates a new frame arriving while a previous result is still unconsumed. Explain why software speed and buffering are system concerns.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 20
UART STUDENT LAB
Ignytion io
20/44
Receive buffer: what backpressure cannot stop
rx_ready=0 preserves a completed byte on the output interface.
The remote transmitter still sends serial bits. There is no CTS/RTS flow control here.
A new completed byte can cause overrun if the previous one is still pending.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
The source has a one-byte output register rather than an arbitrarily deep FIFO. Backpressure protects a byte only until another frame completes. Read the overwrite/overrun branch in the implementation to see that it can replace the pending value and flag the event. A larger FIFO or external flow control would be another design. The current test exercises a limited ready stall and an isolated overrun; it does not promise lossless indefinite stalls.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 21
UART STUDENT LAB
Ignytion io
21/44
Framing and overrun errors
Framing error reports an invalid STOP sample.
Overrun reports loss caused by an occupied receive buffer.
Error outputs are pulses, not persistent counters.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
The bench counts error pulses to compare expected events. A malformed STOP held low can look like another START and later generate a recovery word. The test explicitly drains recovery output before measuring an isolated overrun. This known behaviour is visible, not a claim of clean break detection or guaranteed recovery under any malformed input.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 22
UART STUDENT LAB
Ignytion io
22/44
Framing error: STOP stays low
START and data can look valid while the STOP interval is wrong.
The local receiver pulses frame_error instead of accepting that byte.
Chart: TX
| 0 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 7 | 8 | 8 | 9 | 9 | 10 | 10 | 11 | 11 | 12
TX | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
Logic levels: HIGH=1, LOW=0. IDEAL WORKED EXAMPLE: logic values, not a measured trace
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Compare with the earlier good frame. A framing error checks the expected STOP level; it is not a checksum across the data. A wrong data bit with a valid STOP may go undetected by an 8N1 receiver. Sustained low after malformed STOP can resemble another START in this core, producing later recovery activity. The test drains that recovery before isolating the overrun check.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 23
UART STUDENT LAB
Ignytion io
23/44
RTL walkthrough: frame completion and overrun
STOP high captures data and sets output valid.
If output valid was already high, the core raises overrun.
if (rxd_reg) begin
m_axis_tdata_reg <= data_reg;
m_axis_tvalid_reg <= 1;
overrun_error_reg <= m_axis_tvalid_reg;
end else begin
frame_error_reg <= 1;
end
hw/protocols/uart/01_rtl/uart_rx.v:131
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
This source branch belongs to the STOP-sampling stage. A valid STOP writes the newly assembled data register and marks it available. The prior valid state becomes the overrun flag. This means the error reports loss/overwrite risk; it does not automatically queue another byte. Explain nonblocking assignment semantics: the expression sees the prior register values at the clock edge, even though new values are scheduled below.
Actual source excerpt: hw/protocols/uart/01_rtl/uart_rx.v:131
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 24
UART STUDENT LAB
Ignytion io
24/44
Reset and recovery
rst is synchronous and active high.
Reset returns serial transmit to its idle state.
The bench aborts a transfer, then verifies another byte.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Synchronous reset requires a running clock to take effect. Reset polarity differs from the default I2C and SPI wrappers. Students should check the module contract rather than assume a universal reset convention. Declaration initializers in upstream code are visible lint warnings. The actual reset path and mapped flops still require inspection.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 25
UART STUDENT LAB
Ignytion io
25/44
RTL walkthrough: RX input synchronization
Two flops sample the asynchronous external pin before the UART decoder.
Reset is synchronous active high and initializes the sampled line to idle high.
(* async_reg = "true" *) reg [1:0] rx_sync;
always @(posedge clk)
if (rst) rx_sync <= 2'b11;
else rx_sync <= {rx_sync[0],rxd};
uart controller (
hw/protocols/uart/01_rtl/uart_core.v:24
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
The two-stage chain reduces propagation of metastability into the logic, but it cannot mathematically guarantee no failures. Its delay affects the start detection and must be considered with the baud interval. The marker guides implementation tools; it does not itself prove CDC correctness. The physical flow still needs proper placement and system integration checks before a reliability claim. A separate counter stage in upstream uart_rx samples this synchronized signal.
Actual source excerpt: hw/protocols/uart/01_rtl/uart_core.v:24
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 26
UART STUDENT LAB
Ignytion io
26/44
RTL walkthrough: launching a TX frame
The source byte latches before the serial shifter sends it.
A low START begins the frame and prescale controls its duration.
if (s_axis_tvalid) begin
s_axis_tready_reg <= !s_axis_tready_reg;
prescale_reg <= (prescale << 3)-1;
bit_cnt <= DATA_WIDTH+1;
data_reg <= {1'b1, s_axis_tdata};
txd_reg <= 0;
busy_reg <= 1;
hw/protocols/uart/01_rtl/uart_tx.v:102
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
The data register includes a high bit for the STOP phase alongside the payload. txd becomes low for START while busy becomes high. Later timer expirations shift data bits into the output. Read the enclosing state/ready logic before treating this branch as a standalone handshake formula; upstream ready alternates appropriately around acceptance. No parity generation or alternative word length is enabled by this wrapper.
Actual source excerpt: hw/protocols/uart/01_rtl/uart_tx.v:102
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 27
UART STUDENT LAB
Ignytion io
27/44
Independent full-duplex testing
One model observes the transmitted serial frame.
Another generates a different incoming serial sequence.
Both directions run at the same time.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Avoid simply connecting TX to RX, because loopback can share an error between transmitter and receiver. The local bench independently checks the outgoing frame and provides a separate expected receive pattern. This verifies both directions and exposes bit-order and serial framing errors.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 28
UART STUDENT LAB
Ignytion io
28/44
Measured UART trace: TX 0x53, independent RX
Actual positive full-duplex regression: TX 0x53, independent RX 0xAC.
Bit duration is 0.64 us, so the 8N1 frame is 6.4 us.
Chart: TX
| 0 | 0.32 | 0.32 | 0.96 | 0.96 | 2.24 | 2.24 | 3.52 | 3.52 | 4.16 | 4.16 | 4.8 | 4.8 | 5.44 | 5.44 | 6.08 | 6.08 | 7.04
TX | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
Chart: RX
| 0 | 0.31 | 0.31 | 2.23 | 2.23 | 3.51 | 3.51 | 4.15 | 4.15 | 4.79 | 4.79 | 5.43 | 5.43 | 7.04
RX | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
Logic levels: HIGH=1, LOW=0. MEASURED: positive Icarus regression
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
The VCD decoder selected a transmitted 0x53 frame, sampled each data centre, reconstructed 0x53 LSB first, and checked a high STOP. RX has a different concurrent stimulus rather than TX loopback. This proves the plotted digital frame and independent direction of the test. It is not a measured 115200 baud board capture: the fast test configuration is 1.5625 Mbaud. The independently driven RX frame decodes to 0xAC, the complement of TX 0x53; both STOP samples are high.
Measured waveform: hw/protocols/uart/02_sim/uart_core.vcd
VCD SHA256 (run-specific): adbfeb21e2f40fc1017325b344bd8b465fc06fbea7b51137b15223519d00fcec
TX data 0x53 and independent RX data 0xAC, LSB first, STOP high. Prescale 4, bit time 0.64 us.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 29
UART STUDENT LAB
Ignytion io
29/44
What the UART regression proves
All 256 byte values pass at prescale 4.
The prescale 2..7 sweep checks TX 96 and independent RX 69.
Full duplex, error/reset checks and fatal mismatch control pass.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Evidence lives in hw/protocols/uart/02_sim/test.v and simulation/negative-control logs. Exhaustive byte tests use prescale four; the later divisor sweep uses fixed 96/69 patterns, not every byte at every divisor. The baseline test drains malformed-frame recovery output before measuring overrun. It does not validate every prescaler, break detection, parity, alternate frame formats, noise immunity or external electrical transceivers.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 30
UART STUDENT LAB
Ignytion io
30/44
Guided lab: frame, divider and fault
Decode the 0x53 waveform in transmission order.
For 50 MHz and P=54, calculate baud and ten-bit frame time.
Predict which error flag appears when STOP is low and when a pending byte is overwritten.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Students answer independently before running the baseline. A waveform decode should name START, each data-bit index and STOP, not just report the final hexadecimal number. Find the prescale expression in source and use actual integer arithmetic. The next slide gives model answers and separates a mathematical P54 example from the tested P2-to-P7 range. Locate normal and injected-failure logs in the existing UART unit.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 31
UART STUDENT LAB
Ignytion io
31/44
Lab solution: byte order and framing
Data order for 53 is 1 1 0 0 1 0 1 0 after the low START.
P54 gives 115740.74 baud. 10-bit frame time is 86.4 us.
Low STOP raises frame_error. Pending output at another valid completion raises overrun.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
The prescaler calculation gives 432 core cycles per bit, each 20 nanoseconds, so a bit is 8.64 microseconds and ten bits are 86.4 microseconds. The receive error flags describe different events: malformed framing versus a storage/consumer problem. A valid STOP with corrupted data may raise neither. Neither error flag replaces an application-level checksum or sequence counter.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 32
UART STUDENT LAB
Ignytion io
32/44
Where UART fits
Debug consoles and simple point-to-point links use UART.
A higher-level protocol may add packet length, checksums and retries.
The byte stream alone does not define application messages.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Contrast UART framing with a complete telemetry packet. UART tells us where a byte begins and ends. An application still needs to define how many bytes make a message and what the message means. Discuss when UART’s simple wiring is useful and when synchronous buses or larger buffers fit better.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 33
UART STUDENT LAB
Ignytion io
33/44
RX control sequence: counter states
Actual 8-bit receiver starts bit_cnt at 10 after detecting low.
The count selects START confirmation, eight data samples and STOP check.
bit_cnt | Phase | Action when timer expires
0 | Idle | Observe low candidate START
10 | Confirm START | Continue only if line stays low
9 through 2 | Data b0 through b7 | Shift sampled RX into data register
1 | STOP | Accept data or flag framing error
0 again | Finish | Return to idle detection
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Map this table to uart_rx.v rather than assume an unrelated named-state FSM. A pending timer prevents a new sample until the proper interval expires. At count ten the receiver confirms START; at nine through two it shifts in the eight data bits; at one it evaluates STOP. It returns to zero after the frame. START detection initializes a half-bit delay and later data stages initialize full-bit delays. Output buffering and error flags are separate from this serial phase counter.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 34
UART STUDENT LAB
Ignytion io
34/44
Fault diagnosis: line, baud and buffer
Correct voltage levels are necessary before timing debugging.
Framing failures and overruns point to different parts of the path.
Observation | First checks
No START detected | RX wiring, ground, inversion, reset
Repeated frame_error | Baud mismatch, STOP length, electrical distortion
Overrun during bursts | rx_ready latency, buffer depth, flow control
Wrong byte with valid STOP | Data corruption and application checks
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Start by checking ground and electrical compatibility before changing software baud settings. A consistent wrong byte can indicate the wrong bit order or framing format. Errors that increase with long bursts suggest consumer latency or missing buffering. These are troubleshooting hypotheses, not newly tested board findings. The current proof covers the specified digital regressions and two timing corners, with no external transceiver verification.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 35
UART STUDENT LAB
Ignytion io
35/44
Source and reproducible workspace
alexforencich/verilog-uart at 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Original upstream notices and licences remain in the repository.
crucible.toml selects the protocol environment and crucible.lock pins its tools.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Explain why a repository URL alone is insufficient for reproducibility: the branch can change. A commit identifies the chosen source revision. Local wrappers and benches are separate integration work. Igny records tool bindings, while the PDK revision is pinned separately. Source identity does not mean every upstream feature has been validated.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 36
UART STUDENT LAB
Ignytion io
36/44
WSL Igny laboratory commands
igny init
unset CRUCIBLE_ENV
cd <repository>/hw/protocols/uart
make flow
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Use the existing unit directory, not a new project folder. After initialization, unset a stale environment override so the workspace selection applies. The unit run script then selects janestreet-uart. If tools are missing, bind or install Icarus, Verilator, Yosys, OpenROAD and klayout-stream. Lock the workspace after changing bindings. Keep the actual SG13G2 PDK available.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 37
UART STUDENT LAB
Ignytion io
37/44
Lint and functional verification
make lint elaborates every RTL source for the selected top.
make sim runs assertions and deliberate negative controls.
Warnings remain visible and need review.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Verilator lint can identify widths, unused logic and reset-related warnings. The reference retains upstream warnings instead of claiming warning-free RTL. A simulator exit code or $finish alone is not a PASS. Read the assertion banner, negative-control fatal message and waveform. A deliberately wrong expected byte must fail to demonstrate that comparisons are active.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 38
UART STUDENT LAB
Ignytion io
38/44
Technology-mapped synthesis
make synth maps uart_core to SG13G2 standard cells.
The mapped design contains 543 functional cells.
The build inserts technology tie cells for constant nets.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Yosys elaborates, optimizes and maps combinational/sequential logic using Liberty timing data. Cell counts exclude scope metadata and differ from physical counts that include fillers and buffers. The flow uses hilomap for SG13G2 tie-high and tie-low cells. A zero unresolved-cell report and no latch cells are separate checks from functional correctness.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 39
UART STUDENT LAB
Ignytion io
39/44
Floorplan, placement and clock tree
Reference die is 300 by 300 micrometres.
Placement chooses legal cell locations and builds the power grid.
Clock-tree synthesis buffers the clock before detailed routing.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
The die area is 90000 square micrometres, derived from DEF units and DIEAREA. This rectangle is a reference block, not a Tiny Tapeout tile allocation. CTS manages clock latency, skew and electrical loading. Hold repair may add delay cells. The UART experiment exposed a real root fanout violation, showing why successful execution alone does not establish closure.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 40
UART STUDENT LAB
Ignytion io
40/44
Routing and extracted timing
Detailed routing connects placed cells using allowed layers.
Extraction provides routed parasitic resistance and capacitance.
STA checks both typical and slow Liberty corners at 20 ns.
Corner | Setup slack ns | Hold slack ns
Typical | 15.75 | 0.17
Slow | 14.45 | 0.24
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Explain setup as meeting a capture deadline and hold as avoiding an excessively early change. Positive slack means the analyzed constraint has margin. I/O delays and clock uncertainty are assumed reference budgets. Two passing corners do not establish all process, voltage, temperature and RC combinations. Router DRC checks a subset of geometry rules, not foundry signoff.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 41
UART STUDENT LAB
Ignytion io
41/44
The routed GDS result
10_gds/uart_core.gds contains 1,284,780 bytes.
The decoder resolves 45 structures and compares 16,512 placed cell instances.
Coordinates, orientations and referenced cell identities agree with DEF.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
klayout-stream strm2gds combines routed DEF, technology/cell LEF and actual standard-cell GDS using the PDK layer map. The independent binary reader checks valid records, resolved references and exact standard-cell placement/orientation counts. Many instances are filler cells, so this number is not the synthesized logic-cell count. Raw hashes are run-specific because GDS contains timestamps.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 42
UART STUDENT LAB
Ignytion io
42/44
Evidence and signoff boundaries
Functional tests, mapped synthesis and routed export have evidence.
Foundry DRC, LVS, antenna and full-chip signoff have not run.
Jane Street still requires a programmable emulator on its CMOS5L template.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Distinguish the achieved student reference from a manufacturable submission. Structural GDS comparison is not electrical equivalence. Router-rule DRC is not a foundry deck. The current fixed-function SG13G2 blocks do not satisfy the competition’s reprogrammable general-purpose emulator requirement or process/template requirement. No tapeout-ready claim is justified.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 43
UART STUDENT LAB
Ignytion io
43/44
UART laboratory exercises
Decode a byte using the protocol rules covered in this lesson.
Change one expected result and observe a fatal test failure.
Compare functional cell count with physical filler/buffer counts.
Locate the worst setup and hold paths in both timing reports.
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Ask students to write a prediction before simulation. Keep changed expectations in a separate temporary exercise branch so the baseline remains reproducible. Have them explain why the negative control is evidence about the bench rather than a defect in the DUT. Then read exact startpoint, endpoint, clock path and data arrival time from the reports. Students should state the limitations of each artifact.
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.

## Slide 44
UART STUDENT LAB
Ignytion io
44/44
Review questions and reading
Which event establishes the first bit of a transfer?
Who owns the data wire at each stage?
What does the current regression leave untested?
Why does an exported GDS not prove signoff?
Notes: Ignytion IO - CRUCIBLE CORE
Copyright (c) 2026 Ignytion IO. Author: IGNYTION_TECH.
File: docs/student_decks/UART_Protocol_Students_Ignytion_VIDEO_v11.pptx
Created: 2026-10-03
Answers depend on the protocol: I2C uses START and addressed phases, SPI uses select plus the agreed clock edges, and UART uses START plus local baud timing. Revisit each byte-order rule. Reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Upstream: alexforencich/verilog-uart at 1b867e53af738e4a8bc7c839ca2f1c07f40382dc
Flow: OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Competition: Jane Street official requirements: https://blog.janestreet.com/protocol-emulator-asic-competition/
Protocol reading: Microchip USART asynchronous tutorial: https://ww1.microchip.com/downloads/en/DeviceDoc/usart.pdf
Implementation evidence: hw/protocols/uart/01_rtl, 02_sim, 04_synthesis, 08_sta and 10_gds in this repository.
OpenROAD documentation: https://openroad.readthedocs.io/en/latest/ ; local flow_config.tcl, run_flow.sh and numbered stage scripts.
Original upstream copyright and permission/disclaimer (retained for source excerpts):
# ===============================================================================
# Ignytion IO - CRUCIBLE CORE
# Copyright (c) 2026 Ignytion IO. All rights reserved.
# Author : IGNYTION_TECH
# File : hw/protocols/uart/01_rtl/LICENSE.forencich
# Created : 2026-10-03
# Description : Protocol reference integration and teaching build.
# Upstream copyright and licence notices below remain applicable.
# ===============================================================================
Copyright (c) 2014-2017 Alex Forencich
Permission is hereby granted, free of charge, to any person obtaining a copy
of this software and associated documentation files (the "Software"), to deal
in the Software without restriction, including without limitation the rights
to use, copy, modify, merge, publish, distribute, sublicense, and/or sell
copies of the Software, and to permit persons to whom the Software is
furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in
all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR
IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY
FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE
AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER
LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM,
OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN
THE SOFTWARE.